## Slide 1: HiP EDCA SP TBDs resolution
Date: 2025-15-01
Authors :

## Slide 2
Do you agree to define HIP EDCA in UHR where a STA with Low Latency traffic may be allowed, based on TBD conditions, to send a Defer Signal (it is TBD whether CTS frame or RTS is used) to start a protected short contention for pending LL data
  Conditions to be allowed to send a Defer Signal is TBD
  STA in HiP EDCA always use RTS/CTS as initial frame exchange and retry.
  Duration of protected short contention is TBD.
  Access parameters (AIFSN, CW and the expansion rules) used to transmit the Defer Signal are TBD.
  The retry count where the Defer Signal is allowed to be sent is TBD
  Contention parameters for the protected short contention are TBD. The STAs that transmitted a Defer Signal but did not win the protected short contention will initiate a new retry.
  Low Latency traffic is treated as AC_VO traffic. Other cases are TBD.
  The solution would provide control on the degree of collisions that may occur while using it and, allows for autonomous randomness or/and controlled by the AP
  No new mandatory synchronization requirement on STA side
  HIP EDCA is used by the STAs in a BSS only when this feature is enabled by the AP

## Slide 3: Send a Defer Signal (e.g. CTS frame or RTS) to start protected short contention
The HiP EDCA proposal use CTS frame to start protected contention
  “To start protected contention” – a STA with LL traffic use protected contention to obtain the medium, the period starts at the end of DS frame
CTS frame can be defined as common frame with duration and/or address field set to a predefined value
  Unlike RTS that has to carry unique info
CTS frame is compliant with ETSI regulations which allow SCS transmission w/o performing medium check, i.e. not following regular channel access procedure (backoff)
  RTS on the other hand shall follow ETSI and baseline IEEE spec as in case of successful transmission originator will continue the sequence with DATA transmission (i.e. obtain TXOP). For that to happen a STA shall use defined channel access procedure described both in ETSI and IEEE
We suggest to use CTS as a short control frame to announce HiP EDCA period
Notes: Further thinking/steps:
Define format for CTS – “common” or “unique” – special values for duration (i.e. duration of protected contention is fixed) and for Address (special value OR BSSID value)

## Slide 4: Enablement
The condition(s) “to be allowed to send Defer Signal” require discussion:
  It should include traffic based (STA side) condition as well as enablement-based conditions (AP side)
  Examples of traffic-based conditions may include:
    Retransmission counter
    Channel access time
    Traffic bounded delay/queueing delay
  Examples of enablement-based conditions
    AP enable/disable HIP EDCA
    Number of DS transmissions per time interval (as in ETSI – max 50 TXes per 50ms but no more that 2.5ms in total)
    Frequency of transmission
    Negotiation/request to use or notification of use initiated from a STA side

## Slide 5: Enablement
Multiple individuals expressed concerns about scope of use for HiP EDCA - whether HiP EDCA enabled by default for any environments or controlled by a central entity
  Default mode 1 : Define conservative “default” HiP EDCA Parameters.
    UHR STA capable of HiP EDCA may use it in any environment for the traffic buffered into AC_VO
  Controlled mode 2: In a presence of UHR AP a HiP EDCA capable STA will use parameters provided by UHR AP
    HIP EDCA enabled by default with conservative parameters
      AP may advertise different parameters, including disable HIP EDCA functionality
    When enabled, all STAs can use HIP EDCA for the traffic in AC_VO
  Controlled mode 3: In a presence of UHR AP a non-AP STA shall negotiate the use of HIP EDCA
    STA request with modified SCS for the streams that are mapped into AC_VO
      If AP reject SCS request , STA can use HIP EDCA
      If AP accepts, STA is triggered and do not use HIP EDCA
        STA may use HIP EDCA if triggering is not sufficient
  Controlled mode 4 (or 2.5): In a presence of UHR AP a non-AP STA notify AP before the use of HIP EDCA
    HIP EDCA enabled by default with default parameters
      STA notify AP about the use of HIP EDCA via modified SCS for the streams that are mapped into VO
      AP track incoming requests and may advertise other than default parameters for HIP EDCA of may disable it
Notes: Overall preference is around 2/3
Other modes in mind?

## Slide 6: Duration of protected short contention is TBD
Contributions 11-23/2126r0, 11-23/1065r0, 11-24/0467r1, 11-24/0840r0 and 11-24/0864r1 use EIFS as a _reference_ to determine duration for protected short contention
  EIFS, depending on parameters have a range of values (Table 10-8):
    EIFS = aSIFSTime + AcktTxTime + DIFS = 16 + (28-68)+34 =78-118us
  We propose to fix duration in the protected short contention to the value 97us which is close to EIFS = 16+44+34=94us where:
    44us is AckTxTime @ non-HT BPSK rate
    97us is time equal to short contention of AIFSN2 + 7 SLOTs
  This will be applied when short control frame is sent to establish protection for the short contention

## Slide 7: Contention parameters are TBD The retry count where the Defer Signal is allowed to be sent is TBD
The protected short contention starts after the end of Defer Signal transmission
  The short contention follow existing rules as described in 10.23.3 HCF contention, channel access (EDCA)
  Only EDCAF[VO] and TBD EDCAF (if agreed) are allowed for the contention during short contention period
  Assuming duration of protected short contention of 97us and contention overhead of SIFS + AIFSN2 = 34us
    It is reasonable to define range for BK selection as min(0..7)..
Three possible outcomes of short protected contention:
  STA may win TXOP and successfully TX data. In such a case the condition to use HiP EDCA is no longer valid, and STA return to legacy operations. Best possible outcome
  STA may lose the contention to some other STA. In such a case STA may be able to announce HiP EDCA again subject to number of possible attempts defined in a spec, for example – no more that 1 or 2.
  STA may win contention, but new collision happen (e.g. STA send RTS but did not get response CTS). In such a case a STA may again announce HiP EDCA subject to number of possible attempts defined in a spec, for example – 2.

## Slide 8: SPs
SP1: Do you support to define CTS as Defer Signal to start protected short contention for the pending LL data?
Notes: Instead LL data use AC_VO data?

## Slide 9: SPs
SP2 Do you support that STA may use HIP EDCA
  If HIP EDCA option is enabled by the AP to which that STA is associated to
    Enablement procedure TBD
  May transmit up to TBD but no more than 50 transmissions of DS and up to 2.5 ms of total transmission time to start HIP EDCA contention over 50ms interval
    Note: ETSI regulation of Short Control Signaling transmission
  Shall not initiate more than TBD number of transmissions of DS to start HIP EDCA consecutively.
    Note: consecutive DS transmission are multiple attempts to perform HIP EDCA contention w/o falling back to regular EDCA operation

## Slide 10: SPs
SP3: Do you support to define the default value equal to 97us for the Protected Duration of the protected short contention
  The value of 97us allow for AIFSN[2] + 7 slot contention
  The Defer Signal frame carry that Protected Duration in the Duration field
  UHR AP may advertise values other than default
Notes: prefer not to tie contention with EIFS, like AIFSN + contention window…

## Slide 11: SPs
SP4: Do you support to define default parameters for HIP EDCA for AC_VO to be used during protected short contention period as follows:
  HiP EDCA CWMin=7, HiP EDCA CwMAX=7
  HiP EDCA AIFSN=2
  An UHR AP may advertise values other than default

## Slide 12: Questions?