## Slide 1: Follow Up on Power Budget Negotiation
Date: 2024-11-12
Authors:

## Slide 2: Abstract
Proposal to add power requirement and feedback information in the WPT protocol.
Follow up on 11-24-1561-02-00bp limiting the number of bits required for negotiation and feedback reporting.

## Slide 3: Background
For the AMP technology to be reliable, a WPT protocol is likely needed. [1]
[2] proposes STAs inform the AP about its power status
[3] proposes different modes of WPT protocols
[4] we proposed to exchange power related capabilities and feedback
Concerns expressed on:
  Power consumption needed for WPT negotiation.
  Number of bits required to exchange WPT capabilities and feedback
  WPT negotiation not useful in all use cases

## Slide 4: Motivation
WPT protocol should allow:
  Scheduling charging frames based on AMP STAs needs
  Optimizing duration of charging frames
WPT protocol should minimize AMP STA power consumption for negotiation
Notes: Optimizing duration of charging frame: send as often and long frames as needed in the given environment within the duty cycle constraints.

## Slide 5: Assumptions
An AMP STA has different operating modes
  Each mode with different power requirements
The AMP STA can evaluate:
  its power needs (in the different modes)
  the energy it has harvested from one or more energizing frames (or over a period of time)
An AMP AP or reader needs to provide power to multiple AMP STAs
Notes: Example: AMP STA is a temperature sensor IoT:
Power Mode 1: sensor activity only (need power to power up sensor, read temperature and store it into memory) – amount needed once every one hour.
Power Mode 2: maintain memory alive (need power not to lose stored measurement) – amount needed every second
Power Mode 3: answer poll from AP (need power to receive polling request, format and send response) – amount needed every 12 hours.

## Slide 6
Operating Modes
Different devices can have different operating modes based on their purposes and capability.
An AMP STA switches between operating modes during its operations following its own schedule.
All AMP STA share an operating mode that is “idle” mode: AMP STA has enough energy to maintain its stateful without performing any other activity.
Other examples of operating mode could be:
  Reading a sensor and storing the result
  Performing an RF transaction
  Etc...

## Slide 7
Operating Mode Definition
We propose to define an Operating Mode as follows:
  ID [0-7]
  Name
  Description
  Required Energy Amount
  Default Scheduled Frequency
Notes: For the “idle” mode, the required energy amount would be intended as the energy required not to reset/power off in the default scheduled frequency.
For other manufacturer defined operating modes, the required energy amount is the amount of energy required to perform the full operation and the default scheduled frequency is how often such operation is performed.
Ex. ID 1
Name: read temperature
Description: read ambient temperature and store it in memory
Required Energy Amount: x J
Default Scheduled Frequency: 1 hour
ID 2
Name: RF transaction
Description: send stored temperature measurements since last transaction
Required Energy Amount: x J
Default Scheduled Frequency: 12 hour

## Slide 8
Device Type Profile
Made available OOB (AP accesses it on the internet)
Identified by an ID shared by the AMP STA
Contains:
  Manufacturer Name
  Device Description
  Operating Modes
  Energy Capacity
  Feedback Base Value
    Feedback is expressed as a percentage of this value

## Slide 9
Device Type Profile ID
Proposal A: value is assigned by external organization (IANA, Wi-Fi Alliance, other) – could be for example 32-bit unique identifier
Proposal B: Device Type Profile is a compressed URL where the AP can retrieve the profile (inspired by MUD RFC8520)

## Slide 10
WPT Budget and Feedback Reporting
WPT initial negotiation can happen during discovery
  The AMP device only gives the Device Type Profile ID (32 bits)
WPT feedback:
  Harvested energy (7 bits)
  Current Battery Level (7 bits)
  Possible Scheduled Frequency Change (17 bits)
AP uses this information:
  to calculate the charging frame duration
  to schedule charging of several AMP STAs
Notes: Change can come from AMP STA moving or from environmental changes.
Changes can come also from application (example, requiring measure every 30 minutes instead of 60)

## Slide 11
WPT Budget Reporting Example
Charging frame – AP transmit at x dBm for y μs
Poll for new AMP STAs
AP
AMP STA 1
AMP STA 2
Poll response from AMP STA1:
Energy harvested from charging frame (%)
Battery level (%)
AMP Device Profile ID
Poll response from AMP STA2:
Energy harvested from charging frame (%)
Battery level (%)
AMP Device Profile ID
Notes: This can apply to both active and passive AMP STA: for active STA the charging frames can occur.
Charging frame can happen on a different band from where the communication takes place.
Charging frame can be preamble to the poll for backscattering devices.

## Slide 12
WPT Feedback Reporting Example
Charging frame – AP transmit at x dBm for y μs
Poll for AMP STAs data from AMP STA1 and AMP STA2
AP
AMP STA 1
AMP STA 2
Poll response from AMP1 STA:
Energy harvested from charging frame (optional)
Battery level (optional)
- Operating Mode Frequency Change (optional)
- Data
Poll response from AMP STA2:
Energy harvested from charging frame (optional)
Battery level (optional)
Operating Mode Frequency Change (optional)
Data
Notes: Environmental conditions can change -> AMP STA can report energy harvested feedback during data communication

## Slide 13
Operational Mode Frequency Change
The known device needs to exchange:
  Operational mode ID: 8 bits
  New Frequency: 17 bits [hours (5 bits), minutes (6 bits), seconds (6 bits)]

## Slide 14: Summary
We suggest creating a WPT negotiation protocol for the AMP STA to share its power needs (amount and frequency) and the currently harvested energy with the AP.
AP can avoid sending too long charging frame if no need (except for discovery).
AP can schedule charging frames dynamically.
Example of such WPT protocol (to be discussed) with minimal number of bits used.

## Slide 15: Discussion and Feedback

## Slide 16: Straw Poll 1
Do you agree to include in the WPT protocol an optional mechanism for the AMP STA to inform the AP about its power requirements ?
  Yes
  No
  Abstain

## Slide 17: Straw Poll 2
Do you agree to include in the WPT protocol an optional mechanism for the AMP STA to give feedback on harvested energy, for example, from a charging frame or over a period of time?
  Yes
  No
  Abstain

## Slide 18: References
[1] 11-24-0575-01-0amp-p802-11bp-par.pdf
[2] 11-24-1381-00-00bp-amp-device-power-status
[3] 11-24-1208-00-00bp-thoughts-on-the-amp-wpt-protocol
[4] 11-24-1561-02-00amp-power-budget-negotiation.ppt