## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: Thoughts for Consideration in the Joint 802.11/802.15 Coex Forum
Submitted: 12 November 2024
Source: Benjamin A. Rolfe (Blind Creek Associates)
Contact:
Voice: [deprecated],
E-Mail: ben.rolfe @ ieee.org
Re: Coexistence of 802.11 and 802.15
Abstract: Contribution providing thoughts for consideration in moving forward in promoting positive coexistence outcomes
Purpose: Contribute to peach and harmony within 802, effective spectrum utilization, and world peace
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Thoughts for Consideration in the Joint 802.11/802.15 Coex Forum
Author:
Name | Affiliation | Address | Email
Benjamin Rolfe | Blind Creek Associates | Los Gatos, CA | ben.rolfe @ ieee.org

## Slide 3: FCC Subpart E Interesting facts
(not the entire world, but not insignificant)

## Slide 4: 5.925-7.125 GHz, 5.15-5.35 GHz, and 5.47-5.895 GHz in the US
FCC Part 15 Subpart C (wideband devices)
FCC Part 15 Subpart E (U-NII)
FCC Part 15 Subpart F (UWB)
10.6
UWB Subpart F
10.6
3.1
GHz
7.250
7.125
U-NII
WIdeband
5.15
5.925

## Slide 5: US Title 47, Chapter 1, Subchapter A, Part 15, Subpart E—Unlicensed National Information Infrastructure Devices Contention based protocol

## Slide 6: US Title 47, Chapter 1, Subchapter A, Part 15, Subpart E—Unlicensed National Information Infrastructure Devices
Contention Based Protocol: A protocol that allows multiple users to share the same spectrum by defining the events that must occur when two or more transmitters attempt to simultaneously access the same channel and establishing rules by which a transmitter provides reasonable opportunities for other transmitters to operate. Such a protocol may consist of procedures for initiating new transmissions, procedures for determining the state of the channel (available or unavailable), and procedures for managing retransmissions in the event of a busy channel.
§ 15.407 General technical requirements.
(d) Operational restrictions for 6 GHz U-NII devices.
  6) All U-NII transmitters, except for standard power access points and fixed client devices, operating in the 5.925-7.125 GHz band must employ a contention-based protocol.

## Slide 7: US Title 47, Chapter 1, Subchapter A, Part 15, Subpart E—Unlicensed National Information Infrastructure Devices
That’s it, that’s all the FCC rules say about “Contention Based Protocols”.
  What are the technical requirements?
  Did you find “listen before talk” in there?
  may consist of procedures for … determining the state of the channel
FCC has documented a method that will be acceptable for demonstrating compliance with § 15.407 (d)(6) in KDB 987594 D02 U-NII 6 GHz EMC Measurement v03, GUIDELINES FOR COMPLIANCE TESTING OF UNLICENSED NATIONAL INFORMATION INFRASTRUCTURE 6 GHz (U-NII) DEVICES PART 15, SUBPART E

## Slide 8: KDB 987594 D02 U-NII 6 GHz EMC Measurement v03
Covers indoor access points, subordinate devices, all client devices (except for Fixed clients), and VLP devices operating in the 5.925-7.125 GHz band
Stated purpose is to avoid co-channel interference with incumbent devices sharing the band. “incumbent” in FCC land means licensed (priority) users of the band.
From the KDB: “Unlicensed devices must detect co-channel radio frequency power that is at least -62 dBm or lower.”
  See the next slide summarizing the test procedure for clarification.
Must detect RF energy throughout their intended operating channel
90% or greater certainty (9 out of 10 tries)

## Slide 9: KDB 987594 D02 U-NII 6 GHz EMC Measurement v03
40 MHz
RX BW
10 MHZ
-62 dBm
AWGN
2 MHz RX BW

## Slide 10: KDB 987594: Contention based protocol
KDB 987594 D02 U-NII 6 GHz EMC Measurement v03 section I, contention based protocol
Test method in a nutshell:
  A 10 MHz-wide additive white Gaussian noise (AWGN) signal is selected to simulate and represent incumbent transmission
  Where DUT signal is wider than 10 MHz, test may be repeated with AWGN signal at different center frequencies within the DUT channel (up to 3)
  If DUT signal is less than 10 MHz, test only at one frequency is required
  Run DUT at a constant duty cycle
  Ramp up AWGN signal until DUT ceases transmission: If it stops at or before the 10 MHz-wide AWGN signal is at -62 dBm, pass

## Slide 11: KDB 987594: Contention based protocol
This is one way to demonstrate implementation of a contention based protocol, not the only way
Aligns with an industry alliance conformance test procedure
Has been referenced in approvals of non-802.11 based systems

## Slide 12: Quick look: VLP Approvals (11-Nov-2024) Jan 1 to November 11, 2024
Search on “6VL” type, Part 15E, 6 GHz band
  This will include anything that includes VLP
117 devices approved
The first dozen or so to show up (public) were not 802.11ax
  Determined by examining test report
Of current search spot checked about half
  Most include 802.11ax
  All but 2 include NB U-NII
Caveats:
  If requested, FCC will not make approval public for 6 months
  Many of the search results look like variations of the same or similar (multo-radio) products
Search on “6VL” without Part 15E
  This includes applications for VLP only
  10 results, all NB UNII
  Not a surprise – any 802.11ax w/VLP will also have LPI

## Slide 13: Quick look: VLP Approvals Statement of the obvious
Unlikely an of these devices comply with “mandates” in our standards that are yet to be written
Unlikely these devices are going away
  All look to be commodity consumer devices
Possible that *some* of these devices can accommodate *some) updates via firmware/software
  The higher in the protocol stack the more likely it’s not cast in sand
Very likely that there are variations of these products approved or in process for other markets outside North America
The U-NII 5 + 7 VLP Narrow Band train has left the station!

## Slide 14: Scope of effect: what can we do in 802?
First principles:
  IEEE 802 is not a regulatory body
  Ultimately our standards are recommendations that can be used or ignored
802 standards are adopted when they are useful, make sense, and can be implemented
  Real world: if something in our standard doesn’t work for a purpose, something else is used (parts of our standard are ignored or used with changes)
  Sometimes the “workaround” comes back into 802 to update our standards
The best thing we can do is make good technical sense

## Slide 15: Scope of effect: what can we do in 802?
What we can do in 802
Understand the technology
Realistically evaluate the risks and potential mitigations
  There are multiple mitigations possible
  No single mitigation always works
  Single dimension thinking leads to unsustainable approaches
Develop useful coexistence strategies that are beneficial for all
  Re-review the mechanisms already present in our standards
  Understanding of practical mitigations is a likely outcome
Direct engagement between .11 and .15 can be beneficial
  Need an “all inclusive” approach (the problem is larger than either WG)

## Slide 16: What we can, but should not, do
Spin our wheels blaming "the other working group", "proving" that our favorite technology is intolerant and vulnerable
  Likely outcomes include anxiety, bad PR for 802, with a side effect of loss of credibility and influence outside of 802
  Actual coexistence improvements won't happen
Fixate on only one possible solution
  Effective coexistence requires a depth of “tool kit” capabilities
  RF environments, application needs, and spectrum regulations vary greatly
Impede the progress of any 802 project
  To be effective we must be positive and inclusive
Always do what we’ve always done expecting a different outcome

## Slide 17: A better approach…
Joint efforts with sessions with objective technical discussions
Engage in mutual discussions in joint sessions
  Participation from both 802.11 and 802.15 working groups
  Need the difference perspectives (need input)
Spread the word (more input == better outcomes)
Make joint recommendations that have benefit both ways
Understand the widely varying environments, regulatory requirements, application needs, and other differences that make different standards different and relevant (and equal in importance)

## Slide 18: What we can’t do in 802
Make regulations
Force anyone to use what we put in our standards
Band together within a working group to block progress of a project in another working group project (IEEE SA rules)
Affect the behavior of anyone for whom or “mandates” make no sense for their needs
  Ultimately products are bound by regulatory agency rules, not our standards
  Stuff that doesn't work for their application will be ignored
Change gravity, the rate of decay of the earth's orbit around the sun, or the fundamental reality of the above points (sorry Marc ;-)
  That doesn’t mean we can not have a positive impact and positive outcomes!

## Slide 19: Reaching for positive outcomes
Education is good: help each other learn: can and should be part of the joint sessions.
It’s a learning process!