## Slide 1
Examples of transactions that may cross epoch boundaries
Date: 2024-12-17
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1-404-229-1672 | carol@ansley.com

## Slide 2
Abstract
This submission includes examples of potential problems scenarios to improve EDP operation during the transition period between epochs.

## Slide 3: Summary
During a transition period, an ongoing transaction may spread across an epoch boundary.
The transaction may involve buffered data, a request/response transaction such as a channel sounding request, or a transaction with a trigger frame.
During earlier discussions, we tentatively agreed on some principles:
A transaction within a single TXOP should use the same parameters until it completes.
If a transaction starts with one set of parameters, it probably should complete with the same parameters, if possible.
Still to be determined, how do we build these policies into the text?
Make minimal changes to baseline where appropriate, pointing back to EDP sections as needed for full details.
No changes to baseline, only remarks in EDP sections

## Slide 4: Summary of Transition Period assumptions
The transition period happens when a new EDP epoch begins.
An MLD is expected to be able to receive and correctly act upon frames with its new AID once the transition period has begun.
The purpose of the transition period is to allow stored/buffered frames or frames subject to retransmission an opportunity to be transmitted versus just being deleted to clear the buffers.

## Slide 5: Example Interaction with AID tie-ins (1)
Multi-Link Traffic Indication element in Beacon frame includes Per-Link Traffic Indication Bitmap with bit corresponding to AID of non-AP MLD = 1
PS-Poll frame sent by a STA affiliated with the non-AP MLD to retrieve buffered traffic
AP MLD sends the buffered traffic to the non-AP MLD over an appropriate link
AP MLD receives traffic for non-AP MLD currently in PS and stores it in a buffer
AP MLD
Non-AP MLD

## Slide 6: Details – PS-Poll frame
A PS-Poll frame is generated by a STA, which can be an affiliated STA that is part of a non-AP MLD.
The PS-Poll frame indicates that the transmitting STA has left PS mode and generally wants to retrieve any buffered traffic.
Since the PS-Poll frame is generated by the non-AP MLD’s affiliated STA, the STA can choose to which AID to use (and other FA parameters).

## Slide 7: Example Interaction with AID tie-ins (2)
Multi-Link Traffic Indication element in Beacon frame includes Per-Link traffic Indication Bitmap with bit corresponding to AID of non-AP MLD = 1
PS-Poll frame sent by a STA affiliated with the non-AP MLD to retrieve buffered traffic
AP MLD receives traffic for non-AP MLD currently in PS and stores it in a buffer
AP MLD
Non-AP MLD
Transition start
OLD AID
NEW parameters
AP MLD sends the buffered traffic to the non-AP MLD over an appropriate link
NEW parameters
Transition end

## Slide 8: Details – PS-Poll frame – case 2
In case 2, the use of a new AID in the PS-Poll frame could allow an observer to link the old AID and the new AID.
If the non-AP STA affiliated with a non-AP MLD sends the PS-poll with an old AID, then the AP MLD needs to respond using the previous set of FA parameters (PN/SN, MAC address, etc.)
If the non-AP STA affiliated with a non-AP MLD sends the PS-poll with a new AID, then the AP MLD needs to respond using the new set of FA parameters (PN/SN, MAC address, etc.)

## Slide 9: Details – PS-Poll frame
Proposed text:
9.3.1.5 PS-Poll frame format
9.3.1.5.2 Non-BDT variant of the PS-Poll frame format
TIf the STA is not an EDP non-AP MLD affiliated STA, the Duration/ID field contains the AID value assigned to the STA transmitting the frame by the AP in the (Re)Association Response frame that established that STA’s current association, with the two MSBs set to 1.
If the STA is an EDP non-AP MLD affiliated STA, the STA shall use the AID value assigned to it in the current FA parameter set.

## Slide 10: Example Interaction with AID tie-ins (3)
Multi-Link Traffic Indication element in Beacon frame includes Per-Link traffic Indication Bitmap with bit corresponding to AID of non-AP MLD = 1
PS-Poll frame sent by a STA affiliated with the non-AP MLD to retrieve buffered traffic
AP MLD sends the buffered traffic to the non-AP MLD over an appropriate link
AP MLD receives traffic for non-AP MLD currently in PS and stores it in a buffer
AP MLD
Non-AP MLD
Transition start
OLD AID
OLD parameters
OLD parameters or NEW parameters

## Slide 11: Details – PS-Poll frame – case 3
In case 3, the use of parameters from the new FA parameter set could allow an observer to correlate the old AID/MAC with the new AID MAC for that STA.
The AP MLD should respond with frames using the previous FA parameter set.

## Slide 12: Details – PS-Poll frame – case 3
Proposed text:
35.3.12.4 Traffic indication (modify paragraph 17 and add new 18th paragraph)
When an AP affiliated with an AP MLD receives a PS-Poll frame or a U-APSD trigger frame from a non-AP STA affiliated with an associated non-AP MLD that is in power save mode, it shall transmit buffered BU(s) to the STA, if the buffered BU(s) are available and not discarded for implementation dependent reasons, otherwise, it may transmit a QoS Null frame.
When an AP affiliated with an EDP AP MLD receives a PS-Poll frame or a U-APSD trigger frame from a non-AP STA affiliated with an associated EDP non-AP MLD that is in power save mode, the AP shall follow the addressing guidelines in section 10.71.5.4.
it shall will transmit buffered BU(s) to the STA using FA parameters from the current epoch, if the buffered BU(s) are available and not discarded for implementation dependent reasons, otherwise, it maycan transmit a QoS Null frame.

## Slide 13: Example Interaction with AID tie-ins (4)
Multi-Link Traffic Indication element in Beacon frame includes Per-Link traffic Indication Bitmap with bit corresponding to AID of non-AP MLD = 1
PS-Poll frame sent by a STA affiliated with the non-AP MLD to retrieve buffered traffic
AP MLD sends the buffered traffic to the non-AP MLD over an appropriate link
AP MLD receives traffic for non-AP MLD currently in PS and stores it in a buffer
AP MLD
Non-AP MLD
Transition start
NEW AID
NEW AID
NEW parameters
Based on MLO model, this should be fine, but leakage could happen if there was a previous beacon with the old AIDs.
Multi-Link Traffic Indication element in Beacon frame includes Per-Link traffic Indication Bitmap with bit corresponding to AID of non-AP MLD = 1
OLD AID

## Slide 14: Details – PS-Poll frame – case 4
Case 4 should be covered by the texts already proposed.

## Slide 15: Multi-STA BlockAck Details
The BA Control field is defined in Figure 9-53 (BA Control field format):
Multi-STA BlockAck variant (9.3.1.8.6) –
  This variant is the only BlockAck frame making use of AID11. But for this frame type, the TID_INFO subfield in the BA Control field is reserved. A bit from that field can be used to indicate which epoch the AID values are from.
  If the AP MLD does mark a multi-STA BlockAck as containing AIDs from the previous epoch, it should only contain AIDs from the previous epoch and AIDs of legacy STAs.
See also 26.4.2 Acknowledgement context in a Multi-STA BlockAck frame
B0 | B1 B4 | B5 B8 | B9 | B10 | B11 | B12 B15
Reserved | BA Type | Reserved | No Memory Kept | Memory Configuration Tag | Management Ack | TID_INFO

## Slide 16: Example BlockAck interactions (1)
Multi-Link BlockAck sent in response to receipt of above
HE TB PPDU or multi-STA Multi-TID, Multi-STA single-TID, or single-STA multi-TID A-MPDUs.
AP MLD supports Multi-Link BlockAck if either UL MU or multi-TID A-MPDU operation is supported.
AP MLD
Non-AP MLD

## Slide 17: Discussion – Multi-STA BlockAck
Proposed text:
9.3.1.8.6 Multi-STA BlockAck variant (inserting new paragraphs as shown and modifying previous 5th paragraph)
During an EDP transition period, the most significant bit of the TID_INFO subfield of the BA Control field is set to 1 if the AIDs in the AID TID Info subfield are from the previous EDP epoch. The MSB is set to 0 if the AIDs in the AID TID Info subfield are from the current EDP epoch.
Otherwise, the The TID_INFO subfield of the BA Control field of the Multi-STA BlockAck frame is reserved.
NOTE—A Multi-STA BlockAck frame can only contain AIDs for EDP non-AP MLDs from a single set of FA parameters.

## Slide 18: Example BlockAck interactions (2)
Multi-Link BlockAck sent in response to receipt of above
HE TB PPDU or multi-STA Multi-TID, Multi-STA single-TID, or single-STA multi-TID A-MPDUs.
AP MLD supports Multi-Link BlockAck if either UL MU or multi-TID A-MPDU operation is supported.
AP MLD
Non-AP MLD
Transition start
OLD parameter set
OLD AID(s)
Old AIDs
AID marker in frame

## Slide 19: Example BlockAck interactions (3)
Multi-Link BlockAck sent in response to receipt of above
HE TB PPDU or multi-STA Multi-TID, Multi-STA single-TID, or single-STA multi-TID A-MPDUs.
AP MLD supports Multi-Link BlockAck if either UL MU or multi-TID A-MPDU operation is supported.
AP MLD
Non-AP MLD
Transition start
OLD AID(s)
NEW AID(s)
New AIDs
AID marker in frame
Not desirable because an observer could correlate the OLD FA parameter set to the new AID(s).

## Slide 20: Example Sounding interactions (1)
EHT NDP Announcement
EHT Compressed Beamforming/CQI
AP MLD
Non-AP MLD
EHT sounding NDP

## Slide 21: Example Sounding interactions (2)
EHT NDP Announcement
EHT Compressed Beamforming/CQI
AP MLD
Non-AP MLD
EHT sounding NDP
OLD AID
OLD MAC
Transition start
Notes: Note that this scenario allows an observer to correlate the previous AID/MAC to the new MAC

## Slide 22: Example Sounding interactions (3)
EHT NDP Announcement
EHT Compressed Beamforming/CQI
AP MLD
Non-AP MLD
EHT sounding NDP
Transition start
OLD AID
OLD MAC
Notes: Note that this scenario allows an observer to correlate the previous AID/MAC to the new MAC

## Slide 23: Example Sounding interactions (4)
EHT NDP Announcement
EHT Compressed Beamforming/CQI
AP MLD
Non-AP MLD
EHT sounding NDP
Transition start
OLD AID
NEW MAC
Notes: Note that this scenario allows an observer to correlate the previous AID/MAC to the new MAC

## Slide 24: Discussion – NDP Announcement frame
Proposed text:
35.7.3 (TGbeD7.0)
When an EHT beamformer is an AP and EHT beamformees are non-AP STAs, the EHT beamformer that transmits an EHT NDP Announcement frame to one or more EHT beamformees shall set the AID11 subfield to the 11 LSBs of the AID of each EHT beamformee.
An EHT beamformer that is an EDP AP MLD shall not initiate a new EHT sounding sequence that may continue into an EDP epoch transition period.
An EHT NDP Announcement frame shall not include multiple STA Info fields that have the same value in the AID11 subfield.

## Slide 25: Discussion – Trigger frame
9.3.1.22 Trigger frame format
Based on the changes in TGbeD7.0, a Special User Info field is always present when an EHT User Info field is used. One of the reserved bits in that field can be used by the AP to indicate if the EHT AIDs of EDP non-AP STAs are from the current FA parameter set or from the previous set.

## Slide 26: Discussion – Trigger frame
Proposed text defines a currently reserved bit for use to indicate the presence of AIDs from the previous FA parameter set.
Because of the variety of Trigger frames and Trigger frame uses, this change would contain the needed text alterations to a single section versus trying to note the change in all of the different uses.
Alternatively, the AP could be instructed to only use AIDs from the current FA parameter set. This approach would use text similar to the NDP Announcement frame text added to 35.2.1.2.1, 35.2.2.1, and maybe other sections as appropriate.

## Slide 27: Discussion – Trigger Frame
Proposed text: (section 9.3.1.22.3 - change to table 9-90d and new text)
The format of the Special User Info field is defined in Figure 9-90d (Special User Info field format).
During an EDP transition period, the Transition Active subfield of the BA Control field is set to 1 if the AIDs in the AID TID Info subfield are from the FA parameters of the previous EDP epoch. The Transition Active subfield is set to 0 if the AIDs in the AID TID Info subfield are from the current EDP epoch.
NOTE—A Trigger frame can only contain AIDs for EDP non-AP MLDs from a single set of FA parameters.
Transition Active
Reserved
Trigger Dependent User Info
1 2 variable
B37 B38