## Slide 1
December 2024
Usage of NPCA in M-AP coordination
Date: 2024-12-xx
Authors:
Name | Affiliations | Address | Phone | email
Si-Chan Noh | Newracom |  |  | sc.noh@newracom.com
Joonsoo Lee |  |  |  | js.lee@newracom.com

## Slide 2: Introduction
According to the current SFD [1],
  The event that triggers switching to the NPCA primary channel shall be
    OBSS control frame exchange (e.g., (MU-)RTS/CTS) or HE/EHT/UHR PPDU
    Note : Other conditions TBD
The above conditions that may trigger NPCA operations in the C-TDMA scenario, which is one of the Multi-AP coordination scheme(s), have not yet been discussed and defined
  For example, OBSS control frame exchange is occurred after TXOP allocation phase
We need further discussions on considering the potential interference when performing NPCA operations in the C-TDMA scenario
In this contribution, we define interoperating issues and discuss some approaches whether or not to perform NPCA during C-TDMA

## Slide 3: Interoperating scenario – Ⅰ
C-TDMA operation
  TXOP allocation phase :
    The sharing AP may allocate a time portion within the obtained TXOP to the shared AP
      MU-RTS TXS + CTS
  Frame exchange(s) of shared AP’s BSS after TXOP allocation phase :
    The shared AP can start control frame exchanges with in-BSS devices
      (MU-)RTS + CTS
    Or; it can exchange data PPDU/ACK during allocation duration
NPCA operation
  The sharing AP and STA1-2 may overhear control frame exchanges of shared AP’s BSS after the TXOP allocation phase
  If the sharing AP and STA1-2 have NPCA operation capability, and the control frame exchange satisfies conditions that may trigger NPCA, they can perform channel switching
C-TDMA with NPCA operation
  Shared AP’s BSS
    The shared AP can use allocated TXOP as indicated in allocation duration field in MU-RTS TXS
  NPCA STAs(e.g., sharing AP/STA1-2)
    NPCA can be performed during the TXOP duration determined by shared AP's control frame exchange (i.e., if it is larger than the NPCA minimum duration threshold)
Shared AP
(BSS 2)
Sharing AP
(BSS 1)
STA 2
(BSS 2)
MU-RTS TXS
CTS
Frame exchange(s) within shared AP’s BSS
TXOP allocation phase
Coverage of sharing AP
Coverage of shared AP
CTS
(MU-)RTS
STA 1-2
(BSS 1)
CTS
CTS
* Assumption : The (MU-RTS TXS/CTS) exchange between the sharing AP and shared AP did not overlap with the NPCA primary channel of the sharing AP’s BSS

## Slide 4
C-TDMA operation
  TXOP allocation phase :
    The sharing and shared AP exchange MU-RTS TXS/CTS for C-TDMA
NPCA operation
  After the TXOP allocation phase, OBSS STAs exchange control frame (e.g., (MU-)RTS/CTS)
    The sharing AP and STA1-2 can overhear these exchanges
  If the sharing AP and STA1-2 have NPCA operation capability, and the control frame exchange satisfies the conditions that may trigger NPCA, they can perform channel switching
C-TDMA with NPCA operation
  Shared AP’s BSS
    The shared AP can use allocated TXOP as indicated in allocation duration field in MU-RTS TXS
  NPCA STAs(e.g., sharing AP/STA1-2)
    NPCA can be performed during the TXOP duration determined by OBSS control frame exchange (i.e., if it is larger than the NPCA minimum duration threshold)
Shared AP
(BSS 2)
Sharing AP
(BSS 1)
MU-RTS TXS
CTS
TXOP allocation phase
Coverage of sharing AP
Coverage of shared AP
CTS
(MU-)RTS
STA 1-2
(BSS 1)
OBSS AP
OBSS STA
Frame exchange(s) of OBSS
* Assumption : The (MU-)RTS/CTS) exchange of the OBSS did not overlap with the NPCA primary channel of the sharing AP’s BSS
Interoperating scenario – Ⅱ

## Slide 5: Problem definition
In the previous slides, we defined the interoperating scenarios for C-TDMA with NPCA
These interoperating scenarios can occur when a shared AP attempts to return the remainder of the shared TXOP time to the sharing AP
  While the shared AP is transmitting TXOP return frame to the sharing AP, the sharing AP can operate on the NPCA Primary channel
    In this case, it may not identify TXOP return frame
  Moreover, if the sharing AP intends to share its TXOP with multiple shared AP(s), it is unable to do
Therefore, we need a rule to allow/prevent the interoperability between C-TDMA and NPCA
Sharing AP
Shared AP
CTS
Allocated time
OBSS TXOP (e.g., shared AP)
Shared AP’s BSS frame exchanges
TXOP
return
MU RTS TXS
NPCA operation during OBSS TXOP
Channel
Switching
to NPCA primary channel
Switching back
to BSS primary channel
CTS
(MU-) RTS
(DATA + ACK) / (TF + DATA +ACK)/..,/
Sharing AP
Shared AP
CTS
OBSS TXOP (i.e., not a shared AP)
Shared AP’s BSS frame exchanges
TXOP
return
MU RTS TXS
NPCA operation during OBSS TXOP
Channel
Switching
to NPCA primary channel
Switching back
to BSS primary channel
Interoperating scenario – Ⅰ
(NPCA triggered by shared AP BSS)
Allocated time
Interoperating scenario – Ⅱ
(NPCA triggered by OBSS)

## Slide 6: Allowing interoperation between C-TDMA and NPCA
To enable the interoperation of C-TDMA and NPCA, we can a consider conditional approach
Proposal 1 : If the sharing AP requests TXOP return from the shared AP, NPCA operation may not be performed; If not, NPCA can be carried out
  Requests for TXOP return : Regardless of whether the NPCA operation is triggered by the sharing AP’s BSS, it means that the NPCA operation will not be performed during C-TDMA
    It can be prevented until the end of allocation duration indicated in the MU-RTS TXS sent to the corresponding shared AP
    By through this, if the sharing AP intends to allocate TXOP to multiple shared AP(s), it can prevent the issue of not receiving the TXOP return frame from the shared AP due to NPCA operation
  No requests for TXOP return : NPCA can be performed during C-TDMA but only triggered by the shared AP’s BSS
    If the NPCA operation is triggered by the OBSS and performed during C-TDMA, it may cause interference with the TXOP return frame
    Therefore, NPCA may only be performed when triggered by the shared AP’s BSS frame exchanges
Sharing AP
Shared AP
CTS
Allocated time
OBSS TXOP (i.e., shared AP’s BSS)
TXOP
return
MU RTS TXS with TXOP return
NPCA operation during OBSS TXOP
Sharing AP
Shared AP
CTS
Shared AP’s BSS frame exchanges
MU RTS TXS without TXOP return
NPCA operation during OBSS TXOP
Channel
Switching
to NPCA primary channel
Switching back
to BSS primary channel
Allocated time
(Requests for TXOP return)
(No requests for TXOP return)
Shared AP’s BSS frame exchanges
OBSS STA
OBSS TXOP (i.e., shared AP’s BSS)
* Assumption : shared AP uses almost the entire TXOP

## Slide 7: Preventing interoperation between C-TDMA and NPCA
Proposal 2 : Preventing the interoperation of C-TDMA and NPCA without any conditions
  It can prevent the following ambiguity :
  Ambiguity
    We can consider the scenario when the sharing AP does not request TXOP return to the shared AP
    The frame exchange of the shared AP ends earlier than expected
      We cannot ensure that the shared AP uses almost the entire allocated TXOP
    In this case, if the sharing AP is on the NPCA primary channel, it cannot sense the situation on the BSS primary channel
      It may not cause significant issues in terms of NPCA, but it might cause major issues in C-TDMA because the sharing AP is original TXOP holder
Sharing AP
Shared AP
CTS
Shared AP’s BSS frame exchanges
MU RTS TXS with/without
TXOP return
NPCA operation during OBSS TXOP
Channel
Switching
to NPCA primary channel
Allocated time
OBSS TXOP
Considering the situation where frame exchange may end earlier than the allocated time, NPCA is not performed

## Slide 8: Summary
In this presentation, we define interoperating scenarios of C-TDMA with NPCA and discuss some approaches to allow/prevent interoperating
  Allowing interoperation based on requesting TXOP return
  Preventing interoperation without any conditions

## Slide 9: Reference
[1] 11-24/0209r6, “Specification Framework for TGbn,”

## Slide 10: SP1
Do you agree to allow the NPCA operation under the following conditions during C-TDMA when the sharing AP requests TXOP return to the shared AP?
  The only event that triggers switching to the NPCA primary channel during C-TDMA is shall be with
    Shared AP’s BSS control frame exchange
    Shared AP’s BSS HE/EHT/UHR PPDU
  Signaling details are TBD

## Slide 11: SP2
Do you agree to prevent the NPCA operation unconditionally during C-TDMA?
  Signaling details are TBD