## Slide 1: NPCA Primary Channel Access
Date: 2024-12-12
Authors:

## Slide 2: Introduction
According to SFD [1], TGbn has agreed to define a non-primary channel access (NPCA) mode that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
  A BSS shall only have a single NPCA primary channel
In this proposal, we discuss how to access NPCA primary channel (PCH)

## Slide 3: Background
Many contributions have discussed the “switching then access” procedure; ideally, AP and non-AP STAs switch to NPCA PCH synchronously/simultaneously
  See references in [Sec 3.4 Non-primary channel access, 1] and [2]
A potential approach is to enable only AP triggered transmission in accessing NPCA PCH (trigger-only mode)
Motion #129：TGbn defines a mode of operation in NPCA where the NPCA non-AP does not use untriggered UL transmissions on the NPCA primary channel [1]
  This mode can be enabled/disabled by the AP
  Whether the mode is for all associated non-APs or per non-AP is TBD
  TBD whether MU EDCA parameters mechanism is used for this or not

## Slide 4: Proposed Solution 1 Enable Trigger-only Mode & Contention-enable Mode
However, with trigger-only mode
  Non-AP STAs passively lose the opportunity for channel contention after switching
  especially for those that have the capability to maintain medium synchronization in NPCA PCH
As such, it would be more beneficial to consider both trigger-only mode and contention-enable mode for accessing NPCA PCH
AP signals access mode, trigger-only mode or contention-enable mode, which include
  Trigger-only mode: enable only AP triggered transmission in accessing NPCA PCH
  Contention-enable mode: both AP and non-AP can initiate contention and obtain transmission opportunity in accessing NPCA PCH
Besides, we may define another restricted contention-enable mode, see next page

## Slide 5: Proposed Solution 1 - ctnd Enable Restricted Contention-enable Mode
What is a restricted contention-enable mode for NPCA?
  Let non-AP use EDCA to access NPCA PCH, improve overall possibility to win contention
  Mandate non-AP to share wireless resources to AP on NPCA PCH
    non-AP may signal its traffic status (BSR or TID) for AP’s consideration
  AP may choose whether to reply/accept depending on its capability (whether can reply on NPCA PCH) and channel state
  AP may perform BW extension to find more available channels after being shared
    A special case: PCH is idle on AP side, then PCH can potential also be utilized
with the following benefits
  Let non-AP keep the opportunity for channel contention in accessing NPCA PCH
  Take the advantage of AP triggered transmission in enabling “synchronous switching”

## Slide 6: Proposed Solution 2 Improvement for Triggered Access
Improvement 1: AP signals a Maximum acceptable switch time
  Considering switch time for some non-AP STAs may be too long to access a certain NPCA PCH, especially when beyond its operating bw
  AP can have control over the Maximum acceptable switch time to improve access efficiency for performing NPCA
Non-AP signals a Preferred NPCA duration/ending time
  It can choose to keep staying on NPCA PCH after this NPCA occurrence ends, to avoid frequently switching back and forth
  It can choose to stay on NPCA PCH for DSO without switching back
  It can change its choice for each NPCA occurrence by updating this time value

## Slide 7
NPCA coordination negotiation: signal location of PCH & NPCA PCH, switch delay
  Scenario: AP2 discovers its PCH2 is often busy caused by AP1’s transmission, then AP2 initiates NPCA coordination negotiation with AP1
When AP1 starts tx, it shares certain BW or time resource for AP2, with padding if needed; indicate this frame is used for NPCA switch signaling
  Scenario: AP2’s PCH2 is within the tx /operating BW of AP1
  The same BW can be allocated to non-AP STA in BSS1 after AP2 is done using
Proposed Solution 3
MAP-assisted Access
TA = AP1 | RA = Broadcast | AID 12 = AP2 ID | RU Allocation = Shared BW | Allocation Duration = Shared time | Trigger Usage = NPCA switch signaling | AID 12 = non-AP
MAC header |  | User Info field #1 |  |  |  | User Info field #2
Example: Trigger frame |  |  |  |  |  | 

## Slide 8
Proposed Solution 3 - ctnd
MAP-assisted Access
For AP2, corresponding actions can be below
  If shared BW includes PCH2, then signal on PCH2 to non-AP STAs to switch to NPCA PCH2
  If shared BW includes NPCA PCH2 but not PCH2, then switch to NPCA PCH2 immediately and perform channel access; it may not need to perform backoff if BW and time has been shared
  If shared BW includes both PCH2 and NPCA PCH2 , then signal on PCH2 to non-AP STAs to switch to NPCA PCH2; it may not need to perform backoff after switching to NPCA PCH2 if BW and time has been shared

## Slide 9: Summary
In this contribution, we discussed how to access NPCA PCH and corresponding solutions
  Solution 1: Enable trigger-only access mode & contention-enable access mode
  Solution 2: Improvement for triggered access
  Solution 3: MAP-assisted access
Notes: In this proposal, we focus on the TXOP level preemption, introducing a credibility criterion to assist the fair classification among streams and honest behavior between STAs to further promote the preemption feature

## Slide 10: Straw Poll 1
Do you agree to define a mode in NPCA where the non-AP can access NPCA primary channel after switching under TBD conditions?
NOTE – Whether to mandate the non-AP to share wireless resources to AP on NPCA PCH is TBD

## Slide 11: Straw Poll 2
Do you agree that the AP may signal a maximum acceptable switch time in NPCA?
NOTE – Considering the switch time for some non-AP STAs may be too long to access a certain NPCA PCH, degrading the overall access efficiency for performing NPCA

## Slide 12: Straw Poll 3
Do you agree that the non-AP may signal a preferred NPCA duration/ending time when responding on the NPCA primary channel?

## Slide 13: Straw Poll 4
Do you agree to introduce NPCA coordination negotiation between APs?
NOTE – The detailed signaling procedure is TBD

## Slide 14: References
11-24/209r6, Specification Framework for TGbn
11-23-2005-01-00bn-non-primary-channel-access-npca