## Slide 1: Considerations on NPCA Follow Up
Date: 2024-11-26
Authors:

## Slide 2: Introduction
Non-Primary Channel Access (NPCA) has been widely discussed in TGbn group[1-9].
The first motion for NPCA passed at the May 2024 meeting.
TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
  The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
  A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions

## Slide 3: Motivation
If the only one NPCA primary channel is also known to be busy due to TBD conditions?
Ongoing/potential interferences may cover or interfere with the predefined NPCA primary channel. It may happen that a predefined NPCA primary channel has been interfered with for a long time, or it is known in advance that it will be interfered with for a long time in the future.
Setting only one NPCA primary channel has low implementation complexity. However, the channel conditions will change, a fixed position is not always the best choice.
Slide 3

## Slide 4: Proposal: NPCA primary channel update
During the NPCA capability negotiation or update phase, AP determines the NPCA primary channel to update based on bandwidth of BSS, OBSS and other ongoing or potential interferences, etc. AP got related indications during or before NPCA negotiation or update phase. NPCA primary channel updates occur when necessary, the specific conditions for triggering updates are not limited.
Element ID | Length | Element ID Extension | NPCA Primary Channel | Effective Time
AP announces the NPCA primary channel (via channel number etc.) and the time it becomes effective to STAs. . For example, the time can be indicated by a delay (microseconds or the number of beacon cycles) after the AP sends the corresponding frame. After it takes effect, the NPCA STAs can switch to it when NPCA conditions are met. Before it takes effect, the NPCA STAs switch to the old NPCA primary channel or NPCA mode is disabled.
The above information can be carried in a NPCA element of the beacon and other management frames.
The time when the updated NPCA primary channel takes effect
AP
beacon
beacon
beacon
First announcement

## Slide 5: Summary
In this contribution, we propose to update NPCA primary channel.
AP announces the NPCA primary channel and the time it becomes effective. After it takes effect, the STA can switch to it when NPCA conditions are met.
The mechanism to update the NPCA primary channel to adapt to the channel conditions is conducive to realizing the original intention of non-primary channel access.

## Slide 6: References
[1] 11-23/34, Non-primary channel utilization
[2] 11-23/1414, Secondary channel usage follow up
[3] 11-23/961, UHR secondary channel access
[4] 11-23/797, Non-primary channel access
[5] 11-23/1891, Nonprimary channel access - follow up
[6] 11-23/2005, Non-primary channel access (NPCA)
[7] 11-24/427, Enabling Non-Primary Channel Access
[8] 11-24/486, Some considerations on non-primary channel access
[9] 11-24/70, Some details about non-primary channel access

## Slide 7: SP
Do you support to include the following in the 11bn SFD?
  After NPCA enabled, AP may update the NPCA primary channel through beacon and TBD frames, which include below information:
  -- Updated NPCA primary channel
  -- The time when the updated NPCA primary channel takes effect