## Slide 1: AMSDU Aggregation operations based on SCS
Date: 2024-9-4
Authors:

## Slide 2: Introduction
One of the 11bn goals is to further improve the MSDU QoS performance , including the (peak) latency performance, at least for some kinds of traffic
Since 11be, the SCS steam has been introduce to help classify traffic in the MSDU level based on different parameters, including the delay bound/MSDU lifetime etc.
In [1], some proposals have been discussed about the MSDU QoS enhancement based on SCS
In this contribution, we try to further enhance the QoS of MSDUs in AMSDU based on the SCS stream

## Slide 3: Recap: AMSDU Aggregation Operation
The current AMSDU Aggregation(Tx) is based on the MSDU’s DA/SA/Priority parameters:
  No matter what the SCSID is, the MSDUs can be aggregated in one AMSDU as long as those MSDUs map to the same RA/TA/TID
  And to maintain the MSDU order in the receiver, the AMSDU Aggregation needs process the MSDUs at the order of the MSDUs’ arrival timing, no matter what the MSDUs’ SCS stream is
  In practical products, the AMSDU aggregation parameters that depend on the implementation can include,
    The number of MSDUs to be included,
    The max length of the final AMSDU,
    The “aggregation timeout” to wait for the new MSDU to be included in one AMSDU

## Slide 4: Recap: AMSDU Aggregation Operation
  Below is an example that shows a transmitter that can aggregate max 4 MSDUs in one AMSDU. Although the SCS traffic has 2 MSDUs, the current AMSDU aggregation procedure still needs aggregate MSDUs from other non-SCS traffic to keep the MSDU order.
  And, once a MSDU is aggregated into one AMSDU (which will be included in one MPDU), it will share the same L2 MPDU parameters with other MSDUs, until the corresponding MPDU is transmitted successfully or dropped (e.g. due to lifetime expiration)
    Same SN/PN
    Same Tx MCS (or further, same Tx rate adaptation/scheduling algorithm, same retransmission algorithm etc.)
    Same AMSDU level lifetime (current baseline requires the AMSDU uses the maximum MSDU lifetime value among all the MSDUs, in order not to drop any MSDU)
  Generally, the current AMSDU Aggregation procedure do not consider the finer QoS differences (e.g. the belonging SCS stream) among MSDUs, as long as those MSDUs map to the same TID

## Slide 5: Proposed Solution
Based on the SCS stream establishment, the AMSDU Transmitter and Receiver also establish additional rules for the AMSDU Aggregation operations for the corresponding SCS traffic/MSDUs,
  For the AMSDU transmitter (Aggregation side),
    When the AMSDU transmitter processes an AMSDU aggregation, the MSDU’s SCS stream (SCSID) is also considered
      For example, the additional AMSDU operations rules can require only MSDUs belonging to the same SCSID can be aggregated into one AMSDU
      The additional AMSDU operations rules can also allow whether the MSDU belonging one SCSID can be aggerated with MSDUs belong other SCSID
        This can be caused by the implementation/resource limitations
      The MSDUs that do not belong to any SCS stream are aggerated in the same AMSDU

## Slide 6: Proposed Solution
Example for the AMSDU Transmitter,
  The AMSDU Transmitter and Receiver establish two SCS streams, and also establish additional AMSDU operation rules to require the SCS1 (SCSID1) traffic MSDUs to be isolated from the non-SCS/SCS2 traffic MSDUs during the AMSDU aggregation
  So the AMSDU Transmitter,
    Will only aggregate MSDUs belonging to SCS1 into one AMSDU in the order of the corresponding MSDU arrival time
    Will still aggregate MSDUs belonging to non-SCS/SCS2 into one AMSDU in the order of the corresponding MSDU arrival time

## Slide 7: Proposed Solution
Based on the SCS stream establishment, the AMSDU Transmitter and Receiver also establish additional rules for the AMSDU Aggregation operations for the corresponding SCS traffic/MSDUs,
  For the AMSDU receiver (de-aggregation side),
    When the AMSDU receiver processes the MSDUs de-aggregated from an AMSDU,
      Depending on the implementation, the possible options can be:
        Option 1: the same as the existing AMSDU de-aggregation operations for AMSDU under both AMPDU and non-AMPDU;
        Option 2: enhance the case of AMSDU under AMPDU agreement,
          If the AMSDU is under the AMPDU agreement, the MSDU’s SCS stream (SCSID) is also considered for the MSDU’s replay detection and delivery order
      We think the possible options are all implementation specific, and may not be defined in the specification
        And for the above Option 2, we provide a possible solution in the Appendix to show the feasibility of the option

## Slide 8: Proposed Solution
Some reasons to not (only) use specific TID for SCS stream, in which the MSDUs in different SCS stream will naturally be aggerated into different AMSDU
  Multiple SCS streams may be mapped to same TID, as already discussed in the 11bn group
  TID is a quite “lower MAC” resource, which indicates
    Some features related to TID can be implemented in lower MAC,
    in many implementations, the lower a feature is, the more possible the feature is done by HW(hardware)
    For example, some implementations have limitation of max number of Tx/Rx BA Agreement
  On the other hand, the AMSDU Aggregation/De-aggregation etc. features can be done in SW/Driver level, which means the features on those levels can be more easy to be enhanced/modified
    Of course, there are also implementations that use the HW for the AMSDU Aggregation/De-aggregation operations

## Slide 9: Simulation
Simulation is done to compare the proposed AMSDU Aggregation operations based on SCS and the legacy AMSDU operations
  In the simulation, only the AMSDU Aggregation(Tx) operation is different between the proposed AMSDU operation and the legacy AMSDU operation
    The AMSDU Rx (reorder/duplicate check/delivery to upper layers) uses the same procedure as that in the legacy AMSDU operation
Simulation scenario:
  Run two DL application traffics based on UDP between the AP and the STA
    One application traffic uses the UDP destination port (dport) of 9, and another uses the UDP dport of 10
    The two application traffics map to the same TID (AC_BE in our simulation)
  Establish one SCS Stream for the application traffic that uses the UDP dport of 9
  Run the two application traffic simultaneously

## Slide 10: Simulation
General simulation condition:
  A single link between AP and STA, with the capability of BW80 + 1x1
  Use the constant rate (or fixed rate) of MCS9
  Use the MPDU level packet error rate (MPDU PER), to simulate the error rate of every single MPDU (containing AMSDU)
    The MPDU PER ranges from 1% to 25% in the simulation
  Use the AMSDU+AMPDU for traffic delivery, and no limit for the AMSDU aggregation number
    The number of sub-MSDU in AMSDU is limited by the max AMSDU size (~11K Bytes) and the available TxOP remaining time
  Use the AC_BE with TxOP limit of 2.528ms (default value in 11me)
  Use two different application traffic models with 1500 bytes MSDU and different packet interval
    One application traffic model uses the packet interval of 500us, and this is the traffic that uses UDP dport=9 and the SCS Stream SCSID1 is established over this traffic
    The other application traffic mode uses shorter packet interval (exact values are showed in the later simulation results)
Figure of Merit:
  Packet delay of the application traffic with dport=9 (i.e. the SCS Stream of SCSID 1)
    Record the delay of packet that is successfully exchanged

## Slide 11: Simulation
We use the PCAP sniffer file to illustrate the difference of the proposed AMSDU aggregation operation and the legacy AMSDU aggregation operation
  For the propose AMSDU aggregation operation, below is an AMPDU containing AMSDU. And the AMSDU only contains the MSDUs that belong to the same SCS Stream. For example, in the simulation, only MSDUs with UDP dport=9 are aggregated into the same AMSDU, and other MSDUs with UDP dport=10 are aggregated into the other AMSDU
  For the legacy AMSDU aggregation operation, below is an AMPDU containing AMSDU. One AMSDU can contain MSDUs with both UDP dport=9 and UDP dport=10.

## Slide 12: Simulation
Simulation Result 1:
  SCS Stream (UDP dport=9) uses ~500us packet interval in the application layer
    This traffic’s theoretical throughput is about 24Mbps (1500B/500us )
    So this traffic occupies about 1/16 of the 802.11 BSS max link capability (~400Mbps, BW80/MCS9/1x1)
  Non-SCS Steam (UDP dport=10) uses ~60us packet interval in the application layer
    This traffic’s theoretical throughput is about 200Mbps (1500B/60us )
    So this traffic occupies about 1/2 of the 802.11 max link capability (~400Mbps, BW80/MCS9/1x1)
  The right figure shows the average packet delay of the SCS Stream (UDP dport=9) traffic with different AMSDU operations
    As the total traffic (224Mbps, SCS Stream + non-SCS Stream) do not fully occupy the whole BSS link capability (400Mbps), most of MPDUs can be exchanged successfully with enough retransmission opportunities. So the average packet delay at different MPDU PER do not vary too much
    The average packet delay for the case with the propose AMSDU aggregation operation is only half (~120us) of that for the case with the legacy AMSDU aggregation operation (~240us)

## Slide 13: Simulation
Simulation Result 2:
  SCS Stream (UDP dport=9) uses the same traffic model as that in Simulation Result 1
  Non-SCS Stream (UDP dport=10) uses the different traffic model from that in Simulation Result 1.
    In this simulation, non-SCS Stream traffic nearly saturates the 802.11 BSS link capability
  The right figure shows the average packet delay of the SCS Stream (UDP dport=9) traffic with different AMSDU operations
    As the non-SCS Stream traffic almost saturates the 802.11 BSS link load capability, the SCS Stream’s packet delay increases along with the increase of the MPDU PER
    Still, at all different MPDU PER, the average packet delay for the case with the propose AMSDU aggregation operation is better than that for the case with the legacy AMSDU aggregation operation
      The former case has a 8%~10% (1.5ms~2ms) shorter average packet delay

## Slide 14: Summary
In this contribution, we discuss the possibility of AMSDU Tx/Rx operations based on SCS stream
  The AMSDU Transmitter and Receiver will establish additional AMSDU Aggregation operation rules based on the established SCS stream
  The AMSDU Tx will classify MSDUs based on SCSID during AMSDU aggregation
We also provide some simulation results to show the benefits (shorter packet delay) of the proposed AMSDU Aggregation operations

## Slide 15: Straw Poll
Do you support that the UHR AP and UHR STA can support an AMSDU Aggregation operation rule, in which only MSDUs with specific one or more SCSID(s) can be aggregated into the same AMSDU?
  The other MSDUs that do not belong to those specific SCSID(s) still follow the legacy rule of AMSDU Aggregation operation
  The detailed signaling/establishing procedure of enabling this rule is TBD

## Slide 16: References
[1] 11-24-0463-01-00bn-qos-enhancements-for-uhr

## Slide 17
Appendix

## Slide 18: Possible method for AMSDU Receiver with SCSID
Example for the AMSDU Receiver,
  For the AMPDU+AMSDU case, the AMSDU Receiver will use the parameter tuple <TA, TID, SCSID> for the reorder/replay/delivery operation of MSDUs
    It behaves as if the AMSDU Receiver is using a reorder buffer control based on <TA, TID, SCSID>, instead of the legacy reorder buffer control based on <TA, TID>
    Actually, for existing AMDPU reception process, the reorder/replay detection solution can be different depending on implementations
    Left figure shows one typical implementation for the AMPDU reorder/replay detection process,
      The Reorder Window in the figure is just a logical module. Its data structure varies depending on implementation
        It can be an data array containing elements of SN/PN. Or,
        It can just a linked-list containing buffer pointer to each MPDU/AMSDU

## Slide 19: Possible method for AMSDU Receiver with SCSID
For the AMSDU Receiver operation based on SCS stream,
  The <TA, TID> reorder window is further divided into <TA, TID, SCSID> reorder window
  The multiple <TA, TID, SCSID> reorder windows use the same WinStart/WinEnd/WinSize parameter
  Once an MPDU/AMSDU is received, it’s firstly classified into one of the <TA,TID,SCSID> reorder window
    If an MDPU/AMSDU with specific SN/PN is classified into one <TA, TID, SCSID> reorder window, the corresponding position element of other <TA, TID, SCSID> can be labelled as INVALID.
    The <TA, TID, SCSID> reorder window will ignore those INVALID element for the later Reorder/Replay detection process
  The Reorder/Replay Detection Process is done per each <TA, TID, SCSID> reorder window
    The INVALID element can be ignored in the process
  The later MSDU delivery (or passing up to next MAC process) is also done per <TA, TID, SCSID> reorder window
    Still, the INVALID element can be ignored in the process. i.e. the corresponding element is not treated as a “hole” in the process

## Slide 20: Possible method for AMSDU Receiver with SCSID
This is an example for the AMSDU Receiver,
  The AMSDU Transmitter and Receiver establish two SCS streams, and also establish additional AMSDU operation rules to require the SCS1 (SCSID1) traffic MSDUs to be isolated from the non-SCS/SCS2 traffic MSDUs
  Assume the AMSDU arrival sequence is AMSDU3/AMSDU4/AMSDU2/AMSDU1
    The right figure illustrates how each <TA, TID, SCSID> Reorder Window processes the receiving AMSDU
  As long as each <TA, TID, SCSID> Reorder Window satisfies its own delivery MSDU requirements, the MSDUs in the corresponding <TA, TID, SCSID> Reorder Window can be triggered to be delivered independently