## Slide 1: Coex SC Closing Report
Date: 2025-01-16
Authors:

## Slide 2: Abstract
Closing report for IEEE 802.11 Coex SC (Coexistence Standing Committee) for January 2025.

## Slide 3: Coex SC’s week at a glance
Coex SC met once this week
Technical discussion topics
ETSI BRAN Update
Bluetooth SIG Update
Review of NBE with LBT normative text for EN 303.687
Status update on proposed comment resolution for LBT comments against 802.15.4.ab

## Slide 4: ETSI BRAN Update to 802.11 (1/3)
EN 303 687 (Wireless Access System/Radio Local Area Network (WAS/RLAN) in the license-exempt 6 GHz band)
Version 1.1.1 has been published; Updates to OJEU expected during first quarter in 2025
Work on next version continued
TC BRAN achieved consensus on Narrowband Frequency Hopping (NB FH) medium access rules (see draft version 1.1.6)
  General concept approved;
  details (e. g., various durations) reman to be defined at future meetings
Publication in OJEU still on hold:
  Open question on potential lack of technology neutrality
  Request for clarification arrived after BRAN #125
  ETSI’s response to the EC is available from BRAN(24)127006r1
discuss proposals related to requirements for NB FH operation
contribution discusses the inclusion of Client-to-Client (C2C)

## Slide 5: ETST BRAN Update to 802.11 (2/3)
EN 301 893 (Wireless Access System/Radio Local Area Network (WAS/RLAN) in the license-exempt 5 GHz band)
Final national voting concluded
  No objections
  No comments
ETSI published version 2.2.1
  Offered to European Commission for citation in the Official Journal of the European Union (OJEU)
  Currently, average duration of Harmonised Standards (HSs) exceeds one year

## Slide 6: ETST BRAN Update to 802.11 (3/3)
European Commission decision 2021/1067 (and amendments)
updates related to Out-Of-Band Emissions (OOBE) below 5935 MHz for Very Low Power (VLP) devices
Decision to raise OOBE from −45 dBm/MHz to −37 dBm/MHz delayed until end of this year

## Slide 7: Update from Bluetooth SIG Work
  Work on technical proposal for ETSI BRAN:
  Draft text for EN 303 687 (Clause 4)
    ACCEPTED in December (BRAN #127)
    A few TBD parameters still need to be finalized in February 2025 (BRAN #128)
  FCC strategy in process
  Change in Leadership
  FCC shifting back to Republican control; timing of NPRM activities uncertain; Net Neutrality the focus again

## Slide 8: Technical Discussions (1/2)
Review of BRAN(24)124017r3 (NBE with LBT normative text)
  New alternative type of channel access mechanism:
    “Narrowband Equipment (NBE) with listen before talk (LBT)”
    NBE-LBT shall perform an NB CCA before transmitting on an NB channel,
    Two priority classes: determine how often CCA is repeated in case of busy channels
    EDT = function of TX power. Having upper and lower limits
  Reminder: Local copy of ETSI BRAN documents available in the 802.11 members’ area

## Slide 9: Technical Discussions (2/2)
  Review of 15-24/0407r7 (“Proposed Resolution for Comments #988” on LBT for 802.15.4ab)
  Building on BRAN(24)124017r3
  Proposing that LBT-based solution should be the de facto channel access mechanism in 802.15.4ab.
  Ongoing discussion; no consensus so far; expecting deferral of technical comment resolution (withdraw comment or rejection based on non-consensus of the comment resolution committee)

## Slide 10: Plans for March
Two dot11 Coex (only) slots
Tuesday AM2
Thursday AM1
One joint session with 802.15.4ab Tuesday PM3/EVE
Topics:
Update on ETSI BRAN
Update on Bluetooth SIG
Technical submissions (tba)
Note: coexistence-related topics are welcome. Please contact the Chair

## Slide 11: Telcos
No telco scheduled.
May be announced with 10-day notice. Member feeling the need for telco and have submissions ready for discussion are asked to approach the Chair.

## Slide 12: References for this week
Agenda for this week: 11-24/2101
Snapshot Slide: 11-24/2102
Meeting / Chair’s Slide Deck: 11-24/2103
Closing report: 11-24/2104
Meeting minutes: 11-25/0072