## Slide 1: Roaming Configuration to Reduce Ping-Pong
Date: Dec. 18, 2024
Authors:
Name | Affiliations | Address | Phone | Email
Pei Zhou | TCL | Building G1, TCL International-E City, Shenzhen, Guangdong, China. |  | zhoupei36@gmail.com
 | TCL |  |  | 

## Slide 2: Introduction
  Seamless Roaming has become the dominant feature of UHR
    A lot of roaming related motions (e.g., Motion #2, Motion #26, Motion #27, Motion #44, Motion #162) has passed [1]
  Seamless Roaming provides a non-AP MLD continuous and reliable wireless communications
  However, frequently handover between neighboring AP MLDs causes a bad QoS/QoE
  Few contributions has discussed how to improve ping-pong issue
    Contribution [2] proposed a new concept “Client Experience Score + areas for improvement”
    Contribution [3] discussed how AP can use the “BTM Status frame” to warn/avoid ping-pong
  In this contribution, we propose a flexible and accurate Roaming Configuration mechanism to reduce the potential Ping-Pong issue

## Slide 3: Define Roaming Configurations
To avoid potential ping-pong, we need to configure the accurate triggering conditions of non-AP MLD’s roaming execution
Triggering conditions include one or more of the following
  Condition A: Roaming configurations between non-AP MLD and Serving AP MLD
  Condition B: Roaming configurations between non-AP MLD and Candidate AP MLD(s)
  Others are TBD
  Roaming configurations include one (two) or more of the following
  Reference value (e.g., RSSI, delay, Data Rate): Ref
  Hysteresis value: Hys
  Threshold value: Ths
  Others are TBD

## Slide 4: Case study
At legacy roaming point, frequent ping-pong may occur between two AP MLDs
So, we can use Roaming Configurations to the change the roaming point
  Example 1: (Leaving condition)
    Condition A: RSSI of Serving AP MLD worse than Ths_1
  Ref_1 + Hys_1 < Ths_1
  Example 2: (Entering condition)
    Condition B: RSSI of Candidate AP MLD better than Ths_2
  Ref_2 + Hys_2 > Ths_2
To make more reliable roaming experience, Condition A and Condition B can be used together

## Slide 5: Roaming Configuration Procedures
Roaming Configurations can be initiated by non-AP MLD or Serving AP MLD before roaming
  Figure shows an example of non-AP MLD initiated Roaming Configurations
Option 1 only configures Condition A
  Once Condition A (e.g., see Condition A in slide 4) is met, non-AP MLD is free to execute roaming
Option 2 only configures Condition B
  Once Condition B (e.g., see Condition B in slide 4) is met, non-AP MLD is free to execute roaming
Option 3 configures both Condition A and B
  When both Condition A and B are met, non-AP MLD is permitted to execute roaming (i.e., send Roaming Request)
Note: it is TBD to use Roaming Configuration Request/ Response frames.

## Slide 6: Summary
Roaming Configurations make precise roaming decisions to avoid ping-pong
Open Discussions: Detailed design of
  Roaming Triggering Conditions,
    e.g., Condition A, Condition B, other conditions
    mandatory or optional
  Roaming Configuration Procedures,
    Roaming Configuration Sequence(s),
      e.g., Condition A first and then Condition B
      e.g., Stop Condition B when finding the first Candidate AP MLD that meets Condition B
    Configuration signaling/frame formats
  Roaming Configuration parameters,
    e.g., Reference value, Hysteresis value, and Threshold value
    mandatory or optional

## Slide 7: Straw Poll 1
Do you agree to add the following text to the TGbn SFD:
TGbn defines a mechanism that enables a non-AP MLD to configure roaming triggering conditions with Serving AP MLD and/or Target AP MLD(s) to reduce ping-pong.
Note: Roaming triggering conditions are the conditions that trigger a non-AP MLD to initiate roaming procedure. Detailed triggering roaming conditions are TBD.
Y/N/A

## Slide 8: References
[1] 11-24-0209-06-00bn-specification-framework-for-tgbn
[2] 11-24-1123-01-00bn-client-experience-reporting
[3] 11-24-0519-02-00bn-pingpongwarningforuhr