## Slide 1: Non-Primary Channel Access with MLO
Name | Affiliations | Address | Phone | email
Hui Che | Ruijie Networks Co., Ltd |  |  | chehui@ruijie.com.cn
Ke Zhong |  |  |  | 
Hang Yang |  |  |  | 
LongLong Hong |  |  |  | 
Fachang Guo |  |  |  | 
Date: 2024-12-30
Authors:

## Slide 2: Introduction
Current 802.11 standards:
Channel bonding is used to increase bandwidth. However, if the primary channel is congested, even if secondary channels are idle, nodes cannot transmit on them, leading to bandwidth waste. Larger bandwidths lead to lower channel utilization.
TGbn’s (Non-Primary Channel Access, NPCA) contribution:
NPCA allows switching to a non-primary channel when the BSS primary channel is congested (due to OBSS interference or other factors), helping improve spectrum efficiency.
This contribution focuses on addressing NPCA’s current limitations by considering interference on NPCA primary channels and proposing multi-link operation (MLO) as a solution to increase bandwidth utilization.

## Slide 3: NPCA Background and Challenges
Current Challenges in Wi-Fi Networks:
- In dense environments, BSS primary channel and NPCA primary channel may be congested due to OBSS interference.
- Existing NPCA solutions focus primarily on cases where the BSS primary channel is congested. However, NPCA primary channel can also be interfered with, leading to a waste of spectrum resources even when other channels are available.
Impact:
This results in bandwidth waste as APs and STAs cannot access available channels due to interference on the NPCA primary channel.

## Slide 4: The Problem with Current NPCA Solutions
Single-Link Focus:
Current NPCA solutions are designed mainly for single-link scenarios, where an AP or STA switches from a busy primary channel to a non-primary channel.
The Key Issue:
- The current NPCA mechanism does not consider scenarios where NPCA primary channel itself faces OBSS interference.
- Even if other channels are idle, APs and STAs cannot use those channels, resulting in bandwidth waste.
The NPCA primary channel of Link 1 in the AP MLD or non-AP MLD is also affected by OBSS interference.

## Slide 5: Proposed Solution - NPCA with Multi-Link Operation (MLO)
MLO
Multi-Link Operation (MLO) allows APs and STAs to communicate across multiple links. This provides greater flexibility and efficiency in channel management.
NPCA with MLO:
When both BSS primary and NPCA Primary channels are interfered with on Link1, Link2 can announce new NPCA primary channels for Link1 via Link2’s BSS Primary or NPCA primary channel.
This allows for cross-link coordination, where Link1 can use Link2’s channels, ensuring maximum bandwidth utilization.
Contribution on the NPCA with MLO
- [1] provides important insights to NPCA : the key concept in [1] is the exchange of NPCA channel information between APs, which allows them to determine whether their NPCA channels are the same or overlapping. This exchange of information can occur through the Beacon or Probe Response frames, where APs carry their NPCA information.
-Additionally, in an AP MLD , one AP can include the NPCA information of other APs within the MLD, either in the Multi-Link Element or RNR Element.

## Slide 6: Cross-Link Coordination in Detail
Scenario Example:
Link1: Both the BSS primary and NPCA channels are affected by the OBSS interference.
Link2: The Link2 uses its BSS primary channel to announce NPCA options for Link1.
Cross-Link bonding: Link1 now uses Link2’s secondary channels, resulting in effective bandwidth utilization without interference.
Outcome:
No wasted bandwidth, as Link1 and Link2 work together to identify and use available channels across both links.
Link2 Uses its BSS primary channel to announce NPCA options for Link1

## Slide 7: Conclusion
NPCA combined with MLO offers a promising solution to optimize channel utilization, especially in dense environments where both primary and NPCA channels may be interfered with.
This contribution addresses the current limitations of NPCA and significantly improves spectrum efficiency and network performance.

## Slide 8: References
[1] Consideration of MAP Coordination on NPCA Channel, 24-1596r1.