## Slide 1: Condition for Interference Channel Sounding
Name | Affiliations | Address | Phone | email
Hui Che | Ruijie Networks Co., Ltd |  |  | chehui@ruijie.com.cn
Ke Zhong |  |  |  | 
Hang Yang |  |  |  | 
Fachang Guo |  |  |  | 
Date: 2024-12-30
Authors:

## Slide 2: Introduction
Coordinated Beamforming (Co-BF)
It is a collaborative mechanism between multiple access points (APs) designed to improve network throughput and reduce latency, particularly in dense wireless environments. It aims to enhance performance by optimizing transmission across APs, ensuring minimal interference, and maximizing the efficiency of spatial stream utilization.
Current motions in Co-BF:
-Motion 99: Limits the number of APs involved in the transmission phase to 2.
-Motion 100 & 101: Define sequential NDP and joint NDP sounding protocols.
-Motion 114: Limits the maximum number of spatial streams per user to 2.
-Motion 115: Limits the maximum number of spatial streams supported by UHR sounding NDP receivers as 4.
Some Contributions[1][2] about Co-BF:
-Support up to 4 users in Co-BF
-Total Nss ≤ 4, with up to 2 SS per user
Extensive work has been done on sounding and transmission. This contribution aims to conditions of channel sounding and calculating the NULL matrix for interference channel.

## Slide 3: Interference Channel Sounding Problem
During channel sounding in Co-BF, STA1 needs to compute two critical channel matrices:
H11 (AP1 → STA1): AP1 and STA1 are associated.
H21 (AP2 → STA1): STA1 and AP2 are an OBSS Pair(Non-Associated). Meanwhile, AP2 should know if STA1 will receive the DL data during the Co-BF transmission. If STA1 will not receive data during the Co-BF transmission,
(1) AP2 does not need to calculate the NULL matrix according to H21,
(2) and further, the channel sounding for H21 is not essential.
Similarly, AP1 should know if STA2 will receive DL data during the Co-BF transmission.
H11
H21
H22
H12
If STA1 will not receive data, the channel sounding for H21 is not essential;
AP2 and STA1 are an OBSS pair.
H21 is an interference channel.
AP1 and STA2 are an OBSS Pair (op1).
AP2 and STA1 are an OBSS Pair (op2).
OBSS Pair set contains the op1 and op2.

## Slide 4: Solution
Condition for DL Co-BF interference channel Sounding
-The STA in the signal overlapping area and the corresponding AP are a valid OBSS pair.
-The downlink transmission(omni) from the AP will have an OBSS interference to the STA for the above OBSS pair.
Solution
-Step 1: Identify OBSS Pairs in the Signal Overlap Area
For the MAP coordinated set, identify the OBSS pair set of the STAs in the signal overlapping area.
-Step 2: Determine Valid OBSS Pairs
For the OBSS pair set, the OBSS pair corresponding to the STA with DL data transmission is a valid OBSS pair. For valid OBSS pairs, channel sounding and NULL matrix calculation are necessary.
This Solution ensures that the channel sounding and NULL matrix calculation are essential, reducing unnecessary air interface and computational resources overheads.
AP2 and STA1 are an OBSS pair
STA1 will receive the DL data
channel sounding for H21
calculating the NULL matrix

## Slide 5: Summary
Issue of Co-BF:
The necessary conditions for effective interference channel sounding and NULL matrix calculation: AP (AP1 or AP2) knows that its corresponding OBSS STA has DL data reception for the valid OBSS pair.
Solution
Step 1: Identify the potential OBSS pairs in the overlapping area.
Step 2: Select valid OBSS pairs for interference channel sounding and NULL matrix calculation.
This contribution addresses necessary conditions for interference channel sounding and NULL matrix calculation, reducing unnecessary air interface and computational resources overheads. This contribution presents a preliminary solution for identification of valid OBSS pair.

## Slide 6: References
[1] UHR-SIG Signaling for Co-BF, 24-1829r1
[2] Co-BF Design for UHR, 24-1822r4