## Slide 1: NPCA following up

## Slide 2: Introduction
In this contribution, we would like to discuss the group address data/mgmt. frame delivery for NPCA STA.

## Slide 3: The different view issue causes additional trouble for group addressed frame delivery and reception.
Several contributions fully discuss the different view issue on AP and STA side.
  AP or STA may switch to NPCA primary channel at any time once detecting the OBSS PPDU under certain conditions.
  It’s hard for the AP to detect when and which STAs still stay in the primary channel.
  The group addressed data and mgmt. frame intends to be received by all the STAs.
  E.g. if AP obatins the group address data frame from DS, how to make the decision, deliver or buffer them?

## Slide 4: The Proposal of group addressed mgmt. frame and data frame delivery
        Group addressed data and mgmt. frame are not allowed to be delivered on NPCA primary channel.
    NPCA STA also expects to transmit and receive the group addressed data and mgmt. frame after DTIM Beacon.
      In 11be baseline, EMLMR,EMLSR,PS STA device are expected to receive the group addressed mgmt.frame after DTIM Beacon on primary channel.
          To compatible with pre-UHR STA and make the implementation more simple.

## Slide 5: Summary
Analyze the trouble of group addressed frame delivery caused by different view issue on NPCA STA.
Propose the group addressed frame(s) are not allowed to be delivered on NPCA primary channel
Propose NPCA STA that are expected to receive the group addressed frame after DTIM Beacon.

## Slide 6
THANK YOU 

## Slide 7: Reference
24/209r6 TGbn Specification Framework for TGbn
24/1762r13 PDT-MAC-NPCA

## Slide 8: SP1
Do you agree the NPCA AP shall not transmit group addressed data and management frame on NPCA primary channel except some TBD conditions?

## Slide 9: SP2
Do you agree that NPCA STAs are expected to receive the group addressed data and mgmt. frame after DTIM Beacon?