## Slide 1: WPT Waveform Comparison
Date: 2025-01-13
Authors:

## Slide 2: Abstract
In previous contributions [1], a WPT (Wireless Power Transfer) comparison was made between OFDM and single carrier waveforms for the sake of getting the best RF harvesting efficiency for a given output EIRP.
In this contribution we add to [1] with an analysis of implemented harvester and also with a PPM (Pulse Position Modulation) waveform.

## Slide 3: WPT Considerations In Terms of RF Harvesting Efficiency
Other important considerations that were not covered in this contribution:
Impact of regulations on EIRP and duty cycle in S1G and 2.4 ISM bands
  There are multiple regulatory limitations depending on geographic location that change the preferences, range, channels, etc. of the possible WPT waveforms 802.11bp should consider.
Impact of transmitter efficiency
  Since all the system energy is eventually coming out of the WPT transmitter, it is of importance that it can operate in an efficient way so to save electricity bill or battery life.
Impact of transmitter implementation complexity (incl. thermal issues)
  There are TX power levels that require higher complexity transmitters compared to lower levels. For example, transmitter with 30dBm transmit power is much more complex compared to one with 10dBm.
Impact of interference to communication in nearby or same band
  There may be waveforms that are more prone to cause interference to neighbouring channels/bands or within the same channel.

## Slide 4: RF Harvesting Efficiency
Most RF harvesters are optimized to certain input power level. As the input power level is different  the resulting efficiency will be reduced
For example, a harvester optimized for energy collection efficiency over some arbitrary input power can look like this:
Notice that even though efficiency is not monotonic in Pin, the collected power is still monotonic
Trade-off: optimizing for long range (sensitivity)  the shorter range is slower relative to the power increase
Design consideration: optimizing for maximum harvested and stored energy vs. maximum output power [most academic reports]

## Slide 5: Considered WPT Waveform for Comparison
OFDM (high PAPR):
  Very common in multiple communication standards, e.g. 802.11ax, 5G-NR,…
  Provides very good protection for frequency selective channels
  Transmitters usually operate at 20-25% efficiency
  Keeping low out of band emissions require more complex devices, especially for higher power
Constant Envelope (low PAPR):
  Very common in multiple communication standards, e.g. 802.11b, LTE,…
  Transmitters usually operate at >50% efficiency
PPM (Pulse Position Modulation, very high PAPR):
  Several communication standards, e.g. UWB (802.15.4)
  Lower interference impact due to lower duty cycles
  Transmitters usually operate at >50% efficiency
  Transmit in high power requires higher power PAs or higher duty cycles

## Slide 6: WPT Waveform Comparison
We compared the wavefroms using the same average input power: metric is time to first packet (TTFP)
Assumptions made for: Pin, triggering frequency (50ms) and wakeup, receive and transmit energies
For device sensitivity point, PPM provides almost x10 improvement over OFDM/CE in terms of TTFP
We did not observe OFDM advantage
PPM duty cycle of 50%,10%,5%,1% means PAPR of PPM TX of 3dB/10dB/13dB/20dB resp
PPM provides flexibility to reach each efficiency point within every Pin [under HW and regulation limits]

## Slide 7: Summary
We presented RF harvesting efficiency over an examplary harvester
Main challenge is collecting enough energy from lower input power
We noticed that PPM modulation provided ~x10 advantage over OFDM or CE when comparing the same average power at the device sensitivity point.
We notice that PPM can be transmitted using efficient transmitters.
For very short cycles of few us, the impact of PPM to existing OFDM/MSK/CSS devices in S1G is very limited
Amendment recommends specific 1-2 S1G channels for energizing  An advantage
More work is needed to encompass regulatory status, tx complexity and efficiency, frequency selective channels and also interference to other devices.

## Slide 8: References
[1] 11-24-1808-00-00bp-ofdm-based-wpt-waveform, Panpan Li (Huawei)