## Slide 1: TGbn Motions List - Part 2
Date: 2025-01-01
Authors:

## Slide 2: IEEE 802.11 TGbn: Enhancements for Ultra High Reliability (UHR) WLAN Task Group
Motions List from January 2025
Chair: Alfred Asterjadhi (Qualcomm Inc.)
Vice Chairs: Laurent Cariou (Intel), Jianhan Liu (Mediatek), Kiseon Ryu (NXP)
Secretary: Yusuke Asai (NTT)
Technical Editor: Ross Jian Yu (Huawei)
PHY Ad-hoc chairs: Dongguk Lim (LGE), Sigurd Schelstraete (MaxLinear), Tianyu Wu (Apple)
MAC Ad-hoc chairs: Srinivas Kandala (Samsung), Jeongki Kim (Ofinno), Xiaofei Wang (Interdigital)

## Slide 3: Motions on January 15th

## Slide 4: Motion 190 (PHY)
Move to add to the TGbn SFD the following:
The MCS field in the User field of UHR-SIG field consists of 5 bits.
  The B11 ~ B15 of the UHR-SIG field is assigned for the MCS field
  The configuration of MCS field is TBD.
Move: Dongguk Lim Second:
Discussion:
Result:
Reference docs:[24/1427r2]. SP result: No objection.

## Slide 5: Motion 191 (PHY)
Move to add to the TGbn SFD the following:
Define the assigned bits for the NSS field and Spatial Configuration field by considering the maximum NSS is 8 in 11bn
  For non-MU-MIMO allocation of the UHR SIG field
    NSS field consists of 3 bits in the User field
For MU-MIMO allocation of the UHR SIG field
  Spatial Configuration field consists of 4 bits in the User field.
Move: Dongguk Lim Second:
Discussion:
Result:
Reference docs:[24/1427r2]. SP result: No objection.

## Slide 6: Motion 192 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/1977r5 to the latest TGbn draft
Move: Alice Chen Second:
Discussion:
Result:
Reference docs:[11-24/1977r5]. SP result: No objection.

## Slide 7: Motion 193 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/1985r3 to the latest TGbn draft
Move: Rui Cao Second:
Discussion:
Result:
Reference docs:[11-24/1985r3]. SP result: No objection.

## Slide 8: Motion 194 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1966r2 to the latest TGbn draft
Move: Giovanni Chisci Second:
Discussion:
Result:
Reference docs:[11-24/1966r2]. SP result: No objection.

## Slide 9: Motion 195 (PHY)
Move to add to the TGbn SFD the following:
In the 5bit MCS table
  MCS17 signals QPSK rate 2/3; MCS19 signals 16QAM rate 2/3;
  MCS20 signals 16QAM rate 5/6; MCS23 signals 256QAM rate 2/3
Move: Ron Porat Second:
Discussion:
Result:
Reference docs:[11-24/1826r1]. SP result: No objection.

## Slide 10: Motion 196 (PHY)
Move to add to the TGbn SFD the following:
MU-MIMO+OFDMA in both DL and UL is limited to UHR PPDU of 160 and 320MHz only
  160MHz PPDU – 996 and, when the PPDU is punctured, 484+242
  320 MHz PPDU: 2x996, 3x996 and, when the PPDU is punctured, 996+484, 2x996+484
MU-MIMO+OFDMA is further limited to a maximum of 2RUs supporting MU-MIMO and each 80MHz segment is either MU-MIMO or OFDMA
RU Allocation table in UHR-SIG is the same as that in EHT-SIG except that the rows for RU 242, 484 and 3x996+484 with two or more users are changed to Validate
Move: Ron Porat Second:
Discussion:
Result:
Reference docs:[11-24/1827r1]. SP result: No objection.

## Slide 11: Motion 197 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2046r4 to the latest TGbn draft
Move: Jianhan Liu Second:
Discussion:
Result:
Reference docs:[11-24/2046r4]. SP result: No objection.

## Slide 12: Motion 198 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2025r1 to the latest TGbn draft
Move: Eunsung Park Second:
Discussion:
Result:
Reference docs:[11-24/2025r1]. SP result: No objection.

## Slide 13: Motion 199 (PHY)
Move to add to the TGbn SFD the following:
Exclude BPSK from UHR UEQM.
Move: Qinghua Li Second:
Discussion:
Result:
Reference docs:[24/1832r6, 24/1807r0]. SP result: No objection.

## Slide 14: Motion 200 (PHY)
Move to add to the TGbn SFD the following:
Include 4K QAM in UHR UEQM.
Move: Qinghua Li Second:
Discussion:
Result:
Reference docs:[24/1832r6]. SP result: No objection.

## Slide 15: Motion 201 (PHY)
Move to add to the TGbn SFD the following:
Reuse HT stream parser for UHR UEQM with the following restrictions and extension
Move: Qinghua Li Second:
Discussion:
Result:
Reference docs:[24/1832r6, 24/1451r2]. SP result: No objection.

## Slide 16: Motion 202 (PHY)
Move to add to the TGbn SFD the following:
For equal modulation, UHR stream parser remains the same as EHT.
Move: Qinghua Li Second:
Discussion:
Result:
Reference docs:[24/1832r6]. SP result: No objection.

## Slide 17: Motion 203 (PHY)
Move to add to the TGbn SFD the following:
For bandwidths greater than 80 MHz, the coded bit parsing of UHR is stream parsing first followed by segment parsing.
Move: Qinghua Li Second:
Discussion:
Result:
Reference docs:[24/1832r6]. SP result: No objection.

## Slide 18: Motion 204 (PHY-PDT)
Move to incorporate the proposed text changes in 11-24/2028r3 to the latest TGbn draft
Move: You-Wei Chen Second:
Discussion:
Result:
Reference docs:[24/2028r3]. SP result: No objection.

## Slide 19: Motion 205 (MAC-PDT)
Move to incorporate the proposed text changes in 11-24/1961r4 to the latest TGbn draft
Move: Sanket Kalamkar Second:
Discussion:
Result:
Reference docs:[11-24/1961r4]. SP result: No objection.

## Slide 20: Motion 206 (PHY)
Move to add to the TGbn SFD the following:
CoBF is only applied in DL non-OFDMA MU MIMO transmission
C-SR is only applied in UHR DL SU transmission in each BSS
The entire U-SIG format in a UHR MU PPDU is as in the following figure
The definition of BSS color 1/2 are TBD
Move: Alice Chen Second:
Discussion:
Result:
Reference docs:[24/1834r4, 24/1831r3, 24/1864r1]. SP result: 55Y/8N/22A.

## Slide 21: Motion 207 (PHY-PDT)
Move to insert the proposed text changes below to Section 38.3.19.2 (Pre-correction accuracy requirements) of 11-24/1981r3, and to the latest TGbn draft
For the ELR PPDU carrying immediate response frame in response to a preceding soliciting frame, after compensation, the absolute value of residual CFO error with respect to the preceding PPDU carrying soliciting frame shall not exceed 15 kHz at the 10% point of the complementary cumulative distribution function (CCDF) of CFO error in AWGN at a received power of -82 dBm in the primary 20 MHz channel.
Move: Rui Cao Second:
Discussion:
Result:
Reference docs:[11-24/1841r1]. SP result: No objection.
Chair’s note: Ensure instructions are clear to the group and TGbn editor.

## Slide 22: Motion 208 (PHY-PDT)
Move to replace the “TBD” to “8 us” for the PE block in the Figure 38-xx (UHR ELR PPDU format) in Section 38.3.6 (UHR PPDU formats) of 11-24/1981r3, and in the latest TGbn draft
Note: the PE value applies for UHR ELR PPDU.
Move: Rui Cao Second:
Discussion:
Result:
Reference docs:[11-24/1841r1]. SP result: No objection.
Chair’s note: Ensure instructions are clear to the group and TGbn editor.

## Slide 23: backup

## Slide 24: Motion X (SFD Template)
Move to add to the TGbn SFD the following:
Move: Second:
Discussion:
Result:
Reference docs:[]. SP result:

## Slide 25: Motion Y (Draft Template)
Move to incorporate the proposed text changes in 11-24/xxxxry to the latest TGbn draft
Move: Second:
Discussion:
Result:
Reference docs:[]. SP result: