## Slide 1
Mobile Wi-Fi
Date: Jan 2025
Authors:
Name | Affiliation | Address | Phone | Email
Steve Arendt | CableLabs |  |  | s.arendt@cablelabs.com
Lili Hervieu |  |  |  | l.hervieu@cablelabs.com

## Slide 2: Introduction
What is Mobile Wi-Fi? A way to do AP-AP roaming without breaking the current Wi-Fi session.
1.
2.
3.

## Slide 3: Same AP-AP Roaming Can Work For Vehicles
1.
2.
3.

## Slide 4: Don’t We Already Have AP-AP Roaming?
“Sticky Client”: Client stays associated to an AP even if better AP available
Other Roaming issues:
“Edge of Coverage”: Client stays connected to Wi-Fi even if signal strength is too low and there is a cellular network available
“Sub-Optimal Band”: Client stays on a particular band even when there is a more appropriate band available (e.g. 2.4 when should be on 5, or vice versa)

## Slide 5: This Is Not A New Problem
Many attempts to improve roaming over 10+ years
  802.11r (2008) –Fast BSS Transition
    Shorten the time to re-authenticate when moving AP
  802.11k (2008) – Radio Resource Measurement
    “Assisted Roaming”
    Neighbor report to help choose next AP based on RSSI and load
  802.11v (2011) BSS Transition
    Unsolicited/Solicited roaming request
  802.11ai (2016)
    Fast Initial Link Setup
  802.11u (2011)
    Automatic discovery of networks (HotSpot 2.0/Vantage)
  Vantage/Agile Multiband
    802.11r/k/v/u
  Vantage/Optimized Connectivity
    802.11k/ai
  802.11 bn (coming)
None of these fix the underlying problem: The phone struggles to maintain optimal Wi-Fi connection, and functionality varies by phone.

## Slide 6: What’s the Real Problem?
Clients are responsible for choosing when to go to another AP or band and often don’t do a good job of Wi-Fi roaming.
Clients often stick with what they know
  Connectivity is “good enough”, don’t risk switching (reassociation delay/failure = risk)
  Stay with what they know – don’t risk changing
  Clients may not have full visibility into network
  Phones often stick to using Wi-Fi over cellular, even when Wi-Fi is the worst choice (very low throughput)
Consumer has bad experience: unresponsive phone -> turn Wi-Fi off

## Slide 7: Mobile Wi-Fi / vBSS Technology
Converts APs into a managed, virtualized Wi-Fi Radio Access Network (RAN)
  The client associates with its own virtualized BSS
  When a client moves, its virtualized BSS moves with it, no reassociation is needed
  No more need for client steering to try to force a client to roam
  Similar in spirit to cellular network
Does not require any changes to client devices: no apps, no connection manager modifications, no VPNs

## Slide 8
8
Mobile Client
AP1
Radio 1
Normal BSS
Normal BSS
Normal BSS
Radio 2
VBSS
(Assoc. Context)
Normal BSS
Normal BSS
Normal BSS
AP2
Radio 1
Normal BSS
Normal BSS
Normal BSS
Radio 2
Normal BSS
Normal BSS
Normal BSS
VBSS
(Assoc. Context)
Controller
VBSS
(Assoc. Context)
VBSS
(Assoc. Context)

## Slide 9: Example Throughput
Throughput Traditional
Position
Throughput Mobile Wi-Fi
“Bad Wi-Fi”
AP1
AP2

## Slide 10: How Well Does It Work?
Actual High-End Phone without Mobile Wi-Fi
Actual High-End Phone with Mobile Wi-Fi
Drop in throughput
NO Drop in throughput
RSSI to Red and
YellowAPs

## Slide 11: Current State of Project
Concept developed and prototyped at CableLabs -- 2018
WFA EasyMesh R5 spec contribution for Mobile Wi-Fi submitted, approved, and released (2021 - 2022).
Mobile Wi-Fi implemented in prplMesh open-source EasyMesh codebase (2022-2023).
Currently working on RDK-B implementation (2024) – RDK-B is an open-source software platform that standardizes core functions used in broadband home network devices.

## Slide 12: Automotive Possibilities
Seamless Wi-Fi connectivity for vehicles via
  Community-wide Wi-Fi networks
  Municipal Wi-Fi networks
  Automotive-specific Wi-Fi networks
  Campus Wi-Fi networks
Automotive users:
  Service vehicle fleets
  Delivery vans
  Public transit