## Slide 1: AMP PPDU Design
Date: 2025-01-13
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Ke Wang |  |  |  | 
Shengjiang Cui |  |  |  | 
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 2: Abstract
In this contribution, we discuss the remaining open issues in AMP PPDU design covering issues such as preamble, synchronization, SIG, data field and PPDU format.
Doc.: IEEE 802.11-25/0027r1

## Slide 3
Recap of the Agreements [1]
  Motion #8 for DL PPDU format
    IEEE 802.11bp will specify, in 2.4 GHz, an AMP Downlink PPDU containing at least an 802.11 preamble field, an AMP-Sync field and an AMP-Data field. Inclusion of an AMP-SIG field is TBD.
        The details of the 802.11 preamble field are TBD.
        Additionally, for transmission to backscatter STAs there will be one or more Excitation fields
        Additionally, for transmission to backscatter STAs there may be more than one AMP-Data field
            Additionally, AMP-Sync and AMP-SIG field may precede each AMP-Data field
        Name of this Downlink PPDU is TBD.
  Motion #9 for DL modulation
    The AMP Downlink PPDU AMP-Sync field and the AMP-Data field will use On-Off Keying (OOK) modulation.
  Motion #10 for DL coding
    The AMP Downlink PPDU AMP-Data field will use Manchester encoding for non-backscatter operation.
      For the Backscatter case, the AMP-Data field encoding scheme is TBD
  Motion #16 for DL data rate
    The AMP Downlink PPDU in 2.4 GHz shall support the following data rates:
      1 Mb/s (for non-Backscatter STAs only)
      250 kb/s
  Motion #18 for DL synchronization
    The AMP-Sync field in AMP Downlink PPDU in 2.4 GHz is defined with chip duration of 2us for backscattering case.
  Motion #11 for UL PPDU format
    IEEE 802.11bp shall specify, in 2.4 GHz, an AMP uplink PPDU for AMP STA supporting active transmission that contains an AMP-Sync field and AMP-Data field. Inclusion of an AMP-SIG field in the AMP uplink PPDU is TBD.
      The bandwidth of the AMP uplink PPDU is less than 20 MHz
  Motion #19 for UL coding
    11bp defines Manchester encoding for the data portion of UL transmission in 2.4 GHz, including both backscattering and active transmission.
  Motion #20 for UL clock offset
    When performing transmission, the maximum clock offset is ± 10^3 ppm for AMP Non-AP STA supporting active transmission.
  Motion #21 for UL modulation
    11bp will define On-Off Keying (OOK) modulation for AMP-Sync field and the AMP-Data field in an AMP Uplink PPDU for Active Transmission.
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 4
Preamble Design
  Two candidate legacy preambles can be considered :802.11a and 802.11b
  802.11a preamble
    Waveform: multi-carrier OFDM
    BW: 20MHz
    Format: STF(8us)+LTF(8us)+SIG(4us), overall 20us
  802.11b preamble
    Waveform: single carrier DSSS
    BW: 22MHz
    Two formats
      Long preamble for compatibility
      Short preamble for higher throughput
    SYNC+SFD+PLCP header
      Long preamble: 192us + 48us = 240us
      Short preamble: 96us + 48us = 144us
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 5
Preamble Design
  Comparisons
    Duration: 802.11b preamble is much longer than 802.11a preamble  shorter air time
    Tx power: 802.11a BW is narrower than 802.11b  less Tx power with PSD constraint
    Complexity: uniform waveform for preamble and the following AMP segments and excitation fields
  Both preambles can be supported, e.g., 802.11b for close-range backscattering and active Tx, and 802.11a for long-range backscattering and AMP assisted devices.
  Mark symbols need to follow legacy preambles [2]
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 6
Synchronization
  Asymmetric Sync sequences
    Different sync sequences for DL/UL for indication
      AMP devices will not process UL PPDU to save energy
      AMP non-AP STA only synchronizes with DL sync sequence(s) and AMP AP only synchronizes with UL sync sequence(s)
  Different DL synchronization sequence length for 250kbps and 1Mbps
    1Mbps with length 16
      Chip duration
        Same as 250kbps: 2us, total 32us, longer than preamble (8+8+4us)
        Scale with data rate: 0.5us, total 8us, shorter length is beneficial, but more complicated since AMP needs to assume two chip duration
      Sync chip duration is relevant to SIG chip duration
      Length 16 achieves good balance between false detection and miss detection probabilities
    250kbps with length 32, total 64us
      Chip duration 2us
      Formation: 16+16, one sync sequence + its complementary sequence or vice versa
  Synchronization rely on correlation at AMP non-AP STAs
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 7
DL Payload Size
  Different payload size for DL and UL
    DL frames:
      Data frame, e.g., ID(s) of AMP non-AP STAs for sensor reporting
      Other frames, e.g., management frame such as triggering frame.
    UL:
      Data frame, e.g., ID(s) of AMP non-AP STAs for inventory and/or EH related info reporting [2]
      Other frames, e.g., RFID payload, such as RN16, encapsulated in 11bp payload
    With DL/UL indication, different configurations can be applied to DL and UL, respectively.
  801.11ba
    Typical DL payload:
      MAC Header: Frame control (8) + ID (12) + TD control (12), total 32
      Frame Body: 16 for each non-AP STA ID, total 16*n and n less than or equal to 8, total less or equal to 128
      FCS: 16
      Total: less or equal to 176
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 8
DL Payload Size
  Similar structure for 802.11ba can be applied to AMP DL data frame
    Frame body is m*n
      m is the size of AMP non-AP STA ID, e.g., AID or compressed AID
      n is the number of AMP non-AP STAs to be addressed
      For close range backscatter devices, n can be 1
      For other devices types, e.g., active Tx AMP devices, maximum n can be larger than 8 since the number of deployed AMP non-AP STAs is expected be larger than 802.11ba, e.g., 32
  How to configure payload size
    DL SIG or MAC header
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 9
DL PPDU Design: BW and Waveform
  AMP part BW
    10MHz as baseline BW
      Reserve sufficient guard band on both sides to ease simple receiver implementation
      Transmission power, subject to regulation, e.g., PSD requirement, max PSD is 10dB/MHz in some country
      Balance between energy consumption and transmission power
  Waveform
    SIG and data: DSSS
    Excitation: OFDM or DSSS for backscattering
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 10
DL PPDU Design: SIG
  SIG
    Length indication
    Backscatter indication
      Indication of whether this PPDU is to trigger active device or backscattering device
      For hybrid deployment, AMP non-AP STA can stop decoding data part to save energy when unsupported mode is indicated to save energy
      For backscatter devices, they can assume excitation following DL data and still transmit UL using excitation even without successful decoding of DL data, decouple DL data and UL
    CRC
    UL configuration n bits
      Configure the following UL transmission in followed excitation field
      For backscatter devices, they can still transmit UL using excitation even without successful decoding of DL data, decouple DL data and UL
Yinan Qi (OPPO)
Slide 10
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 11
DL PPDU Design: Additional DL PPDU Format
  New DL/UL format needs to be supported
    Can be interpreted as UL PPDU from perspectives of other nodes in the same network receiving this PPDU
    Assistant node/energizer can send preamble on behalf of the AMP device and then the excitation part to AMP device for backscattering
    AMP device can be assumed with energy storage so the excitation part is purely for backscattering
    Sync may be needed for AMP devices to know when the backscattering begins
    AP has full control of the energizer to avoid misuse of excitation field
Yinan Qi (OPPO)
Slide 11
Doc.: IEEE 802.11-25/0027r1
January 2025
Preamble
SYNC
Excitation
AP
Control
Notes: Preamble + Sync + excitation

## Slide 12
UL PPDU Design
  Sync
    Uniform sync design for backscattering and active Tx
    Single sync sequence length can be applied for multiple data rates
  SIG might be needed in some cases
    AP has no knowledge of UL payload size, FEC if applied, and data rate if autonomously chosen by AMP non-AP devices
  Data
    Rate: 250kbps, 1Mbps, 2Mbps, 4Mbps
      Link budget around 66.5 dB for 4Mbps, still larger than DL link budget [3]
      250kbps and 1Mbps for backscatter AMP devices
      250kbps-4Mbps for non-backscattering AMP devices
      Chip duration can scale with rate, e.g., 0.5, 0.25, 0.125us for 1, 2, 4Mbps with chip level repetition
    FEC coding: convolutional coding with coding rate 1/2
      Not for backscattering devices due to chip duration limit 2us
      Can be done for active Tx with halved chip duration
      MSC table can be defined accordingly (w/wo coding)
Yinan Qi (OPPO)
Slide 12
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 13
UL PPDU Design: UL PPDU Format
  Active Tx
  Backscattering
    The excitation part should be further defined including at least sync and data for AP reception, i.e., UL.
    UL PPDU for backscattering should be defined as follows:
      IEEE 802.11bp shall specify, in 2.4 GHz, an AMP UL PPDU for AMP STA supporting backscattering transmission that contains an AMP-UL-Sync field, AMP-UL-SIG field and AMP-UL-Data field.
      Note: This UL PPDU is backscattered by AMP device in one excitation field which is contained in a DL PPDU
Doc.: IEEE 802.11-25/0027r1
January 2025
SYNC
Data
UL Sync+ UL Data
Excitation
Preamble
SYNC
SIG
Data
Excitation
WPT + DL Rx + backscattering UL for Data
Yinan Qi (OPPO)
Slide 13

## Slide 14
Summary
  The following issues are discussed and analysed in this contribution
    Preamble design
    Synchronization design for both DL and UL
    DL/UL SIG
    Payload size
    DL and UL PPDU format
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 15: Reference
[1] “IEEE 802.11 TGbp Motion Dock,” IEEE 802.11-24/1322r5, Nov. 2024
[2] “Further Discussion on AMP PPDU Design,” IEEE 802.11-24/1780r2, Nov. 2024
[3] “UL Data Rate for AMP,” IEEE 802.11-24/1198r0, Jul. 2024
Doc.: IEEE 802.11-25/0027r1
January 2025

## Slide 16: SP 1
Doc.: IEEE 802.11-25/0027r1
January 2025
  An AMP Downlink PPDU shall contain one Q-BPSK mark symbol and one BPSK mark symbol immediately following 802.11a preamble.

## Slide 17: SP 2
Doc.: IEEE 802.11-25/0027r1
January 2025
  An AMP Downlink PPDU shall contain an AMP-SIG field containing at least following information:
    Length indication
    Backscatter indication bit
    CRC
    UL configuration
      Details TBD

## Slide 18: SP 3
Doc.: IEEE 802.11-25/0027r1
January 2025
  IEEE 802.11bp will specify additionally, in 2.4 GHz, an AMP Downlink PPDU containing at least an 802.11 preamble field and an Excitation field.
  AMP-Sync field is TBD

## Slide 19: SP 4
Doc.: IEEE 802.11-25/0027r1
January 2025
  IEEE 802.11bp shall specify, in 2.4 GHz, an AMP UL PPDU for AMP STA supporting backscattering transmission that contains an AMP-UL-Sync field, AMP-UL-SIG field a nd AMP-UL-Data field.
  Note: This UL PPDU is backscattered by AMP device in one excitation field which can be contained in a DL PPDU.

## Slide 20: SP 5
Doc.: IEEE 802.11-25/0027r1
January 2025
  IEEE 802.11bp will specify, in 2.4 GHz, an 802.11 preamble field based on 802.11a and/or 802.11b preamble

## Slide 21: SP 6
Doc.: IEEE 802.11-25/0027r1
January 2025
  IEEE 802.11bp will specify, in 2.4 GHz, a single UL synchronization sequence length.