## Slide 1: AMP PPDU Configuration
Date: 2025-01-12
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Doc.: IEEE 802.11-25/0028r0
January 2025

## Slide 2: Abstract
In this contribution, we discuss the configuration of PPDU, focusing on PPDU length and specific PPDU field length, e.g., excitation field.
Doc.: IEEE 802.11-25/0028r0

## Slide 3
Legacy Transmission Duration Indication Methods
  PPDU length indication
    SIG: number of OFDM symbols (based on MSC, BW, etc.), or number of bytes
    Indicate only the current PPDU length
  MAC indication
    Duration field: in terms of time, e.g., us
    Include the entire transmission procedure duration including data Tx, SIFS and ACK
  802.11ba
    Frame control (3 bits) in MAC header
    Indicate 2 to 16 bytes frame body length
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0028r0
January 2025

## Slide 4
AMP UL PPDU Length: Active Tx
  Challenge: for specific use cases, e.g., inventory, AP has no knowledge of UL channel condition, payload size at AMP non-AP STA, etc.
  Explicit indication of UL PPDU length
    UL-SIG, in terms of OOK symbols
    MAC header, e.g., in frame control, in terms of bytes.
  AP configuration without AMP non-AP STA indication
    E.g., in triggering frame
    AP presumes default UL PPDU length
      Padding by AMP non-AP STA if configured UL PPDU length longer than actual payload size
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0028r0
January 2025
Notes: Insert FCS in MAC header

## Slide 5
AMP UL PPDU Length: Backscattering
  Excitation field for activating AMP devices, e.g., first excitation field
    Pre-defined duration
      Based on energy harvesting (EH) efficiency of the AMP devices
        AP can assume EH efficiency of the AMP devices and decide duration
        Obtained from AMP feedback, not applicable to the first charging excitation field (no feedback)
    Flexible duration
      Configured in the SIG field or data field ahead of excitation field
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0028r0
January 2025
Excitation
SYNC
SIG
Data
Excitation
Preamble
?

## Slide 6
AMP UL PPDU Length: Backscattering
  Excitation field for backscattering for UL PPDU transmission, e.g., second excitation field
    Challenge: AP has no knowledge of UL data rate, payload size, thus does no know the required duration of excitation field.
    AP/Energizer keeps sending excitation field until receives the indication of UL transmission duration
      UL indication of PPDU length can be contained in, e.g., explicitly in UL SIG, UL MAC header or UL payload.
      Difficult for energizer if it cannot receive indication directly
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0028r0
January 2025
Excitation
SYNC
SIG
Data
UL length indication
Excitation
Preamble

## Slide 7
AMP UL PPDU Length: Backscattering
  Excitation field for backscattering, e.g., second excitation field
    AP assumes and configures a pre-defined excitation length, e.g., the longest excitation length, to guarantee UL Tx time.
      UL PPDU length is pre-fixed;
      Such PPDU length can be updated once UL length is indicated in UL indication
      Padding can be used if the actual payload size is shorter.
      AP configures shorter length based on previous received actual PPDU length.
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0028r0
January 2025
Excitation
SYNC
SIG
Data
UL length indication
Excitation
Preamble

## Slide 8
AMP UL PPDU Length: Backscattering
  Excitation field for backscattering, e.g., second excitation field
    AMP non-AP STAs indicate the expected UL configuration, e.g., payload size, for the next UL Tx occasions
      AP receives such info and configures in DL accordingly.
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0028r0
January 2025
Excitation
SYNC
SIG
Data
Preamble
Indicate length
Data
Excitation

## Slide 9: SP 1
Doc.: IEEE 802.11-25/0028r0
January 2025
  The following configuration for UL PPDU duration shall be supported:
  AMP non-AP STA indication in UL SIG

## Slide 10: SP 2
Doc.: IEEE 802.11-25/0028r0
January 2025
  The duration of the excitation field for activating AMP non-AP STAs can be configured with multiple pre-defined values. The exact duration values are TBD.

## Slide 11: SP 3
Doc.: IEEE 802.11-25/0028r0
January 2025
  The duration of the excitation field for AMP non-AP STAs backscattering can be configured with one of the following methods:
AP/Energizer keeps sending the excitation field until feedback is received
AP assumes and configures a pre-defined excitation length
AMP non-AP STAs indicate the expected UL configuration