## Slide 1: CDM access for AMP
Date: 2025-1-10
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Ke Wang |  |  |  | 
Doc.: IEEE 802.11-25/0035r0
Jan. 2025

## Slide 2: Abstract
This submission is to discuss CDM access procedure for AMP IoT.
CDM access is able to provide more access opportunities compared without CDM(e.g. only use TDM and/or FDM).
Doc.: IEEE 802.11-25/0035r0

## Slide 3
Weijie Xu (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  In RFID, slot-aloha is used as the access procedure.
    The access timing is fully provided/controlled by the interrogator
      RFID device determines whether to access based on the its random number and the control of Query/QueryRep
    RN16 is the 1st message that RFID device send to the interrogator
    When there are collisions among RFID tags, RN16 can not be correctly decoded
      Figure: slot-Aloha in RFID[2]
Background(1)

## Slide 4
Background(2)[1]
  As discussed in [3], one of the most important scenarios is where there are large number of devices
      E.g. in logistics and warehouse scenarios
      E.g. sensors in smart manufacturing scenario
  In many of the concerned use cases as in [3], the purpose of AMP communication is to poll AMP data (e.g. sensor data, EPC code etc.).
  The ID may be unknown by the AP in these use cases. When an AMP device is trying to access the system, fast identification of an AMP device is very important.
  AMP system shall be able to provide sufficient access opportunities in order to reduce collisions and speedy the access process.
  In [4], multiple access for AMP was discussed, we propose to study TDM, FDM and CDM. In[5], we will further discuss TDM and FDM for AMP.
  In this submission, CDM access for AMP will be discussed.
Weijie Xu (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0035r0
Jan. 2025

## Slide 5
Access procedure with CDM codes
Weijie Xu (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  CDM code will be the first message from AMP device when it is triggered/polled.
  When CDM code is detected by AP, this CDM code can be used to identify AMP device for the consequent communication.
    Since the AMP device is identified, the following transmission can be scheduled by AP thus there will be no collision any more.
    Figure 1 Triggered CDM codes from multiple AMP STAs

## Slide 6
Feasibility of supporting CDM access for AMP
Weijie Xu (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  Although with low complexity, AMP device is able to generate CDM code.
      As discussed in [6], OOK waveform is proposed as the uplink waveform. There are candidate binary CDM codes (e.g. m/Gold sequence) that can work in conjunction with OOK.
  Impact of non-ideal factors
      Synchronization error
        CDM sequence from different AMP devices may be not synchronous at the beginning of transmission due to different distance from the AP or different clock drifting time
        Analysis:
          The coverage of one AMP AP will be 10m~20m, so the RTT(Round Trip Time) is only 0.067us~0.133 us
          For active device with clock accuracy of 1000ppm, the max drifting time after a time duration of 2ms is 2us.

## Slide 7
Feasibility of supporting CDM access for AMP
Weijie Xu (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  Although with low complexity, AMP device is able to generate CDM code.
      As discussed in [6], OOK waveform is proposed as the uplink waveform. There are candidate binary CDM codes (e.g. m/Gold sequence) that can work in conjunction with OOK.
  Impact of non-ideal factors
      Synchronization error
        CDM sequence from different AMP devices may be not synchronous at the beginning of transmission due to different distance from the AP or different clock drifting time
      Clock drifting
        During the transmission, the relative distance of two CDM sequence may change due to different clock drifting rate of different AMP devices.

## Slide 8
Exemplary CDM Code for AMP
Weijie Xu (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  Both M sequence and gold sequence are binary sequences. AMP device is able to generate m or gold sequence with low-complexity implementation.
    M or Gold sequence can be generated with OOK waveform
  Both m sequence and Gold sequence have good auto-correlation and cross-correlation.
  Sufficient number of sequences can be generated with m sequence/Gold sequence and their cyclic-shift sequences.
Auto-correlation of M sequence

## Slide 9
Simulation assumptions
Weijie Xu (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  Link level simulations are performed for CDM codes with the following simulation assumptions.
  Table 1: Simulation assumptions
Parameters | Values
Sequence types | m-sequence,
Number of devices / sequences | 2
Channel model | Channel D
SNR | 0.0dB
Chip duration | 2µs
Sampling rate at the AP | 20MHz
Modulation | OOK
Cyclic shift of m- and Gold sequences | 10
Sequence length | 63
Clock accuracy | +-1000ppm

## Slide 10
Case 1
Weijie Xu (OPPO)
Slide 10
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  2 Users transmit CDM code on the same resource. 2 codes are aligned in the beginning of transmission. Channel D, 1000ppm.
    Equal or non-equal receiving power at the AP side
2 AMP STAs, equal power
2 AMP STAs, 10dB power difference

## Slide 11
Case 2
Weijie Xu (OPPO)
Slide 11
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  2 CDM codes are not synchronous at the beginning and there is a 2us mis-alignment (Corresponding to 1 chip and 40 sampling points) between the 2 CDM sequence, Channel D, 1000ppm.
2 AMP STAs, Aligned
2 AMP STAs, 2us timing misalignment

## Slide 12
Comparison of CDM codes and RN16(1)
Weijie Xu (OPPO)
Slide 12
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  RN16 is used as access code in RFID. It is fragile in case of collision and channel fading.
  Under the same situation, CDM code is better than RN16.
      When the receiving power from multiple AMP STAs has similar power, CDM codes with similar power outperforms RN16 based on the simulations.
      When the receiving power from multiple AMP STAs are different (e.g. 10dB difference)
        For RN16, at most one RN16 may be decoded correctly and the other will fail
        For CDMA, at least one CDMA code can be correctly decoded and there is probability to correctly decode another one.

## Slide 13
Comparison of CDM codes and RN16(2)
Weijie Xu (OPPO)
Slide 13
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  When RN16 from multiple AMP STAs collides on the same resources, and the receiving power from multiple AMP STAs are similar, RN16 from all the AMP STAs can’t be decoded.
Decoding performance of RN16 when there is collision

## Slide 14
Observations
Weijie Xu (OPPO)
Slide 14
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
  Based on the simulation results, the following can be observed:
      There is obvious advantage of CDM access code than RN16, when there is collision on the same access resource
      With proper selection of the CDM codes (e.g. use big cyclic shift), the impact from synchronization error can be easily handled, at least for active AMP device, with a clock accuracy of 1000ppm

## Slide 15
Summary and proposals
  In this submission, CDM access is discussed and its feasibility and the advantage over RN16-like message is analyzed.
  Based on the discussion, it is proposed to support CDM access code for at least active AMP device.
Weijie Xu (OPPO)
Slide 15
Doc.: IEEE 802.11-25/0035r0
Jan. 2025

## Slide 16
Straw Poll #1
Weijie Xu (OPPO)
Slide 16
Doc.: IEEE 802.11-25/0035r0
Jan. 2025
Do you agree with the following text:
  CDM access is supported for active AMP STA.
Yes
No
Abstain

## Slide 17: Reference
IEEE 802.11-24/0826r0, Energy balance of the state-based AMP station
Specification for RFID Air Interface Protocol for Communications at 860 MHz – 960 MHz
IEEE 802.11-23/0436r0 Technical Report on support of AMP IoT devices in WLAN
IEEE 802.11-24/1501r0 Multiple Access for AMP IoT
IEEE 802.11-24/1776r0 Multiple access mechanisms for AMP
IEEE 802.11-24/1780r0 Further Discussion on AMP PPDU Design
Doc.: IEEE 802.11-25/0035r0
Jan. 2025