## Slide 1: Follow up on Downlink Sync Field Design
Date: 2025-01-13
Authors:
Name | Affiliations | Address | Phone | Email
Bin Qian | Huawei | Shenzhen, China |  | qianbin14@huawei.com
Lei Huang |  | Singapore |  | 
Panpan Li |  | Singapore |  | 
Jan. 2025
Notes: September 2012

## Slide 2: Introduction
Downlink Sync field design has been previously discussed in [1-5]
  [1] explores two options for the DL Sync field:
    A single Sync field for transmission to all AMP STAs
    Two separate Sync fields for transmission to non-backscatter STAs and backscatter STAs
  [2-4] evaluates several DL Sync sequence examples
    Suitable for backscatter STAs to perform counter based per-bit transition detection [2]
    Supports data rate indication [3-4]
  [5] proposes a Manchester-encoded Sync field for active UL transmitters
This contribution presents a design for the DL Sync field, addressing differences in link budget and data rates in both integrated and non-integrated energizer deployments
Jan. 2025

## Slide 3: Integrated vs. Non-Integrated Deployment for Non-backscattering Case
Integrated deployment
  Bottleneck: Energizer link is the limiting factor between AP and STA
  Data rate: Supports 1 Mbps for non-backscatter STAs due to higher received SNR at the STA
  Sync field: Shorter downlink Sync sequence and chip duration than WUR
Non-integrated deployment
  Coverage: Extended coverage with a separate energizer
  Data rate: Requires a lower data rate (i.e., 250 kbps) due to extended coverage
  Sync field: Requires similar Sync sequence and chip duration as WUR
Jan. 2025

## Slide 4: Unified Sync Field Design for Both Deployments
Unified Sync field design for both deployments is preferred
  Simplified receiver design: A consistent chip duration and sequence length reduce complexity, making receiver implementation easier
  Seamless STA operation: The STA can operate seamlessly in both integrated and non-integrated deployments without requiring configuration changes or different protocol handling
  Consistent protocol implementation: A single Sync field ensures uniform protocol implementation across both deployments, simplifying standardization, testing, and interoperability
Chip duration: 2 us for both deployments (same as backscatter use case [2])
  A shorter chip duration may limit performance at lower rate, especially in non-integrated deployments
Jan. 2025

## Slide 5: Synchronization Methods and Sequence Design
Three different STA types [6] may support distinct synchronization methods
AMP Assisted STAs can perform correlation-based detection
  Length-16 Sync sequence for 1 Mbps
    Length-8 sequence shows poor cross-correlation performance with random Manchester-encoded data [4]
  Length-32 Sync sequence (constructed from length-16 in the same manner as WUR) for 250 kbps
Backscatter STAs can perform counter based per-bit transition detection [2]
  Some sequence selection criteria are defined in [2]
  A distinct Sync sequence from AMP Assisted STAs can help reduce the false alarm rate
  Due to the high SNR at the STA side, a shorter sequence length (e.g., length-8) could be used
Active UL transmitters may support Manchester-encoded Sync [5]
Jan. 2025

## Slide 6: Simulation Results (1/2)
Sync sequence example for AMP Assisted STAs
  1 Mbps:
  250 kbps:
Simulation settings
  Local sequence:
  Six preceding ON symbols are considered due to 802.11 Preamble field
Jan. 2025
  Data rate indication: The peak polarity after correlation is used to indicate the data rate

## Slide 7: Simulation Results (2/2)
Sync sequence example for backscatter STAs
Cross-correlation performance
  Local sequence:
  Received signal: with eight preceding ON symbols
Jan. 2025
  Limited cross-correlation results

## Slide 8: Summary
Sync design proposals
  Unified Sync field for both integrated and non-integrated deployments
  2us chip duration for the Sync field
  For AMP Assisted STAs:
    Length-16 Sync sequence for 1 Mbps
    Length-32 Sync sequence for 250 kbps
  Backscatter STAs could use a distinct and shorter Sync sequence
Several Sync sequence examples have been provided
Jan. 2025

## Slide 9: References
[1] 11-24-1816-00-00bp-amp-downlink-sync-field-options
[2] 11-24-1797-00-00bp-design-considerations-of-dl-data-rate-and-sync
[3] 11-24-1819-00-00bp-downlink-sync-sequence-design
[4] 11-24-1803-00-00bp-sync-field-for-amp-ppdu
[5] 11-24-1982-00-00bp-considerations-for-sync-sequence-selection
[6] 11-24-1846-01-00bp-amp-client-sta-types
Jan. 2025

## Slide 10: Straw Poll #1
Do you agree to add following content to TGbp SFD:
  IEEE 802.11bp defines a consistent AMP-Sync field in AMP Downlink PPDU for both integrated and non-integrated energizer deployments in 2.4 GHz
Jan. 2025

## Slide 11: Straw Poll #2
Do you agree to add following content to TGbp SFD:
  The AMP-Sync field in AMP Downlink PPDU in 2.4 GHz is defined with chip duration of 2us for non-backscattering case
Jan. 2025

## Slide 12: Straw Poll #3
Do you agree to add following content to TGbp SFD:
  For AMP Assisted non-AP STAs, the duration of the AMP-Sync field in the AMP Downlink PPDU in 2.4 GHz depends on the data rate of the AMP-Data field. When the AMP-Data field data rate is 1 Mbps, the AMP-Sync field includes 16 chips. When the AMP-Data field data rate is 250 kbps, the AMP-Sync field includes 32 chips.
Jan. 2025

## Slide 13: Straw Poll #4
Do you agree to add following content to TGbp SFD:
  IEEE 802.11bp shall support the duration of the AMP-Sync field in the AMP Downlink PPDU in 2.4 GHz shorter than 32 us for backscattering communication
Jan. 2025