## Slide 1: Active AMP STA Polling Requirements
Date: 2025-01-12
Authors:

## Slide 2: Abstract
We analyse the performance of an active AMP STA which is only permitted to transmit after being polled.

## Slide 3: Scope: Active AMP STA
Scope is given by the TGbp Specification Framework Document:
  PM-2: 11bp defines at least one mode of MAC/PHY that allows an AMP-only device with active uplink communication in 2.4GHz subject to the following requirements:
    clock accuracy requirement is relaxed compared to legacy 802.11 devices;
    the active uplink communication can only be sent in response to being polled by the AP.
Assumed behavior of an Active AMP STA:
  Energy model:
    Awake (transmit, receive, listen) consumes aW
    Sleep recharges with a/xW, x >> 1, constant
  Not synchronized to an AP’s poll schedule (yet)
    Cycle between sleep and awake until an AMP trigger frame is received
t
E

## Slide 4: Scenario: Initial Detection of Active AMP STAs
Stationary AP
  Regularly transmits AMP Trigger Frame (TF) to poll unknown AMP STAs
  All AMP STAs within the coverage area receive the TF without errors
Active AMP STA
  STA Moves through the AP’s coverage area
  Equivalent: STA is switched on
  How long does it take to receive a TF?
STA
AP

## Slide 5: Evaluation: Mean TF Interval 10ms
Stationary AP
  Transmit TF, select random wait time from uniform distribution between [0ms, 20ms] (mean 10s), repeat...
Active AMP STA
  Awake for 1ms every 100ms
Mean
Median
90-percentile
99-percentile

## Slide 6: Evaluation: Impact of Mean TF Interval
Stationary AP
  How does the mean TF interval change the time to receive the TF?
Active AMP STA
  Awake for 1ms every 100ms
Linear Relationship
  Typical beacon interval is 102.4µs, this would give a 99-percentile of ~45s
AMP STA

## Slide 7: Evaluation: Impact of AMP STA Sleep Duration
Stationary AP
  Transmit TF, select random wait time from uniform distribution between [0ms, 204.8ms] (mean 102.4ms), repeat
Active AMP STA
  How does the sleep duration change the time to receive the TF?
Linear Relationship
  Halving the sleep duration will halve the time to receive
  Adding variance to the sleep duration does not change the results
AMP STA

## Slide 8: Conclusion
Assuming
  the AMP-TF is sent by the AMP-AP with a mean interval of 102.4ms, and
  the AMP STA has a wake / sleep cycle of 1ms / 100ms,
  the AMP STA will receive a TF within ~1 minute.
This is sufficient for many AMP applications, e.g. home temperature sensors.
This may be sufficient for some AMP applications for the initial TF; subsequent polls may be more efficient if the AMP STA’s wake schedule is known to the AP.
This is not sufficient for any event-triggered application.