## Slide 1: Wireless connectivity challenges for backscattering AMP STA
Date: 2025-01-07
Authors:

## Slide 2: Abstract
This contribution shows that the proposal presented in document 11-24-1537-02-00bp-wireless-connectivity-challenges-for-amp-only-iot-devices-under-802-11-specification is adequate for AMP backscatter STA and AMP bistatic backscatter STA

## Slide 3: Summary
Our vision of the wireless connectivity is presented in 11-24-1537-02-00bp-wireless-connectivity-challenges-for-amp-only-iot-devices-under-802-11-specification
Backscatter matches our vision presented in the contribution
  The same role of the AMP-capable STA is maintained across monostatic and bistatic modes
    The AMP-capable STA passes information to/from the tag to the distribution system and to higher layers of internet protocols
  AMP-only STA communicates through optimized .11bp frames

## Slide 4: Un-Associated mode for Active TX, Monostatic Backscatter, and Bistatic Backscatter STA
There are three types of AMP-only STAs:
Active Transmission - energy is accumulated by the STA before transmission. The energy source can be co-located with an AMP-compatible STA or separated
Backscatter STA, the STA transmits at the time the energy is delivered to it
  Monostatic – the energy source is co-located with the AMP capable STA
  Bistatic – the energy source is separated from the AMP capable STA
There is no difference between the AMP-only STA types with respect to un-associated mode to communicate between AMP-only STA and AMP-capable STA (see DCN 11-24-1537).

## Slide 5: Frame formats for Active TX, Monostatic Backscatter, and Bistatic Backscatter STA
Here are the reasons not to use PV0 and PV1 frame formats and to define frame formats optimized for .11bp. The reasons are basically the same for all AMP-only STAs: active, backscatter, and bistatic backscatter.
Using PV0 and PV1 frame formats at low DL bitrates may exceed the TXOP limit.
The new .11bp PHY is defined for STA communications; therefore, defining frame formats optimized for .11bp will not interfere with legacy STAs

## Slide 6: Straw Poll
SP#1
Do you agree to include the following text to the 11bp SFD?
  .11bp defines an “AMP-capable STA” (name TBD)
  AMP-only STAs communicate with AMP-capable STAs
  The AMP-capable STA provides access to the DS for the AMP-only STA
Note: the AMP-capable STA may be part of an access point.
Yes
No
Abstain

## Slide 7: Straw Poll
SP#2
Do you agree to include the following text to the 11bp SFD?
.11bp defines communication with AMP-only STA through optimized .11bp frames
Yes
No
Abstain

## Slide 8: References
1. 11-24-1537-02-00bp-wireless-connectivity-challenges-for-amp-only-iot-devices-under-802-11-specification