## Slide 1: DRU hybrid mode for 20 MHz-only STAs
Date: 7-Jan-25
Authors:

## Slide 2: Introduction
Several agreements on DRUs limit the allowed distribution bandwidths and the use of hybrid RRU/DRU mode.
Specifically [1]:
  Motion 65 (Distribution Bandwidth values)
    11bn supports the following DBW dependent DRU size support to maximize BW and power efficiency
      No MRU in distributed transmission
      20MHz: RU26, RU52, RU106
      40MHz: RU26, RU52, RU106, RU242
      80MHz: RU52, RU106, RU242, RU484
  (continued on next slide)

## Slide 3: Introduction
  Motion 66 (Hybrid mode)
    11bn supports per 80MHz DRU/RRU switch if PPDU BW >80MHz and no hybrid DRU and RRU mode for up to 80MHz
  Motion 20 (DW in 80 MHz)
    In a non-punctured 80 MHz PPDU, the following distribution bandwidth modes are allowed for DRU
      80 MHz
      20 MHz + 20 MHz + 40 MHz (or 40 MHz + 20 MHz + 20 MHz)

## Slide 4: Illustration of agreements
Allowed
Not Allowed

## Slide 5: 20 MHz-only STAs
20 MHz-only STAs are mostly confined to the primary 20 MHz
They can not be combined as easily with other STAs in an OFDMA transmission due to this limitation
  Lack of opportunities may get worse when AP uses DRU
It may make sense to allow 20 MHz to send regular RU in combination with DRU, e.g.:

## Slide 6: 20 MHz-only STAs
This could be easily achieved by modifying the existing agreement:
  11bn supports the following DBW dependent DRU size support to maximize BW and power efficiency
    No MRU in distributed transmission
    20MHz: RU26, RU52, RU106, RU242
    40MHz: RU26, RU52, RU106, RU242
    80MHz: RU52, RU106, RU242, RU484
  Doesn’t conflict with agreed signaling

## Slide 7: Conclusion
Hybrid RRU/DRU mode is not well suited for 20 MHz-only STAs
We propose to allow a hybrid mode that provides better compatibility with 20 MHz-only STAs

## Slide 8: Straw Poll 1
Do you agree to define a hybrid mode that allows a mix of 20 MHz RRU and 40 MHz DRU within 80 MHz, for use by 20 MHz-only STAs

## Slide 9: References
[1] tgbn-motions-list-part-1, IEEE 802.11-24/0171r26