## Slide 1: Indication of the Unavailability Information for IDC
Date: 2025-01-14
Authors:

## Slide 2: Introduction
The motion related to signaling dynamic unavailability information has been agreed [1]
  (Motion #146) A non-AP STA that is a TXOP responder can indicate in a response frame 1) for how long it will be available, if known and/or 2) whether it will be unavailable after a specific point in time and, if known, for how long
    The response frame is a multi-STA BlockAck frame sent by the non-AP STA in response to the initial control frame or to MPDUs that solicit an immediate response
Details on signaling dynamic unavailability information using a Multi-STA BA frame are under discussion [2-19]
However, the signaling details for indicating that a non-AP STA has no unavailability information have not been discussed
In this contribution, we discuss how the non-AP STA conveys its absence of unavailability information to the AP using the Multi-STA BA frame.

## Slide 3: The response rule for a DUO non-AP STA
If a DUO STA receives an individually addressed BSRP Trigger frame as ICF that solicits a response in non-HT (dup) PPDU and contains a Multi-STA BA frame, the STA responds with the Multi-STA BA frame as ICR (Motion #152)
If a DUO STA’s unavailability information changes, it can transmit the Multi-STA BA frame to update the unavailability information. The AP will then maintain the most recent dynamic unavailability report (Motion #143)
AP
DUO
STA
ICF
BSRP TF
Multi-STA BA
Unavailability Info ‘A’
ICR
DL PPDU
Multi-STA BA
Unavailability Info ‘B’
AP updates ‘A’ info
Unavailability Info ‘A’
Unavailability Info ‘B’
AP overwrites the information of ‘A’ with ‘B’
AP
DUO
STA
Individually addressed
BSRP TF
ICF
ICR
Multi-STA BA
Non-HT (duplicate) PPDU
Indication : solicits the response in non-HT (dup) PPDU and contains a Multi-STA BA frame
Unavailability Info ‘A’
Unavailability Info ‘A’

## Slide 4: Problem Discussion
In the previous slide, we discussed the response rules for a DUO STA based on approved motions
  When a DUO STA receives an individually addressed BSRP TF as ICF that solicits a response with a Multi-STA BA frame in non-HT (dup) PPDU, it responds with the Multi-STA BA frame as ICR even though it has no unavailability information
  After a DUO STA reports its unavailability information, the information may change before the unavailability period starts due the internal status change. Then the DUO STA should indicate the updated information to the AP in the Multi-STA BA frame.
However, there are no signaling details to indicate the absence of unavailability information using the Multi-STA BA frame
In the following slides, we discuss two options to indicate the absence of unavailability information for a DUO STA using the Multi-STA BA frame

## Slide 5: Indication of the absence of unavailability information in the Multi-STA BA frame
Option 1) Set specific values for Ack Type & TID subfields in Per AID TID Info subfield
  Set Ack Type == 1, so that both Block Ack Starting Sequence Control and Block Ack Bitmap subfields are not present
  Set TID == TBD reserved value, to indicate it is related to unavailability information (e.g., 13)
  Pros: Less overhead than Ack Type subfield is set to 0 (not requiring the following subfields)
  Cons: Using an additional combination within the limited reserved values of the Ack Type and TID subfields
Per AID TID Info
AID TID Info
BlockAck Starting
Sequence Control
BlockAck Bitmap
AID11
Ack Type
TID
not present
== 1
== TBD (e.g.,13)

## Slide 6: Indication of the absence of unavailability information in the Multi-STA BA frame
Option 2) Set specific values for Unavailability Target Start Time & Unavailability Duration subfields in Per AID TID Info subfield
  Set Ack Type == 0 & TID == TBD reserved value, for reporting the unavailability feedback
  Set Unavailability Target Start Time == TBD value & Unavailability Duration == 0, to indicate the absence of unavailability information
    The specific TBD value of Unavailability Target Start Time field cannot be used to indicate the certain TSF time
  Pros: Using one combination of the reserved values of the Ack Type and TID subfields for reporting unavailability
  Cons: More overhead than Ack Type subfield is set to 1 (requiring following subfields for indication)
Per AID TID Info
AID TID Info
BlockAck Starting
Sequence Control
BlockAck Bitmap
AID11
Ack Type
TID
== 0
== TBD (e.g.,13)
Unavailability
Target Start Time
Unavailability Duration
Reserved
== TBD
== 0

## Slide 7: Summary
We discussed the need to indicate the absence of unavailability information using the Multi-STA BA frame, and proposed methods:
  Option 1) Using specific value of Ack Type & TID subfields
    Ack Type == 1 && TID == reserved value (e.g., 13)
    (BA Starting Sequence Control and BA Bitmap subfields are not present)
  Option 2) Using specific value of Unavailability Target Start Time & Unavailability Duration subfields
    Ack Type == 0 && TID == reserved value (e.g., 13)
    (BA Starting Sequence Control and BA Bitmap subfields are present)
    Within BA Bitmap subfield
      Unavailability Target Start Time == TBD && Unavailability Duration field == 0
      Then the TBD value of Unavailability Target Start Time subfield does not indicate the corresponding TSF time

## Slide 8: Straw Poll 1
Do you agree to add the following into the 11bn SFD ?
  An UHR STA indicates the absence of unavailability information by using a Multi-STA BlockAck frame

## Slide 9: Straw Poll 2
Do you agree to add the following to the 11bn SFD ?
  An UHR STA indicates the absence of unavailability information using a Multi-STA BlockAck frame by setting Ack Type subfield to 1 and TID subfield to TBD reserved value
    Block Ack Starting Sequence Control subfield and Block Ack Bitmap subfield are not present

## Slide 10: Straw Poll 3
Do you agree to add the following to the 11bn SFD ?
  An UHR STA indicates the absence of unavailability information using a Multi-STA BlockAck frame by setting Unavailability Target Start Time subfield to TBD value and Unavailability Duration subfield to 0

## Slide 11: References
[1] 11-24/0171 tgbn-motions-list-part1 Alfred Asterjadhi
[2] 11-23/1103 In-device Coexistence Discussion Liwen Chu
[3] 11-23/1964 Coexistence Protocols for UHR Alfred Asterjadhi
[4] 11-23/2002 In-device Coexistence and P2P – follow-up Laurent Cariou
[5] 11-24/0494 In-device Coexistence Follow Up: Control Frame Liwen Chu
[6] 11-24/0543 Coexistence Protocols for UHR – Follow Up Sherief Helwa
[7] 11-24/0834 Some Details on In-device Coexistence Insun Jang
[8] 11-24/0856 Further Discussions on In-device Coexistence Jeongki Kim
[9] 11-24/0857 ICR Consideration Liwen Chu
[10] 11-24/1109 More Consideration for In-device Coexistence Hongwon Lee
[11] 11-24/1170 Further Considerations on In-device Coexistence Jaheon Gu
[12] 11-24/1247 ICF and ICR Design For Coex Abdel Karim Ajami
[13] 11-24/1464 Discussion on ICF Insun Jang
[14] 11-24/1504 Considerations on Aperiodic In-device Coexistence Hank Hyeonjun Sung
[15] 11-24/1550 In-device Coexistence Follow Up Abdel Karim Ajami
[16] 11-24/1558 In-device Coexistence – Follow Up Sherief Helwa
[17] 11-24/1559 In-device Coexistence Next Steps Sindhu Verma
[18] 11-24/1562 In-device Coexistence Follow Up Liwen Chu
[19] 11-24/1848 Frame Exchange Sequences for In-device Coexistence Sanghyun Kim