## Slide 1: Considerations on NPCA Operation
Date: 2025-02-05
Authors:

## Slide 2: Introduction
Non-primary channel access (NPCA) allows AP and STA to access non-primary channel while the primary channel is busy due to OBSS traffic [1]
Different aspects of NPCA have been widely discussed [2-13]
  Triggering events
  Switching time
  Location of NPCA primary channel
  NPCA duration
  Hidden node / different view problem
  …
In this contribution, we will further discuss
  NPCA primary channel update
  NPCA duration update

## Slide 3: NPCA primary channel setting
Problem with AP setting the same NPCH as OBSS
  AP1 and AP2 have the same NPCA primary channel (NPCH)
  OBSS3 TXOP triggers both AP1 and AP2 to do NPCA
  AP1 or AP2 cannot utilize NPCH due to contention – NPCA gain is limited

## Slide 4: NPCA primary channel update
AP may update its NPCH considering OBSS NPCH, for example
  AP1 finds its NPCH is occupied by OBSS2 after AP1 is triggered to do NPCA by OBSS3
  AP1’s NPCH is the same as (or adjacent to) the NPCH announced by OBSS
In this way, AP reduces collision with OBSS on NPCH and gets better NPCA efficiency

## Slide 5: NPCA primary channel update
APs may coordinate on NPCH updating
  e.g., AP1 and AP2 coordinate to set NPCHs on different 80MHz subchannels on S160
  AP1 can request AP2 to update NPCH
  NPCH coordination can be supported by Multi-AP Coordination framework [15]
Additional considerations
  APs are recommended to coordinate on NPCH setting if they have a common OBSS
    Since this common OBSS may trigger both APs to do NPCA at the same time
  Other NPCA parameter setting can also be coordinated, e.g., NPCA bandwidth
  APs are recommended to set gaps (e.g., 20MHz) during NPCA transmission to avoid adjacent channel interference

## Slide 6: NPCA different view problem
Different view of OBSS TXOP length [10]
  AP’s and STA’s NPCA may be triggered by different OBSS TXOP –> different NPCA duration
  One existing solution: all STAs follow AP’s view
    e.g., STA updates NPCA duration based on AP’s NPCA duration in ICF/ICR
AP
STA1
STA2
STA3
OBSS1
OBSS2
OBSS3
P80
NAV set by OBSS1
(AP & STA1)
P80
NAV set by OBSS2
(STA2)
P80
NAV set by OBSS3
(STA3)

## Slide 7: Problem with following AP’s view
In some cases, AP may be better off updating NPCA duration based on STA’s view
For example
  When AP switches back to PCH at T1, AP cannot transmit due to OBSS2’s ongoing TXOP
  If AP was still on PCH, its NAV should have been updated by OBSS2 NAV
  AP can stay on NPCH until OBSS2 NAV ends (T2), if it does not intend to interference with OBSS2
AP
STA1
STA2
OBSS1
OBSS2
P80
NAV set by OBSS1
(AP & STA1)
P80
NAV set by OBSS2
(STA2)
T1
T2

## Slide 8: NPCA duration update
AP and STAs indicate NPCA duration in ICF/ICR
  NPCA duration is based on NAV set by the OBSS that triggers AP/STA’s NPCA
AP may update its NPCA duration based on associated STA’s NPCA duration
Additionally, AP and STAs can indicate OBSS BSS color
  i.e., BSS color of the OBSS that triggers AP/STA’s NPCA
  AP can use this to determine if OBSS viewed by STA will also affect AP itself
    AP is recommended to update if STA indicates a longer NPCA duration and OBSS BSS color known by AP
STAs switch back to PCH based on AP’s NPCA duration
  e.g., if AP updates NPCA duration based on STA2’s view, STA1 also follows updated NPCA duration
  Optional for STAs to indicate NPCA duration if they have the same view of OBSS as AP

## Slide 9: NPCA duration update
AP
STA1
STA2
OBSS1
OBSS2
Example of AP updating NPCA duration:
AP updates NPCA duration based on NPCA duration indicated by STA2 in ICF. Updated NPCA duration is indicated in AP’s ICR.

## Slide 10: Conclusion
In this contribution, we have discussed some problematic NPCA scenarios, including
  APs in OBSS set the same NPCA primary channel
  AP and STAs have different view of OBSS TXOP length
To improve NPCA efficiency, we propose
  AP may update NPCA primary channel considering OBSS NPCA primary channel
  AP may update NPCA duration based on STA’s reported information
    e.g., STA’s NPCA duration and BSS color of the OBSS that triggers STA to do NPCA

## Slide 11: References
11-24-0209-06-00bn-specification-framework-for-tgbn, Ross Jian Yu
11-23-2005-01-00bn-non-primary-channel-access-npca, Minyoung Park
11-24-0486-01-00bn-some-considerations-on-non-primary-channel-access, Ming Gan
11-24-0803-01-00bn-the-switching-time-in-npca, Yunbo Li
11-24-1077-00-00bn-discussions-on-non-primary-channel-access, Jason Yuchen Guo
11-24-1093-03-00bn-special-scenarios-in-non-primary-channel-access, Sindhu Verma
11-24-1104-03-00bn-some-details-on-npca, Seongho Byeon
11-24-1115-01-00bn-channel-switching-rules-for-npca, Vishnu Ratnam
11-24-1125-01-00bn-considerations-on-switching-for-npca, Dongju Cha
11-24-1155-00-00bn-further-discussions-on-npca, Sanghyun Kim
11-24-1218-01-00bn-npca-next-level-discussions, Gaurang Naik
11-24-1259-02-00bn-sp-based-non-primary-channel-access-follow-up, Yue Zhao
11-24-1563-02-00bn-npca-follow-up, Liwen Chu
11-24-1596-01-00bn-consideration-of-map-coordination-on-npca-channel, Yan Li
11-24-1838-00-00bn-considerations-on-coordinated-npca, Mahmoud Hasabelnaby