## Slide 1: Follow-up of automotive use case study

## Slide 2: Abstract
Jing Ma (Toyota)
In the July meeting, IEEE 802.11 WG approved the creation of Automotive (AUTO) TIG to investigate:
  Use cases, current and planned mechanisms in 802.11 for vehicle connectivity to external APs
  Gaps between requirements and standards for automotive connectivity to external APs
  Recommendations to address gaps
A use case of regional HD MAP is discussed [1]
More details and numerical examples are discussed in this contribution

## Slide 3: Recap: Regional HD MAP use case
Overview: This use case leverages opportunistic Wi-Fi connectivity for vehicles, either in motion or parked within a specific geographic region.
Functionality: vehicles connect to local WLAN access points (APs) to
  Share data such as sensor data, environmental data.
  Receive updates of the map information.
Benefits:
  Enhances the accuracy of HD maps
  Utilizes local infrastructure for efficient data exchange.
Actors: Vehicle, AP, Edge Cloud
Jing Ma (Toyota)

## Slide 4: Recap: Regional HD MAP use case
Example service level requirements
 | Assumed service level requirement | 
Range | 500m | Urban area
Information requested/ generated [2] | - 100 bytes/ object※, - 50 objects detected in vehicle | assumed uplink
 | 5000 objects updates | Assumed downlink
Look-ahead time | 1s before entering the area of interest | 
※: Information usually included in HD map are road geometry (e.g. traffic lights, intersection), road furniture (e.g. street lights ), land markers, etc.
AP
Access network (WLAN)
Download the updates of map info.
Upload the detected object info.
Jing Ma (Toyota)

## Slide 5: Example WLAN deployment for regional HD MAP use case
The area of interest has a range L
Each AP has a data transmission diameter D
Overlap between adjacent APs is represented by αD (α < 1)
Vehicle travels at a speed
Look-ahead time window is
Assumptions:
To ensure full coverage of the area, the total deployment must satisfy this condition:
,
Numerical example:
𝐿 | D | α |  |  | N
500m | 200m | 0.3 | 40km/h | 1s | 4
𝐿 | D | α |  |  | N
500m | 200m | 0.3 | 40km/h | 1s | 
AP
AP
Look-ahead area
Download the updates of map info.
Upload the detected object info.
Area of interest
Where represents the required number of APs. Simplified as,
Jing Ma (Toyota)
Coverage condition:

## Slide 6: Numerical example for regional HD MAP use case
Case 1: Vehicle downloading map data in light traffic while approaching the area of interest
,
The downlink time () should meet the required look-ahead time window,
AP
AP
Area of interest
Look-ahead area
Each vehicle downloads bytes of data
As the vehicle approaches the area of interest and enters the AP’s coverage, it establishes a WLAN connection to download and process the data within look-ahead time window
The per-vehicle data rate () is:
=1s, AWGN channel with pathloss model [3]
 | Frequency | BW | TX power | SS |  | 
4Mb | 2.4GHz | 20MHz | 20dBm | 1 |  | 103.2Mbps @ 90m
 | Frequency | BW | TX power | SS |  | 
4Mb | 2.4GHz | 20MHz | 20dBm | 1 |  | 103.2Mbps @ 90m
From the pathloss model, the supported throughput at distance d () can be estimated [3, 4]
Jing Ma (Toyota)
Scenario:
Requirement:
Numerical example:

## Slide 7: Numerical example for regional HD MAP use case
Case 2: multiple vehicles downloading map data while approaching the area of interest
Vehicle density () should be considered.
 |  |  |  |  | Multi-lane |  | 
40km/h | 1.5s |  | 5m | 5m | 4 |  | 108~400 vehicles/km
 |  |  |  |  | Multi-lane |  | 
40km/h | 1.5s |  | 5m | 5m | 4 |  | 108~400 vehicles/km
(vehicles/km, linear) depends on inter-vehicle distance (), calculated using
The required per-vehicle data rate () may not be satisfied when vehicle density becomes high
AP
Area of interest
Look-ahead area
AP
Where : the reaction time; : deceleration; : length of the vehicle.
Jing Ma (Toyota)
Numerical example:

## Slide 8: Summary
More details related to regional HD MAP use case with WLAN are discussed:
  Data transmitted in local WLAN for the regional HD MAP can generally be supported
    Data size for map updates is assumed relatively small
    In high-density traffic scenarios, the require data rates per vehicle may be achievable but face challenges such as avoiding interference
Opportunities for improvement
  Enhancing MAC layer protocols to handle high-density scenario and prioritize critical updates
  Optimizing channel utilization for better performance
Jing Ma (Toyota)

## Slide 9
References
[1] 11-24/1526r1 Automotive WLAN use case study, Sep., 2024
[2] 5gaa-t-200111-tr-c-v2x-use-cases-and-service-level-requirements-vol-i-v3.0
[3] 11-24/1525r2 Use Case Study for Sustained Streaming Services in Moving Vehicles, Sep. 2024
[4] 11-14/0882r1 IEEE 802.11ax Channel Model Document, May, 2014