## Slide 1: ETSI TC BRAN updates, January 2025
Date: 2025-01-13
Authors:

## Slide 2: EN 301 893 version 2.2.1
Final national voting on EN 301 893 (Wireless Access Systems including Radio Local Area Networks, WAS/RLAN, operating in the license-exempt 5 GHz band) concluded
  No objections
  No comments
A major milestone!
  Work on this revision begun 2017
ETSI published version 2.2.1
  Offered to European Commission for citation in the Official Journal of the European Union (OJEU)
  Currently, average duration of Harmonised Standards (HSs) exceeds one year

## Slide 3: Draft EN 303 687
Work on next version of EN 303 687 (WAS/RLAN operating in the license-exempt 6 GHz band) continued
TC BRAN achieved consensus on Narrowband Frequency Hopping (NB FH) medium access rules
  See latest draft version 1.1.6 for details
  General concept approved; details (e. g., various durations) reman to be defined at future meetings

## Slide 4: EN 303 687, version 1.1.1
Updates to OJEU expected during first quarter in 2025
  TC BRAN hopes that the European Commission will list version 1.1.1 of EN 303 687 in the Official Journal of the European Union (OJEU)
  If listed, it is unlikely that version 1.1.1 of EN 303 687 would be listed without a note
  It is expected that a note will limit how this Harmonised Standard (HS) may be used to provide a presumption of conformity

## Slide 5: Review of Harmonised Standards older than five years
TC BRAN reviewed EN 300 652, EN 302 502, EN 303 316, EN 303 339, EN 301 811‑1‑1, EN 301 811‑1‑2, EN 301 811‑1‑3, EN 301 823‑1‑1, EN 301 823‑1‑2, EN 301 823‑1‑3, EN 301 823‑2‑1, EN 301 823‑2‑2, and EN 301 823‑2‑3
Standards relate to HiperLAN, HiperLAN/2, Direct Air-to-Ground communication, 5.8 GHz Broadband Fixed Wireless Access (BFWA)
TC BRAN needs to decide if these standards are still current or should be retired

## Slide 6: European Commission decision 2021/1067
On 2024-11-08, the Electronic Communications Committee (ECC) of the European Conference of Postal and Telecommunications Administrations (CEPT) amended decision DEC(20)01
  See updates related to Out-Of-Band Emissions (OOBE) below 5935 MHz for Very Low Power (VLP) devices
European Commission (EC) amended its decision 2021/1067
  See decision 2024/3157
  Decision to raise OOBE from −45 dBm/MHz to −37 dBm/MHz delayed until end of this year

## Slide 7: Upcoming meetings
BRAN#128
  2025-02-03 until 2025-02-05
BRAN#129
  2025-03-31 until 2025-04-03
BRAN#130
  2025-06-02 until 2025-06-06
BRAN#131
  2025-09-22 until 2025-09-26
BRAN#132
  2025-11-03 until 2025-11-07