## Slide 1: Co-Triggering Frame Design for CoBF
Date: 2025-xx-xx
Authors:
Name | Affiliation | Address | Phone | Email
Insik Jung | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insik0618.jung@lge.com
 |  |  |  | esung.park@lge.com
Eunsung Park |  |  |  | 
Dongguk Lim |  |  |  | 
 |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | 
 |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | 
 |  |  |  | js.choi@lge.com
Geonhwan Kim |  |  |  | 
 |  |  |  | geonhwan.kim@lge.com
Insun Jang |  |  |  | 
 |  |  |  | insun.jang@lge.com

## Slide 2: Introduction
For CoBF transmission, we don’t apply beamforming to the pre-UHR portion
  For this reason, the pre-UHR portion need to be commonly designed to avoid preamble collison
In this contribution, we propose a method to configure the common pre-UHR portion
  We firstly handle the method how sharing AP decides the commonly configured parameters
  We then point out that the sharing AP needs to deliver the derived pre-UHR portion to the shared AP using Co-Triggering frame
  We also propose how to configure the Co-Triggering frame

## Slide 3: Multi-AP Coordination Framework
Multi-AP framework has several benefits [1-2]
  Each AP can simply and dynamically select a better scheme depending on the situations
  It may be easy to deploy newly designed MAPC schemes in the future
In this contribution, we focus on the CoBF transmission method as a part of the MAPC procedure

## Slide 4: CoBF Transmission with Common Pre–UHR Portion
For CoBF Transmission, pre-UHR portion of the PHY preamble needs to be set as identical [3]
The commonly configured fields should be delivered to the shared AP in advance of the CoBF Transmission
  Shared AP then can configure the common preamble based on the delivery
  We are considering Co-Triggering frame as a container
Sharing AP
Shared AP
Co-Triggering Frame
UHR preamble 1+Data 1
Common preamble
UHR preamble 2+Data 2
Common preamble
UHR PPDUs for CoBF Transmission
Information to configure the common preamble
L-STF, L-LTF, L-SIG, RL-SIG, U-SIG, UHR-SIG

## Slide 5: On the Common Setting
Role of the sharing AP to set the common preamble
  Need to decide which parameters are required to be delivered to shared AP. We may need to exclude some parameters which are already obvious to the shared AP
  Need to decide the field value of the parameters
    It can just be determined by sharing AP or can be set via negotiation through ICF-ICR frames before the Co-Triggering frame
In the following slides, we will discuss the parameters which are needed to be delivered
  We will handle both whether to deliver and how to set

## Slide 6: Identical L-SIG / U-SIG Field (1/2)
Identical L-SIG Field
  Length field need to be commonly designed to avoid L-SIG preamble collison. We can implicitly get this value through the Duration field of the co-triggering frame
PHY Version Identifier
  We need this indication for the future extension of CoBF transmission
  Set to the lower version of PPDU for the common setting
PPDU BW
  PPDU BW should be set to a value that both APs are commonly available. We may simply inherit the BW of the PPDU transmitting the co-triggering frame
TXOP
  TXOP field may not be needed since shared AP can know the TXOP information through duration subfield of Co-Triggering frame
UL/DL, BSS color 1, BSS color 2
  These fields are obviously known to the shared AP in advance of the co-triggering frame
U-SIG1 | B0-B2 | B3-B5 | B6 | B7-B12 | B13-B19 | B20-B25
 | PHY version Identifier | PPDU BW | UL/DL | BSS color 1 | TXOP | BSS color 2
*We think that delivery of the colored fields are necessary
Notes: BSS color 1 – COBF sounding 절차의 COBF NDPA에 이미 전달되는 정보임

## Slide 7: Identical L-SIG / U-SIG Field (2/2)
PPDU Type, M-AP Flag
  These fields are obviously known to the shared AP in advance of the co-triggering frame
Punctured Channel Information
  We may need to apply an aggregated puncturing pattern of both APs. We may simply inherit the puncturing pattern of the PPDU containing the co-triggering frame
UHR-SIG MCS
  Considering RSSI, UHR-SIG MCS is set to be a value which is decodable for the target STAs from both APs
Number of UHR-SIG Symbols
  UHR-SIG field includes user fields of all of the target users from both APs. Thus, the number of UHR-SIG symbols need to be set as a value to cover all of the user fields from both APs.
U-SIG2 | B0-B1 | B2 | B3-B7 | B8 | B9-B10 | B11-B15 | B16-B19 | B20-B25
 | PPDU Type | M-AP Flag | Punctured Channel Information | Validate | UHR-SIG MCS | Number of UHR-SIG Symbols | CRC | Tail
Notes: PPDU Type / M-AP Flag  CoBF에선 자명한 세팅이므로 전달 필요 없음

## Slide 8: Identical UHR-SIG Common Field
GI+LTF Size & Number of UHR-LTF Symbols
  GI+LTF needs to be set as a value to guarantee reliable CE performance for all STAs
  # of UHR-LTF symbols needs to be set based on the giant P matrix
  Thanks to this common design, we can strictly synchronize those two PPDUs to avoid residual interference
Number of non-OFDMA Users
  # of non-OFDMA users should be set as the total number of users across the both APs.
Spatial Reuse & LDPC Extra & Pre-FEC padding & PE disambiguity
  Those four parameters need to be commonly configured to avoid preamble collison
B0-B3 | B4-B5 | B6-B8 | B9 | B10-B11 | B12 | B13-B15 | B16-B18
Spatial Reuse | GI+LTF Size | Number of UHR-LTF Symbols | LDPC Extra Symbol Segment | Pre-FEC padding Factor | PE Disambiguity | Disregard | Number of non-OFDMA Users
<Non-OFDMA common field>

## Slide 9: Identical UHR-SIG User Field
Shared AP need to know all of the user field information of the target stations from both APs.
So, multiple sets of the per-user parameters listed below need to be delivered to the shared AP to configure the common UHR-SIG field
  STA-ID
  MCS
  Spatial Configuration
    Since this information is basically not a per-user information. So, we can consider this as a common information.
  BSS Color Indication
  2xLDPC
B0-B10 | B11-B15 | B16-B19 | B20 | B21 | B22
STA-ID | MCS | Spatial Configuration | Reserved | BSS Color Indication | 2xLDPC
<MU-MIMO user field>

## Slide 10: Types of the Parameters to be Delivered
Common PHY parameters
  Identical U-SIG
    PHY version identifier, UHR-SIG MCS, Number of UHR-SIG Symbols
  Common field of the Identical UHR-SIG
    Spatial reuse, GI+LTF size, Number of UHR-LTF symbols, LDPC Extra Symbol Segment, Pre-FEC padding, PE disambiguity, Number of Non-OFDMA users
  spatial configuration
Per-user PHY parameters
  User field of the Identical UHR-SIG
    STA-ID, MCS, BSS color indication, 2xLDPC

## Slide 11: Co-Triggering Frame
Common PHY parameters
  Common PHY parameters would be natural to be delivered in common info field of the co-triggering frame
Per-user PHY parameters
  Per-user parameters would better to be delivered in the user info field of the co-triggering frame
    Since the aggregated data size of the per-user parameters varies according to the number of users, it may not proper to be included in the common field
Common Info field
User Info Field 1
User Info Field 2
…

## Slide 12: Possible Containers
We may consider some candidate trigger frame formats for the co-triggering frame
  MU-RTS TXS Trigger Frame
  BSRP Trigger Frame
  …
We prefer the MU-RTS TXS Trigger Frame
  MU-RTS TXS Trigger Frame is already adopted as a co-triggering frame for coordinated TDMA (Co-TDMA)
  To better use of multi-AP common framework, it is natural for Co-BF to consider MU-RTS TXS Trigger frame as a co-triggering frame

## Slide 13: Container: MU-RTS TXS Trigger (1/4)
CoBF MU-RTS trigger frame parsing
  Multi-AP parsing
    TXOP sharing mode = 3
      If the value is 3, we can parse that the trigger frame is for multi-AP transmission
TXS mode subfield | Description
0 | MU-RTS that does not initiate TXS procedure
1 | MU-RTS that initiates TXS procedure wherein a scheduled STA can only transmit MPDU(s) addressed to its associated AP
2 | MU-RTS that initiates TXS procedure whrein a scheduled STA can transmit MPDU(s) addressed to its associated AP or addressed to another STA
3 | MU-RTS for multi-AP transmission

## Slide 14: Container: MU-RTS TXS Trigger (2/4)
  CoBF parsing
    Multi-AP coordination type
      Newly introduced field to identify the Multi-AP transmission scheme
      If the value is 2, we can parse that the trigger frame is for CoBF
subfield | Description
0 | Co-TDMA
1 | CoSR
2 | CoBF
3 | …

## Slide 15: Container: MU-RTS TXS Trigger (3/4)
Common Field Example
  If the MU-RTS TXS is parsed as CoBF, we can redesign the common field of the trigger frame
    Order of the subfields need to be discussed in the future
    Number of the bits of each field needs to be discussed in the future
    We may need a special user info field to signal the overflowed parameters
  If we do not want to redesign the common info field, Multi-AP coordination type and common PHY parameters may need to be delivered in special user info field(s).
Trigger Type
More TF
CS Required
TXS Mode
Common PHY Parameters
Multi-AP Coordination Type
…

## Slide 16: Container: MU-RTS TXS Trigger (4/4)
CoBF User Field Example
  If MU-RTS TXS trigger frame is parsed as CoBF, we can define a new user field named CoBF user field
    AID 12 field indicates the shared AP’s ID
  Or, we can redesign the UHR variant user info field when the frame is parsed as CoBF
Another option
  We may not even need AID12 field since the RA would be set to shared AP’s address and then shared AP’s ID is obvious and legacy stations will not read this trigger frame.
AID 12
STA-ID
MCS
BSS Color Indication
2xLDPC
B0
B11
B12
B22
Reserved
B23
B27
B28
B29
B30
B39

## Slide 17: Thoughts on ICF/ICR for CoBF
For the common SIG field, some parameters would better to be negotiated through ICF/ICR in advance of transmitting the co-triggering frame for the sharing AP to decide the common parameters
  Available bandwidth
  Punctured channel information (might be a dynamic punc. info.)
  GI+LTF size
  Number of UHR-LTF symbols
  Serving STAs information (number of STAs, STA-IDs)
  Etc..

## Slide 18: Conclusion
We have proposed a method to configure the common pre-UHR portion for CoBF Transmission
We propose to use co-triggering frame as a container to deliver the derived common parameters to the shared AP
  Especially, we proposed MU-RTS TXS trigger frame

## Slide 19: References
[1] 11-19-0842-00, Multi-AP set configuration for C-TDMA
[2] 11-24-1220-00, A Framework for Coordinated Access Points
[3] 11-24-1822-04, COBF Design for UHR

## Slide 20: Straw Poll #1
Do you agree to include following to the 11bn SFD?
  As part of the CoBF procedure, to trigger CoBF PPDUs, a sharing AP shall send a co-triggering frame to a shared AP
    Exact container (e.g, MU-RTS TXS, BSRP …) is TBD
    The name “co-triggering frame” is TBD
Y/N/A: //

## Slide 21: Straw Poll #2
Do you agree to include following to the 11bn SFD?
  The information for some parts of the commonly configured SIG fields (e.g., L-SIG, U-SIG, UHR-SIG) of the following COBF PPDU needs to be delivered from a sharing AP to the shared AP through the co-triggering frame
    NOTE
      Which parts are to be carried in the trigger frame is TBD
      The name “Co-triggering frame” is TBD
Y/N/A: //

## Slide 22: Straw Poll #3
Do you agree to include following to the 11bn SFD?
  Co-Triggering frame includes the following fields to commonly configure the U-SIG fields among two APs
    PHY version identifier, UHR-SIG MCS, Number of UHR-SIG Symbols
Y/N/A: //

## Slide 23: Straw Poll #4
Do you agree to include following to the 11bn SFD?
  Co-Triggering frame includes the following fields to commonly configure the common field of the UHR-SIG fields among two APs
    Spatial reuse, GI+LTF size, Number of UHR-LTF symbols, LDPC Extra Symbol Segment, Pre-FEC padding, PE disambiguity, Number of Non-OFDMA users
Y/N/A: //

## Slide 24: Straw Poll #5
Do you agree to include following to the 11bn SFD?
  Co-Triggering frame includes the following fields to commonly configure the user fields of the UHR-SIG fields among two APs
    STA-ID, MCS, BSS color indication, spatial configuration, 2xLDPC
    Co-Triggering frame includes all of the user fields for the common UHR-SIG
Y/N/A: //

## Slide 25: Straw Poll #6
Do you agree to include following to the 11bn SFD?
  Co-Triggering frame includes length field to configure the common L-SIG field
Y/N/A: //

## Slide 26: Straw Poll #7
Do you agree to include following to the 11bn SFD?
  Co-Triggering frame includes the TXOP field to configure the common U-SIG field
Y/N/A: //

## Slide 27: Straw Poll #8
Do you agree to include following to the 11bn SFD?
  Co-Triggering frame includes the PPDU BW field to configure the common U-SIG field
Y/N/A: //

## Slide 28: Straw Poll #9
Do you agree to include following to the 11bn SFD?
  Co-Triggering frame includes the Punctured Channel Information field to configure the common U-SIG field
Y/N/A: //

## Slide 29: Straw Poll #10
Do you agree to include following to the 11bn SFD?
  As part of the CoBF procedure, to trigger CoBF PPDUs, a sharing AP shall send a MU-RTS TXS trigger frame to a shared AP
    The name “co-triggering frame” is TBD
Y/N/A: //