## Slide 1: Frame Format Discussion
Date: 2025-01-10
Authors:

## Slide 2: Recap: 802.11 Frame Format
The different versions of frame formats are defined in 802.11: PV0, PV1, WUR.
The frame of PV0 has the following format:
0 or 6
Control frame format
Data frame format
Management frame format
The frame of PV1 has the following format:
The frame of WUR has the following format:

## Slide 3: Purpose of Frame Format
The MAC header includes the information about the various frame format.
The identifier of peer device and the transmitter at frame header are needed for
  the acknowledgement of the soliciting frame.
  The handshake of the request management frame and response management frame in the different TXOP.
  The information of the STAs being maintained at associated AP.
  The information of the AP being maintained at associated STA.
The FCS at the end of the frame verifies whether the MAC header and frame body of the received frame has error or not.

## Slide 4: Use Cases of 11bp
Use cases of mono-static backscatter (close-range backscatter) and bistatic backscatter (long-range backscatter).
  RFID message is carried in 11bp where the RFID defines the format of the message.
    The interpretation of the RFID message is up to RFID protocol.
  AMP tag (11bp tag) is read by the AMP reader.
    No power save mode for AMP tag.
    No state/management information maintained in AMP reader of AMP tag except RFID message of the read AMP tag.
Use Cases per wakeup radio.
  The power save mode etc, is maintained in the associated AP.
  The wakeup signal is addressed to the STA with STA’s identifier being carried.
    The frame header carries the identifier of the STA being addressed, e.g, the frame format similar to WUR frame is used here.

## Slide 5: Use Cases of 11bp
active UL AMP communication
  option 1:
    No association is applied to AMP STA.
    One frame exchange sequence transaction includes polling stage and UL frame exchange stage.
      Each stage starts with the polling ( announcing the slot(s)) for AMP STA to transmit its frame transmission request in preparing stage or actual UL AMP information in information transmission stage.
      The two types of polling frames are defined.
    UL AMP up layer information is carried in 11bp frame.
    The AMP AP polls an AMP STA’s UL frame in information transmission stage by using STA’s slot ID of the preparing stage.
  option 2:
    Light beacon is transmitted by AMP AP.
    Association is established for AMP STA.
    UL AMP up layer information is carried in 11bp frame.
    The AMP AP polls an AMP STA’s UL frame by allocating a slot to the STA with or without preparing stage.
      Different AMP STAs can be serviced in different SPs where the AP can poll the STAs in their SPs without preparing stage.

## Slide 6: Frame Format Indication
Frame format 1 for AMP tag:
  FC (frame control) field + frame body + FCS field where the frame body carries RFID message defined by RFID.
Frame format 2 for UL active AMP communication:
  FC (frame control) field + Tx ID + frame body + FCS field where the frame body carries the light beacon.
  FC (frame control) field + Tx/Rx ID ? + frame body + FCS field where the frame body carries UL AMP up layer information.
  FC (frame control) field + Tx ID + frame body + FCS field where the frame body carries the polling information.
  FC (frame control) field + Tx/Rx ID ? + frame body + FCS field where the frame body carries the request.
Frame format 3 for wake up application: similar to WUR frame format.

## Slide 7: Summary
The various frame formats of 11bp are discussed:
  The frame formats are different for the different use cases.
  For some uses cases, the frame format includes frame control (FC) field, frame body and FCS.
  For some use cases, the frame format is similar to WUR frame format.