## Slide 1: On the Maximum number of spatial streams support in Coordinated spatial reuse
Date: 2025-01-08
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek |  |  | jianhan.liu@mediatek.com
You-Wei Chen |  |  |  | 
Shengquan Hu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: On the Number of SS Support for Co-BF
Passed Motions on the maximum number of spatial streams support for Co-BF
  The Coordinated beamforming (Co-BF) transmission phase in 802.11bn shall be limited to 2 APs. [Motion #99, [1] and 179]
  In a Co-BF transmission, the maximum number of spatial streams given to one user will be 2. [Motion #114, [1] and 184]
Based on the above passed motions, the total maximum number spatial streams support for Co-BF is 4.

## Slide 3: On the Number of SS Support for Co-SR
To reduce the complexity on signaling, implementation and testing, it is desirable to also restrict the number of APs to 2 in a Co-SR transmission.
  By making Co-SR and Co-BF the same restriction on number of APs , a lot of protocols can be used for both Co-SR and Co-BF.
Since each AP is not required to suppress the interferences in Co-SR, we propose that each AP can transmit the maximal 4 spatial streams in a Co-SR transmission.
  Most APs are equipped with 4 transmit antennas. Most non-AP STAs are equipped with no great than 4 antennas.
  Restricting the maximum number of spatial streams transmitted by each AP in Co-SR to 4 seems a good tradeoff between potential throughput enhancement and necessarily complexity.

## Slide 4: References
  1) 11-24-0171r20: 11-24-0171-20-00bn-tgbn-motions-list-part-1, Alfred Asterjadhi (Qualcomm Inc.)
  179) 11-24/1542r5: 11-24-1542-05-00bn-sounding-schemes-for-coordinated-beamforming, Sameer Vermani (Qualcomm)
  184) 11-24/1822r3: 11-24-1822-03-00bn-cobf-design-for-uhr, Sameer Vermani (Qualcomm)