## Slide 1: AMP Device Management
Date: 2025-01-10
Authors:

## Slide 2: Recap: AMP Use Cases
Mono-static backscatter (close-range backscatter)
Bistatic backscatter (long-range backscatter)
Active UL AMP communication
  The AMP device can transmit UL AMP frame solicited by DL frame.
Wake up AMP radio
  The device includes wWiFi radio from DL and UL 802.11 frame exchanges.

## Slide 3: Recap: 802.11 baseline Device Management
BSS
  AP establishes BSS, transmits Beacons.
  non-AP STAs associated with the AP.
  MAC address is used to identify an AP or a non-AP STA.
IBSS
  Each STA in IBSS transmits its Beacon.
  Frame exchange without association.
  MAC address is used to identify the peer STA.
MBSS
  Mesh peer establishment.
  Each mesh STA transmits its Beacon.
  MAC address is used to identify an AP or a non-AP STA.
OCB
  No Beacon.
  Each STA does frame exchanges with its neighbor STAs where the peer device identification may be done by the up layer.
  MAC address is used to identify the peer STA.

## Slide 4: Association vs no Association
For mono-static backscatter (close-range backscatter) use case and bistatic backscatter (long-range backscatter) use case, the association is not needed.
  No beacon is transmitted in AMP link.
  An AMP Tag has no MAC layer identifier to identify itself.
active UL AMP communication use case Option 1:
  the association is needed.
    Light Beacon is transmitted in AMP link.
    For active UL AMP communication use case, the AMP client device is managed by AMP AP (associated with the AMP AP) through the AMP link.
      An AP allocates the AMP client device’s identifier during the association procedure.
    The other management frames are needed.
    The power save can be provided.
active UL AMP communication use case Option 2:
  An AMP client has an identifier defined by the up layer.
For wakeup use case, the association is needed.
  For wakeup use case, the AMP link for wakeup of AMP device is managed through the WiFi link.
  No beacon is transmitted in AMP link.

## Slide 5: MAC Security vs no MAC Security
For mono-static backscatter (close-range backscatter) use case and bistatic backscatter (long-range backscatter) use case, the MAC layer security is not needed.
  The RFID layer security is used.
active UL AMP communication use case Option 1:
  the MAC layer security is needed.
For wakeup use case, the MAC layer security is needed.

## Slide 6: Light Beacon Design
A Light Beacon is defined where the Beacon carries the following information in its Frame body:
  TSF time,
  Beacon Interval,
  AP’s capabilities (PHY Capabilities, Security Capabilities, MAC Capabilities),
  Other fields TBD, e.g. broadcast SPs when the frame will be exchanged with AMP client devices.
The light Beacon has frame header that carries:
  FC
    Frame Type to indicate Complete Type,
    Sub Frame Type to indicate Beacon subtype,
  Tx ID to identify the AP (Beacon’s ID extended BSS color, e.g. 12-bit field,).
The light Beacon has FCS at the end of the frame.

## Slide 7: STA Association and STA’s AID Allocation: Association Procedure
The AP announces random slots for unassociated STAs without unassociated AID to contend.
An unassociated STA selects one unassociated AID (e.g. 2046 to 4095) and randomly selects a slot to transmit its Light Association Request with the following information:
  Unassociated AID,
The AP allocates the slot to each unassociated STA to transmit Light Association Request if the following are true
  There is no another unassociated STA selects the same slot to transmit Unassociated AID.
  the STA’s selected unassociated AID is not used by another unassociated STA that are doing the association.
After receiving the Light association Request correctly, the AP transmit Light Association Response to indicate whether the request is accepted.
  If the request is accepted, the new AID (e.g. 1 to 2007) is allocated to the STA.
  The STA releases its unassociated AID.