## Slide 1: STA Polling Procedure----AMP Information Exchange
Date: 2025-01-10
Authors:

## Slide 2: Recap: AMP Use Cases
Mono-static backscatter (close-range backscatter)
  When the information exchange can’t be finished in one TXOP, the state of the previous TXOP can’t be kept.
  No association exist.
Bistatic backscatter (long-range backscatter)
  When the information exchange can’t be finished in one TXOP, the state of the previous TXOP can’t be kept.
  No association exist.
Active UL AMP communication
  The AMP device can transmit UL AMP frame solicited by DL frame.
  When the information exchange can’t be finished in one TXOP, the state of the previous TXOP can be kept.
  association can be established by the client.
Wake up AMP radio
  The device includes WiFi radio from DL and UL 802.11 frame exchanges.
  The WUR protocol can be used here.

## Slide 3: Information Exchange 1 without Association (1)
Query Stage:
  The AP or AMP reader announces the slot(s) for client device (unassociated STA or AMP tagger) to contend by using the trigger frame.
  Each client device, after receiving the announcement, randomly selects a slot to transmit a random number.
    The random number identifies the client temporally and avoid the collision of CRC code.
Information polling stage:
  The AP or AMP reader allocates the slots to a client for it to transmit/receive its information by using the trigger frame if there is no another client that selects the same slot to transmit its random number in query stage.
  The first slot is identified by the client’s random number in the query stage to identify the client.
    Another variant is that the client’s slot ID in query stage is used as the client’s identification.
    the client transmits its CRC code in the first slot allocated to it in the information polling stage.
    After the slot, the AP or AMP reader transmits Ack or Nak to indicate whether it correctly receives the CRC code.

## Slide 4: Information Exchange 1 without Association (2)
Information polling stage: (Cont’d)
  Then, the AP or AMP reader allocates the following slot(s) to the client for the information exchange by using the client’s CRC code by using the trigger frame.
    The trigger frame announces the slot, client CRC code, whether the slot is used for requesting the UL information or for writing the DL information.
    The client transmits its information or receive the information in the slot.
    If the client transmits the information in the slot, the AP or AMP reader transmits Ack or Nak to indicate whether it correctly receives the information after the slot.
    If the client receives the information in the slot, the client transmits Ack or Nak to indicate whether it correctly receives the information after the slot.

## Slide 5: Information Exchange 2 for Using CRC Code in Query Stage or with Association (1)
Query Stage:
  The AP announces the slot(s) for client device (AMP tag or associated STA) to contend by using the trigger frame.
  Each client device, after receiving the announcement, randomly selects a slot to transmit its CRC code (AID).
Information polling stage:
  The AP allocates the slot(s) to a client for the client to transmit its information or for the client to receive the DL information if the following are true
    There is no another client that selects the same slot to transmit its CRC code (AID).
    The CRC code (AID) received in query stage is used to identify the client for transmitting the UL information or for receiving the DL information.

## Slide 6: Information Exchange 2 for Using CRC Code in Query Stage or with Association (2)
Information polling stage: (Cont’d)
  The client whose CRC code (AID) matches the CRC code (AID) of the announced slot uses the slot to transmit the whole (or port) UL information or receive the whole (or port) DL information in the slot.
    If the client transmits the information in the slot, the AP or AMP reader transmits Ack or Nak to indicate whether it correctly receives the information after the slot.
      The Ack/Nak resolves the collision when multiple clients with the same CRC code responds in the same slot of query stage.
    If the client receives the information in the slot, the client transmits Ack or Nak to indicate whether it correctly receives the information after the slot.

## Slide 7: Criteria to Select Slot in Query Stage
Method 1:
  In Query Stage, each trigger frame transmitted by the AP or AMP reader announce one slot:
    The probability to for a client to access the slot is also announced by the frame.
Method 2:
  In Query Stage, each trigger frame transmitted by the AP or AMP reader announce more than one slot:
    The probability to for a client to access each slot is also announced by the frame
    The sync signal exists before each slot other than the first slot.

## Slide 8: Long Information Transmission
Observation:
  One slot may be able to provide enough resource for client to transmit/receive all its information.
Method 1: AMP reader’s/AP’s control of information fragmentation
  When announcing the slot for a client in information polling stage, the AP or AMP reader announces the starting point, the length of the information being solicited from the client, whether the slot is the last slot.
Method 2: client’s control of information fragmentation
  When receiving the slot allocated to it in information polling stage, the client transmits a fragment of its information if the slot is not enough to transmit all the information.
      The fragment indicates whether it is the last fragment of the information.
Method 1 is supported by at least AMP tag.

## Slide 9: Multiple Readers under Multiple Clients with same CRC Code (1)
Observation:
  When one AMP reader is reading the information from an AMP tag with CRC code value CODE through multiple TXOPs, another AMP reader may start to read the information from another AMP tag with the CRC code value CODE.
  The two AMP tags may transmit its fragment respectively when any one of the two AMP reader polls the information by using the CRC code.
Method under random number being not used:
  Each client has a flag being set to 0.
  When 1) a first slot identified by a CRC code value equal to a client’s CRC code is detected, 2) the client transmits its CRC code value in the query stage, and 3) the client has the value 0 of the flag, the client set the flag to 1 and transmits its information in the slot.
  When 1) a first slot identified by a CRC code value equal to a client’s CRC code is detected, 2) the client doesn’t transmit its CRC code value in the query stage, and 3) the client has the value 1 of the flag, the client set the flag to 0 and doesn’t transmit its information in the slot.
  When 1) a slot other than the first slot identified by a CRC code value equal to a client’s CRC code is detected, 2) the client has the value 1 of the flag, the client transmits its information in the slot.

## Slide 10: Multiple Readers under Multiple Clients with same CRC Code (2)
Method under random number being used:
  Each client has a flag being set to 0.
  When 1) a first slot identified by a CRC code value equal to a client’s CRC code is detected, 2) the client transmits its CRC code value in the previous slot, and 3) the client has the value 0 of the flag, the client set the flag to 1 and transmits its information in the slot.
  When 1) a first slot identified by a CRC code value equal to a client’s CRC code is detected, 2) the client doesn’t transmit its CRC code value in the previous slot, and 3) the client has the value 1 of the flag, the client set the flag to 0 and doesn’t transmit its information in the slot.
  When 1) a slot other than the first slot identified by a CRC code value equal to a client’s CRC code is detected, 2) the client has the value 1 of the flag, the client transmits its information in the slot.