## Slide 1: Co-SR Preamble Signaling
Date: 2025-01-08
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Genadiy Tsodik |  |  |  | 
Jason Yuchen Guo |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 

## Slide 2: Background
The following motion has passed regarding co-SR:
  TGbn defines a multi-AP Coordinated Spatial Reuse (Co-SR) at TXOP-level with power control.
    Other multi-AP coordination modes are TBD.
  [Motion #29, [1] and [49-65]]
There are proposals to have the same U-SIG fields, UHR-SIG fields for co-BF [1,2].
There is also proposal to have the same U-SIG field for SU co-SR transmission [1,2].
In this proposal, we discuss our thinking on co-SR preamble signaling.

## Slide 3: Two modes of co-SR preamble signaling
We provide the following two modes for co-SR preamble transmission.
  Mode 1: Trigger + same L-SIG contents, could be different U-SIG contents.
    For UHR + EHT, EHT+UHR or EHT+EHT co-SR transmissions.
  Mode 2: Trigger + same U-SIG contents [1][2]
    For UHR + UHR transmissions.
We will talk about the two modes and analyze the pros and cons of each mode.

## Slide 4: Mode 1 of co-SR preamble signaling
Mode 1: Trigger + same L-SIG contents, could be different U-SIG contents.
  Enable UHR+ EHT, EHT+UHR or EHT+EHT co-SR transmissions, provided no changes to non-UHR EHT non-AP STAs are needed.
  Provide good protection through ICF, ICR and co-SR trigger frame. Also provide further PPDU level protection through L-SIG length.
  Easy implementation for each AP to set the SIG contents for SIG fields after L-SIG.
  PPDUs end at the same time to enable easy ACK feedback.
  UHR PPDU for co-SR transmission will be used, carry signaling needed for co-SR transmission (e.g., co-SR indication) when UHR transmission exists.

## Slide 5: Mode 2 of co-SR preamble signaling
Mode 2: Trigger + same L-SIG contents, same U-SIG contents.
  Provide good TXOP level protection through L-SIG length and BSS color, TXOP info in U-SIG field.
  Enable UHR+UHR co-SR transmissions.
  UHR PPDU for co-SR transmission will be used, carry signaling needed for co-SR transmission (e.g., co-SR indication).
  PPDUs end at the same time to enable easy ACK feedback.
  For UHR-SIG field, propose to have not the same contents for easy implementation, each AP indicates its own signaling.

## Slide 6: Summary
In this contribution, we propose two modes of co-SR preamble signaling.
  Mode 1: Trigger + same L-SIG contents, could be different U-SIG contents.
    For UHR + EHT, EHT+UHR or EHT+EHT co-SR transmissions.
  Mode 2: Trigger + same U-SIG contents [1][2]
    For UHR + UHR transmissions.
We propose to enable both modes in 802.11bn for different use cases and motivations.

## Slide 7: Straw Poll #1
Do you support the following modes for co-SR transmission in 802.11bn?
  Mode 1: trigger + same L-SIG contents, could be different U-SIG contents.
    For UHR+EHT, or EHT+UHR or EHT+EHT co-SR transmission.
    Provided no changes to non-UHR EHT non-AP STAs are needed.
  Mode 2: Tigger + same L-SIG contents + same U-SIG contents
    For UHR+UHR co-SR transmission.
  For all modes, the two PPDUs will start and end at the same time.
  UHR PPDU for co-SR transmission will be used for either mode 1 or mode 2 when UHR transmission exists.
    There exists an indication in U-SIG field to indicate the UHR PPDU is a UHR PPDU for co-SR transmission.

## Slide 8
https://mentor.ieee.org/802.11/dcn/24/11-24-1834-03-00bn-11bn-non-elr-signaling-design-for-new-features.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1864-01-00bn-map-ppdu-consideration-and-harmonized-u-sig-signaling.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1205-02-00bn-analysis-and-simulations-on-coordinated-spatial-reuse.pptx
https://mentor.ieee.org/802.11/dcn/24/11-24-1389-00-00bn-coordinated-spatial-reuse-design-details.pptx
References