## Slide 1: UHR Receive Procedure
Date: 2025-01-xx
Authors:
Name | Affiliations | Address | Phone | email
Lin Yang | Qualcomm |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Alice Chen |  |  |  | 

## Slide 2: Overview of Main Changes from EHT Receive Processing
When to check ELR-MARK, if ELR capable?
  SIG is invalid including CRC fails in legacy preamble portion up to U-SIG
  Recommend parallel processing of 11a and ELR-MARK check or 11ax ER SU and ELR-MARK check
ELR preamble parsing after
  ELR-MARK is detected, or
  U-SIG indicates ELR PPDU and 3 ELR validate bits are “111” or value of 7 plus matching STA-ID
How to do deferral?
  If length from ELR-SIG is valid at Rx, defer based on ELR-length
  Otherwise, defer based on legacy modes’ processing rules
Recommend to remove the support of forward-looking ER SU preamble (defined in EHT) starting from UHR
  UHR introduces ELR feature which is better replacement
  Can significantly simplify the receive state machine
    QBPSK check on the 2nd U-SIG symbol before decoding U-SIG

## Slide 3: If SIG is Invalid in Legacy Preamble Portion up to U-SIG
Case 1: Invalid SIGNAL
Case 2: detected as 11n but HT-SIG is invalid
Case 3: detected as 11ac but VHT-SIG is invalid
Case 4: detected as 11ax SU/MU or TB but HE-SIG is invalid
Case 5: detected as EHT and above but U-SIG is invalid
  Forward-looking ER SU preamble check defined in EHT is removed (QBPSK check on the 2nd U-SIG symbol)

## Slide 4: Recommended Parallel Processing of Legacy Mode and ELR-Mark Detection
Case 1 : detected as 11a due to valid SIGNAL and no RL-SIG and no QBPSK detected
  L-SIG parity check has high false positive probability at low SNR
  Need to parallelly check ELR-MARK while processing 11a data
Case 2 : detected as 11ax ER SU due to HE-SIG-A2 being QBPSK
  Need to parallel processing of HE-SIG decoding and ELR-MARK check
    HE-SIG-A3 and HE-SIG-A4 are at the same symbol location as ELR-MARK

## Slide 5: U-SIG Processing

## Slide 6: ELR-MARK and ELR Preamble Processing
Deferral rules:
If length from ELR-SIG is valid at Rx, defer based on ELR-length
Otherwise, defer based on legacy modes’ processing rules

## Slide 7: SP1
Do you agree to include the following into the 11bn SFD?
  Remove the requirement, for UHR STAs, to receive the forward-looking EHT ER SU preamble in the UHR RX procedure

## Slide 8: SP2
Do you agree to include the following into the 11bn SFD?
  UHR receive procedure is illustrated by the attached PHY receive state machine diagram and the text document of UHR receive procedure

## Slide 9
Appendix

## Slide 10: ELR and Legacy Preamble Formats
L-SIG
Data
11a
LEN%3 = 0
L-LTF
L-STF
HT-STF
HT-SIG1
HT-SIG2
Data
HT-LTF1
HT-STF
L-SIG
HT-STF
HT-SIG1
Data
L-LTF
L-STF
HT-SIG2
HT-LTFs
L-SIG
VHT-STF
VHT-SIG-A1
L-LTF
L-STF
VHT-SIG-A2
L-SIG
HE-STF
RL-SIG
HE-SIG-A1
HE-SIG-A2
Data
L-LTF
L-STF
LEN%3 = 0
LEN%3 = 1
HE-LTFs
L-SIG
HE-STF
RL-SIG
HE-SIG-A1
HE-SIG-A2
Data
L-LTF
L-STF
LEN%3 = 2
HE-LTFs
HE-SIG-Bs
L-SIG
HE-STF
RL-SIG
HE-SIG-A1
HE-SIG-A2
Data
L-LTF
L-STF
LEN%3 = 2
HE-LTFs
HE-SIG-A3
HE-SIG-A4
L-SIG
Mark1
Mark2
OOK
L-LTF
L-STF
LEN%3 = 0
-1*L-SIG
-1*L-SIG
L-SIG
EHT-SIGs
RL-SIG
U-SIG1
U-SIG2
Data
L-LTF
L-STF
LEN%3 = 0
EHT-LTFs
EHT-STF
PHY version = X1 EHT PPDU Type = Y1
11n - HT GF
11n - HT MF
11ac - VHT
11ax - HE SU/TB
11ax - HE MU
11ax - HE ER SU
11ba - WUR
11be - EHT MU
L-SIG
RL-SIG
U-SIG1
U-SIG2
Data
L-LTF
L-STF
LEN%3 = 0
EHT-LTFs
EHT-STF
PHY version = X1 EHT PPDU Type = Y2
11be - EHT TB
Data
L-SIG
RL-SIG
U-SIG1
U-SIG2
L-LTF
L-STF
LEN%3 = 0
PHY version = TBD2
Post-11be
BPSK modulated
QBPSK modulated
Variable modulation
PE
PE
PE
PE
PE
VHT-LTFs
HT-LTFs
L-SIG
RL-SIG
U-SIG1
L-LTF
L-STF
LEN%3 = 0
PHY version = TBD1
ER SU
U-SIG2
U-SIG3
U
L-SIG
RL-SIG
L-LTF 3~6dB+
L-STF 3~6dB+
ELR-Mark2
ELR-Mark1
ELR PPDU
U-SIG1
U-SIG2
PHY version = 1
ELR-SIG
ELR-LTFs
ELR-STF
Data
PE