## Slide 1
Consideration on fairness issue for MAP
Name | Affiliations | Address | Phone | Email
Yan Li | ZTE |  |  | li.yan16@zte.com.cn
Jay Yang |  |  |  | 
Li Quan |  |  |  | 
Zisheng Wang |  |  |  | 
Yurong Qian |  |  |  | 
Date: 2025-01-05
Authors:

## Slide 2
Introduction
Fairness issue has been discussed under some topics(e.g., C-TDMA[1], NPCA[2])
In this contribution, we would like to share our thoughts on the following:
  different types of fairness issue
  which fairness issue should be addressed via standardization
  which fairness issue should be left for implementation

## Slide 3
Recap of channel access
  For a single BSS, channel access scheme has been enhanced for the last few generations
    Before 11ax, normal STA can access channel only via EDCA
    During 11ax, non-AP STA can access additionally via trigger-based UL OFDMA for MU transmission
    After 11ax(i.e., 11be), non-AP STA can access via triggered TXOP sharing(TXS) for SU transmission or P2P
    Especially, MU EDCA has been defined to limit the channel access capacity(i.e., EDCA) of non-AP STA if the corresponding transmission has completed via UL OFDMA/TXS

## Slide 4
Different types of fairness issue
  From the perspective of resource, the fairness issue may be considered on:
    Time resource: new generation STA may obtain a longer TXOP
    Frequency resource: new generation STA may transmit with a wider bandwidth
    Spatial resource: new generation STA may improve the performance via MIMO/SR
  From the perspective of objectives, the fairness issue may be regarded as:
    Delay: legacy STA may experience worse delay when new generation STA exists
    Throughput : the throughput may degrade when new generation STA exisits
    Access frequency: the legacy STA may obtain TXOP less times than the new generation STA for a period of time(including EDCA and trigger-based access)
  From the perspective of scale, we may focus on fairness issue between:
    New (generation) STA and legacy STA
    New STA and new STA
    New group(i.e., MAP) and legacy STA
    New group and new group
    ...

## Slide 5
What we have done for fairness
  (Standardized)MU EDCA has been used for limiting channel access capacity of non-AP STA in some trigger-based transmission(e.g., UL OFDMA, TXS)
    In a single BSS, a non-AP STA(TXOP responder) may complete additional data transmission via trigger of AP(TXOP holder), which is unfair for the legacy STA or untriggered STA. Therefore, it’s a good way to mitigate fairness issue by using MU EDCA to decrease the channel access capacity of the non-AP STA via EDCA
    Generally speaking, fairness isssue of channel access has been addressed in our standard
  (Implemented)We may have more consideration of fairness on product/implementation
    For UL OFDMA, AP should balance the resource allocation for different STAs:
      How often to trigger a STA
      How big a RU allocated
      How long for a trigger-based transmission
    For TXS, one or more factors above should also be taken into account
    However, all above are not standardized, which provides freedom for device design

## Slide 6
What we could do for MAP
  In 11bn, we make more effort on the coordination between APs. Therefore, the fairness issue has extended to to the MAP from a single BSS.
Perspective |  | Single BSS | MAP | Description about fairness
Objectives | Delay | / | / | New generation STA always has better performance than legacy one
 | Throughput | / | / | 
 | Access frequency (channel access times) | MU EDCA | TBD | Besides EDCA, shared AP has additional channel access capacity via trigger of sharing AP

## Slide 7: Summary
In this contribution, we make some discussion on the following :
  analyze different types of fairness issue
  review the fairness issue of channel access
  compare the potential fairness issue of single BSS and MAP

## Slide 8: Straw Poll
Do you support to consider fairness issue of channel access in MAP?
  Exact mechanism is TBD.

## Slide 9: Reference
[1] 11-24-0093-03-00bn-nav-setting-for-coordinated-tdma
[2] 11-24-1688-00-00bn-npca-fairness-for-unsupported-sta