## Slide 1: Further Considerations on NPCA - Follow up
Date: 2025-03-01
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com
Chaoming Luo |  |  |  | 
Ning Gao |  |  |  | 
Liangxiao Xin |  |  |  | 

## Slide 2: Introduction
802.11bn task group has agreed to define NPCA operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic.
And some behaviors currently specified for NPCA operation in 11bn Draft 0.1 are based on the assumption that NPCA AP and non-AP STA detect the same OBSS traffic. But due to the complexity of OBSS environment NPCA AP and non-AP STA possibly detect different OBSS traffic that may trigger them to switch from BSS primary channel to NPCA primary channel.
It would be more efficient to make sure that NPCA AP and non-AP STA(s) switch to the NPCA primary channel and do frame exchanges due to the same OBSS traffic. Therefore a mechanism is needed to have the NPCA STAs know whether their peer STA switch to the NPCA primary channel due to the same OBSS traffic.
This contribution analyzes the key issues for NPCA operation due to different OBSS traffic that trigger NPCA AP and non-AP STA switch to NPCA primary channel, and proposes candidate solutions for NPCA operation to be considered.

## Slide 3: Cases for different triggering switch conditions (1)
Different triggering switch conditions due to different views on OBSS
An example: An NPCA AP and a NPCA non-AP STA(i.e. STA1) can detect PPDUs from OBSS1, but another NPCA non-AP STA(i.e. STA2) can only detect PPDUs from OBSS2
(1) Case 1a: inconsistent switches that result in no frame exchange completed
STA2 switch to NPCA primary channel due to OBSS traffic between AP2 and STA2-1 but AP cannot switch to NPCA primary channel, therefore STA2 cannot do frame exchanges with AP.
(2) Case 1b: inconsistent stay duration on NPCA primary channel due to different OBSSs
Firstly STA2 switch to NPCA primary channel due to OBSS traffic between AP2 and STA2-1
Then AP and STA1 switch to the NPCA primary channel due to OBSS traffic between AP1 and STA1-1
STA2 obtains TXOP and then does frame exchanges with AP if allowed, but the TXOP duration is limited
AP1
AP
(NPCA AP)
STA1
STA2
STA1-1
AP2
STA2-1
(1)
(2)
OBSS1
OBSS2
(3)

## Slide 4: Cases for different triggering switch conditions (2)
Different triggering switch conditions due to different views on DL/UL for the same OBSS
Another example: An NPCA AP and a NPCA non-AP STAs(i.e. STA1 and STA2) can detect PPDUs from OBSS1, but STA1 can only detect PPDUs transmitted by AP1 and cannot detect PPDUs transmitted by STA1-1 from OBSS1
(3) Case 2a: misaligned switches that also result in no frame exchange completed - as STA1 cannot receive ICF in time on NPCA primary channel
Firstly AP1 does frame exchanges with STA1-1 with initial control frame exchange(such as RTS/CTS)
Then AP can detect the control frame exchange from OBSS1 and switches to NPCA primary channel
But STA1 cannot detect the control frame exchange, but detect the PPDU transmitted by AP1 after the control frame exchange, and then switches to NPCA primary channel.
(4) Case 2b: inconsistent stay duration on NPCA primary channel even if STA1 can receive ICF in time on NPCA primary channel – as different OBSS traffic is detected respectively by AP and STA1
AP
(NPCA AP)
AP1
STA1-1
OBSS1
STA2
STA1

## Slide 5: Issues for different triggering switch conditions - Summary
Different triggering switch conditions would result in low medium efficiency:
inconsistent switches from BSS primary channel to NPCA primary channel for different NPCA STAs that result in invalid or useless switches
misaligned switches from BSS primary channel to NPCA primary channel that result in failed frame exchanges.
Inconsistent stay duration and/or available BW on NPCA primary channel for different NPCA STAs that have switched to NPCA primary channel that results in limited potential TXOP duration for frame exchange.
A mechanism or tool is required to resolve the issues that would be helpful:
NPCA STA can collect the information of the triggering switch conditions from its peer STA(s) on the NPCA primary channel and then determine the target peer STA(s) for subsequent transmission based on the information.
NPCA STA can also confirm whether its peer STA switches to the NPCA primary channel due to the same OBSS traffic when it has switched to NPCA primary channel.

## Slide 6: Candidate Solution
Propose to provide a mechanism for triggering switch condition report operation
triggering switch condition report refers to the report on the condition of OBSS traffic that triggers NPCA STA to switch from BSS primary channel to NPCA primary channel, and its related info. may include:
Whether it is consistent with the peer STA’s if it knows triggering switch condition for the peer STA.
Triggering condition type (HE/EHT/UHR PPDU-based or control frame exchange)
OBSS color, OBSS BSSID, UL/DL, Duration, RSSI…
NPCA STA delivers triggering switch condition during frame exchanges on NPCA primary channel to assist its peer STA to know its triggering switch condition, that is helpful for the subsequent data frame exchanges.
For example, NPCA AP send triggering switch condition report poll frame as an initial control frame to trigger its associated NPCA STAs to response with their triggering switch condition report .
NPCA STA explicitly deliver triggering switch condition report in response to AP.
NPCA STA can also indicate whether its triggering switch condition is consistent with AP’s.
AP
(NPCA AP)
AP1
STA1-1
OBSS1
STA2
STA1

## Slide 7: Summary
There are several issues for different triggering switch conditions needed to be addressed for NPCA operation, such as ：
Inconsistent or misaligned switches
Inconsistent stay duration and/or available BW on NPCA primary channel
This contribution proposes to provide a mechanism for triggering switch condition report operation to resolve the issues that would be helpful:
NPCA STA can collect the triggering switch condition reports from its peer STA(s) on the NPCA primary channel and then determine the target peer STA(s) for subsequent transmission.
NPCA STA can also confirm whether its peer STA switches to the NPCA primary channel due to the same OBSS traffic when it has switched to NPCA primary channel.

## Slide 8: References
[1] Draft P802.11bn_D0.1
[3] non-primary channel access (NPCA) - follow up, https://mentor.ieee.org/802.11/dcn/24/11-24-0495-00-00bn-non-primary-channel-access-npca-follow-up.pptx
[4] Non-primary channel access (NPCA), https://mentor.ieee.org/802.11/dcn/23/11-23-2005-01-00bn-non-primary-channel-access-npca.pptx

## Slide 9: SP 1
SP1: Do you support to specify a mechanism to resolve the issues due to different triggering switch conditions for NPCA operation to make sure:
NPCA STA can collect the information of the triggering switch conditions from its peer STA(s) on the NPCA primary channel and then determine the target peer STA(s) for subsequent transmission based on the information.
NPCA STA can also confirm whether its peer STA switches to the NPCA primary channel due to the same OBSS traffic when it has switched to NPCA primary channel.
The mechanism is TBD

## Slide 10: SP 2
SP 2: Do you support to specify a mechanism for triggering switch condition report operation?
The mechanism is TBD
Liuming Lu (OPPO)