## Slide 1: Interoperability of NPCA primary channel switching conditions
Date: 2025-03-07
Authors:
Name | Affiliations | Address | Phone | email
Thomas Handte | Sony Group Corporation |  |  | Thomas.Handte@sony.com
Yusuke Tanaka |  |  |  | Yusuke.YT.Tanaka@sony.com
Dana Ciochina |  |  |  | 
Daniel Verenzuela |  |  |  | 
Ken Tanaka |  |  |  | 
Kosuke Aio |  |  |  | 
Ryuichi Hirata |  |  |  | 
Qing Xia |  |  |  | 

## Slide 2: Introduction
Non-primary channel access (NPCA) is one important enhancement for 11bn
  Several submissions and motions [1] address the operation
    The current development state is well captured in a PDT document [2] and D0.1 [3]
The design of the conditions, based on which STAs switch to the NPCA primary channel, is crucial for the performance of NPCA
  Certainly, a STA pair which intends to communicate need both to switch to NPCA primary channel
    Due to hidden transmissions, STAs may have a different view of the OBSS transmissions
      Thus, the likelihood that both STAs switch to the NPCA primary channel is anyway less than 100%
    Therefore, we need to design the switching conditions such that, if both STAs of a pair are affected by OBSS transmissions, the switching to NPCA primary channel and related frame exchange is (almost) always successful
This submission addresses an interoperability issue of the current switching conditions and proposes solutions

## Slide 3: Issue
Switching to the NPCA primary channel is triggered when any of the following two conditions apply [2]
  a inter BSS PPDU and/or a PHY-RXSTART.indication from a inter BSS HE/EHT/UHR PPDU, or
  a inter BSS control frame exchange is observed
  … and the received frames or PPDUs have certain additional properties [2, 3]
STAs may have a different view of an OBSS frame exchange depending on location
  While a first STA applies condition b), a second STA may apply condition a) because condition b) wasn’t fulfilled for the second STA due to a hidden transmission
    Thus, a first STA may detect a triggering event earlier than a second STA
  Consequently, the first STA may initiate a frame exchange on NPCA primary channel while the second STA is not yet available, or the first STA may have a channel access advantage

## Slide 4: Example
Assumption
  OBSS STA A and STA B perform a frame exchange
    The frame exchange consist of RTS, CTS, HE/EHT/UHR PPDU, BAck
  IBSS STA C may detect all frames
  IBSS STA D may detect RTS and the HE/EHT/UHR PPDU only
    i.e., STA B’s transmissions are hidden to STA D
Switching to NPCA primary channel
  STA C switches after CTS: condition b)
  STA D switches after SIG decoding of HE/EHT/UHR PPDU: condition a)
  Assuming same switching delay, STA C switches earlier than STA D to NPCA primary channel

## Slide 5: Difference in switching times
Switching times as seen from an observing STA
  i.e., a decoding delay later than signal on WM
  Assumptions
    NPCA NHT switch time () = PHY-RXEND.indication(success) of CTS following RTS
    NPCA HE switch time () = PHY-RXTART.indication(RXVECTOR)
Difference is
  can be larger for PPDUs with additional signaling fields such as E(L)R PPDUs
    is 40µs (HE ER, EHT ER, UHR ELR) or 32µs (all other HE, EHT, UHR PPDU formats)

## Slide 6: Implications of different switching times
Availability issue
  A STA may initiate a frame exchange on NPCA primary channel while the peer STA is not yet available
    A STA can access the medium as early as 34µs (or 25µs) after switching to NPCA primary channel
Fairness issue
  The STA that is earlier present on NPCA primary channel has an advantage in gaining channel access by counting down backoff slots earlier
Thus, STAs switching to NPCA primary channel should be available on this channel at (almost) same time

## Slide 7: Solutions
Essentially, two options exist
  Introduce a waiting time …
  Modify the triggering conditions …
  … such that regardless of the triggering conditions both STAs are available on NPCA primary channel at (almost) same time

## Slide 8: Option 1) waiting time
Currently, there are two conditions triggering the switch to NPCA primary channel
  Typically, condition b) (“control frame exchange”) detects a OBSS frame exchange faster than condition a) (“PPDU”)
  Thus, a waiting time should be considered whenever condition b) applies
The waiting time is ideally to be considered together with the switching time of a STA
  A STA that applies condition b) for switching to the NPCA primary channel at “NPCA NHT switch time” shall initiate a frame exchange on NPCA primary channel not earlier than its peer STA’s switching delay and the waiting time has passed.
  The waiting time is , i.e., 48µs or 56µs, subject to the assumptions on slide 5

## Slide 9: Option 2) modified triggering condition
Add to triggering condition b)
  to switch after a PHY-RXEARLYSIG.indication or PHYRXSTART.indication primitive is received on primary channel after the control response frame following the initiating control frame
    Such a primitive should be received within aSIFSTime + aRxPHYStartDelay +2x aSlotTime after the PHY-RXEND.indication(success) of control response frame following the initiating control frame
      This threshold essentially resembles NAVtimeout on primary channel for NPCA
  Implementing this change results in a of 8µs or 16µs which solves the availability issue, but not for the fairness issue
    We may add a small waiting time of 8µs or 16µs to remove the fairness issue as well

## Slide 10: Conclusion
This submission addresses an interoperability issue of the current conditions under which STAs initiate the switch to the NPCA primary channel
  If, due to hidden transmission issues, STAs detect a OBSS transmission with different conditions, a timing mismatch may occur which results in …
    … a first STA starting a frame exchange on the NPCA primary channel, while a second STA is not yet available, or
    … a first STA having a channel access advantage over the second STA
Two solutions are suggested to ensure that STAs are available on NPCA primary channel at almost same time regardless the applied switching condition
  Option 1: Implementation of a waiting time
  Option 2: Modification of the triggering condition for inter-BSS control frame exchange

## Slide 11: References
[1] 11-24/1762r16 “PDT-MAC-NPCA”
[2] 11-24/0209r7 “Specification Framework for TGbn”
[3] P802.11bn D0.1

## Slide 12: Straw Poll #0
(non-SFD, selects subsequent Straw Poll)
Which option do you prefer to address the timing mismatch of NPCA switching conditions
  (a) implementation of a waiting time (slide 8)
  (b) modification of the triggering condition “inter-BSS control frame exchange” (slide 9)
  (c) Abstain

## Slide 13: Straw Poll #1
Do you agree to add the following to the TGbn SFD?
The point in time when a STA may initiate a frame exchange on the NPCA primary channel reflects a waiting time such that STAs are available on the NPCA primary channel at same time, regardless the condition that caused the STA to switch to the NPCA primary channel.
- The waiting time is TBD
- Whether the waiting time is a fixed value or can be set by AP is TBD

## Slide 14: Straw Poll #2
Do you agree to add the following to the TGbn SFD?
In NPCA operation, when the STA received a PPDU containing a Control frame and a PPDU containing an initial response frame of a Control frame exchange on the BSS primary channel the following condition shall be added:
A PHY-RXEARLYSIG.indication or PHYRXSTART.indication primitive is received after the Control frame exchange on the BSS primary channel within TBD time after the initial response frame of the Control frame exchange