## Slide 1: PPDU Parameters for Multi-AP Coordination
Date: 2025-01-13
Authors:

## Slide 2: Abstract
Multi-AP coordination is one of the features in 802.11bn.
To support Multi-AP coordination, one AP may send frames to another AP.
  APs that intend to participate in Multi-AP coordination can use management frames to advertise/discover the capabilities and/or parameters of individual schemes. [Motion #147]
  APs that discovered each other and want to establish agreement(s) for Multi-AP coordination scheme(s), can use individually addressed management frames to establish the agreement(s) and negotiate parameters. Note: The management frame can be a Public Action and/or new Action frames, and so on. [Motion #148]
When management frames are carried in HE/EHT/UHR PPDU, values of the UL/DL flag, BSS Color and STA_ID need to be defined.

## Slide 3: UL/DL, BSS Color and STA_ID
UL/DL - Indicates whether the PPDU is sent in UL or DL
  A value of 1 indicates the PPDU is addressed to an AP.
  A value of 0 indicates the PPDU is addressed to a non-AP STA
BSS Color - An identifier of the BSS.
  Identifies the BSS from which the PPDU originates.
STA_ID
  If UL/DL is set to 0, identifies the STA or group of STAs that is the recipient of an RU in the PPDU
  If UL/DL is set to 1, set to the 11 LSBs of the AID of the non-AP STA transmitting the PPDU.
The baseline spec does not consider AP to AP transmissions in terms of PPDU parameter settings. Based on the current spec, a reasonable setting for the mentioned parameters in a UHR PPDU will be
UL/DL = 1
BSS Color = BSS color of transmitting AP
STA_ID = AP ID of receiving AP
AP ID – A value used for identifying an AP, with which a Multi -AP coordination agreement has been set, prior to or during a M-AP Coordination transmission. [1]

## Slide 4: Problem
If we follow the baseline spec to set UL/DL, BSS Color and STA_ID, APs (e.g. AP 1) will not be able to filter UHR PPDUs based on the U-SIG. This may increase the power consumption of the AP unnecessarily.
  If AP ID has been assigned from another AP (e.g. AP 2), AP 1 needs to decode up to the UHR-SIG to check the AP ID.
  If AP ID has not been assigned from a particular AP (e.g. AP 3), AP 1 needs to decode the entire PPDU.
AP 2
BSS Color =2
AP 1
BSS Color =1
UHR PPDU
UL/DL = 1, BSS Color = 2, STA_ID = AP 1 AP ID
STA 3
BSS Color =3
Not Filtered
STA 2
BSS Color =2
UHR PPDU
UL/DL = 1, BSS Color = 2, STA_ID = STA 2 STA ID
Decode up to UHR-SIG then filtered
UHR PPDU
Decode up to the Data field then filtered
UL/DL = 1, BSS Color = 3, STA_ID = STA 3 STA ID
AP ID
assignment
procedure

## Slide 5: Proposal
Our proposal is to set
UL/DL = 1
BSS Color = BSS color of receiving AP
STA_ID = AP ID of transmitting AP (Optional)
The AP can then use the baseline receive procedure regardless of whether the PPDU is from an associated STA or from another AP.
AP 2
BSS Color =2
AP 1
BSS Color =1
UHR PPDU
UL/DL = 1, BSS Color = 1, STA_ID = AP 1 AP ID
STA 3
BSS Color =3
Not Filtered
STA 2
BSS Color =2
UHR PPDU
UL/DL = 1, BSS Color = 2, STA_ID = STA 2 STA ID
Decode up to U-SIG then filtered
UHR PPDU
Decode up to U-SIG then filtered
UL/DL = 1, BSS Color = 3, STA_ID = STA 3 STA ID
AP ID procedure

## Slide 6: Proposal
UL/DL - Indicates whether the PPDU is sent in UL or DL.
  A value of 1 indicates the PPDU is addressed to an AP.
  A value of 0 indicates the PPDU is addressed to a non-AP STA
BSS Color - An identifier of the BSS.
  For AP to AP transmission, identifies the BSS of the receiving AP.
  Otherwise, identifies the BSS from which the PPDU originates.
STA_ID
  If UL/DL is set to 0, identifies the STA or group of STAs that is the recipient of an RU in the PPDU
  If UL/DL is set to 1 and a non-AP STA is transmitting the PPDU, set to the 11 LSBs of the AID of the non-AP STA transmitting the PPDU
  If UL/DL is set to 1 and an AP STA is transmitting the PPDU, set to the AP ID of the AP STA transmitting the PPDU.

## Slide 7: Strawpoll
Do you agree to explicitly define UL/DL, BSS Color and STA_ID for UHR MU PPDUs transmitted from one AP to another AP as follows:
  UL/DL is set to 1
  BSS Color is set to the BSS Color of the recipient AP
  STA_ID is set to the AP ID of the AP transmitting the PPDU (if available)
Y
N
A

## Slide 8: References
[1] https://mentor.ieee.org/802.11/dcn/24/11-24-2049-02-00bn-pdt-mac-m-ap-coordination-framework.docx