## Slide 1: DRU Distribution BW Indication in UHR Trigger Frame
Date: 2025-1-12
Authors:
Name | Affiliations | Address | Phone | Email
Mahmoud Hasabelnaby | Huawei |  |  | Mahmoud.Hasabelnaby@huawei.com
Junghoon Suh |  |  |  | 
Ross Jian Yu |  |  |  | 
Yan Xin |  |  |  | 
Osama Aboul-Magd |  |  |  | 
Sara Norouzi |  |  |  | 
Notes: September 2012

## Slide 2: Background: Distribution BW of 60 MHz
[Motion #64] DRU distribution bandwidth of 60 MHz is defined in an 80 MHz frequency subblock (with the highest 20 MHz subchannel unallocated) in a UHR TB PPDU
  No allocation is made in the highest 20 MHz subchannel
As a result, Distribution bandwidth (DBW) defined for UHR UL TB PPDU transmission are 20 MHz, 40 MHz, 60 MHz and 80 MHz.

## Slide 3: Background: UHR variant User Info field
[Motion #188] Use the following UHR variant User Info field design:
  The SS Allocation subfield design depends on RRU or DRU.
  Repurpose 1 bit in the SS Allocation subfield in the UHR variant User Info field to indicate NSS (1SS or 2SS) in the case of DRU.

## Slide 4: 60 MHz DBW Indication
The 2-bit DRU Distribution BW is encoded as follow:
Value | Distribution BW Indication
0 | Distribution BW 20 MHz
1 | Distribution BW 40 MHz
2 | Distribution BW 80 MHz
3 | Reserved Distribution BW 60 MHz

## Slide 5: Summary
In this contribution, we propose to indicate a 60 MHz DBW using a value of 3 in the 2-bit DBW indication subfield within the UHR variant User Info field of a Trigger Frame in the case of DRU.

## Slide 6: References
11-24/0209r7, “Specification Framework for TGbn”.
11-24/2046r2, “Proposed Text Draft on DRU”.

## Slide 7: Straw Poll
Do you support to indicate a 60 MHz DBW using a value of 3 in the 2-bit DBW indication subfield within the UHR variant User Info field of a Trigger Frame in the case of DRU?