## Slide 1: Protocol Identifier Encoding of EtherType
Date: 2025-01-13
Authors:

## Slide 2: Abstract
In IEEE Std 802-2024, if EtherType is encoded in a Protocol Identifier using Length/Type encoding, the Protocol Identifier Field (PIF) contains only the EtherType.

## Slide 3: IEEE Std 802-2024
EtherType is an E-Type Protocol Identifier
Can be encoded two ways:
  Type 3 PIF encoding, which uses a Length/Type field (as in Ethernet)
  Type 2 PIF encoding, which does not use a Length/Type field (RFC 1042 form of SNAP)

## Slide 4: IEEE Std 802-2014
Showed bizarre frame formats, such as:
By implication, a simpler form (Form X) was also supported:
Form X is inconsistent with each 802-2024 PIF format.

## Slide 5: Why is the Form X example gone?
Form X includes a “Length”, which is specified only within a Length/Type field.
A Length/Type field is used only in a Type 3 PIF
  Ethernet-like frame
To convey an E-type protocol identifier (an EtherType) using a Type 3 PIF, the PIF contains only the EtherType.
  figure on prior slide
Form X inserts a bunch of bytes before the EtherType.
Questions that might arise:
  Could one, or should one, or why would one:
      insert an extra “Length-0xAAAA03-0x000000” before the EtherType?

## Slide 6: Question 1: Are the LLCs distinct?
Assume Frame 1 arrives with PIF 0x0800 and is sent to an IPv4 protocol stack.
Now Frame 2 arrives with PIF Length-0xAAAA03-0x000000-0x0800.
Question 1: Does it go to the same IPv4 protocol stack as Frame 1? Or to a different IPv4 instantiation?
  Answer: No version IEEE Std 802 has an answer.
  However, according to 802.1Q, if the frame traverses a Type 2 network, Length-0xAAAA03-0x000000 is stripped. So a frame could be delivered in either form; we cannot rely on the network to accurately demultiplex frames to two separate instances.

## Slide 7: Question 2: Are the delivered frames distinct?
Is the intent that the frame passed to the higher-layer protocol (per the EtherType) is formatted to include the Length-0xAAAA03-0x000000, or not include it, depending on how it was sent?
For the reason described on the prior page, that’s difficult to ensure.
This was addressed by IEEE Std 802.1H-1995.
  A specific list of EtherTypes was specified.
  For any EtherType on that list, frame were supposed to be delivered retaining the Length-0xAAAA03-0x000000 encapsulation.
  Only one EtherType was ever on the list.

## Slide 8: View on 802.1H
Per M. Seaman, “Protocol identification in 802 LANs”:
  IEEE Std 802.1H-1995, Recommended Practice for Media Access Control (MAC) Bridging of Ethernet V2.0 in IEEE 802 Local Area Networks was created to clarify that EPD encoding of SNAP Identifiers does not include use of 00-00-00 in the OUI portion of the SNAP Identifier. This Recommended Practice was withdrawn at a time when it was felt no longer necessary to address possible confusion on this point.

## Slide 9: Conclusion
In IEEE Std 802-2024, if EtherType is encoded in a Protocol Identifier using Length/Type encoding, the Protocol Identifier Field (PIF) contains only the EtherType.