## Slide 1: Proposals for hiding SA and DA
Date: 2025-01-14
Authors:

## Slide 2: Abstract
Background: Reference [1] identifies SA/DA privacy issues. Reference [2] requirement 13 states “11bi shall define or reuse a mechanism for CPE Clients and CPE APs to protect the SA/DA values from exposure OTA to 3rd parties.”
Problem: No text has been proposed.
Proposal: The following options are proposed:
Add a note that A-MSDU should be used if SA/DA protection is needed
Encrypt the A3/A4 fields in place -OR- move them inside the payload for encryption
Per-epoch offset added or XORed to A3/A4
Authors suggest using Option 1.

## Slide 3: Background
Background
  Source address (SA) and destination address (DA) are transmitted in the clear (unencrypted) in MAC header fields Address 3/Address 4 (A3/A4).
  SA (or DA) of a frame transmitted to (or from) a given non-AP STA/MLD can identify another non-AP STA/MLD.
  Suppose a non-AP STA/MLD is the source (or destination) of a frame.
    If DS MAC is enabled, then SA (or DA respectively) is the DS MAC. DS MAC changes per (re)association.
    In other cases, SA/DA has a longer lifetime.
  Frame anonymization does not obfuscate SA/DA. Consequently, an attacker can track a EDP device across multiple epochs when frame anonymization is enabled.
Problem
  The requirement to hide SA/DA has been identified in [1,2] and discussed, but no text has been proposed. This document presents some options, so TGbi can decide on a way forward.

## Slide 4: Option 1. Recommend A-MSDU
Description
  An A-MSDU aggregates one or more MSDU into a single encrypted payload.
  The A-MSDU MAC header does not transmit A3 and A4 fields.
    The A3 and A4 fields of constituent MSDUs are sent in the payload, where the values are encrypted.
  Simply requires adding a note “A-MSDU should be used if SA/DA protection is needed”
Analysis:
  Advantages: Prevents presence monitoring. No new description text needed.
  Disadvantages: A-MSDU adds some overhead
Authors’ Suggestion: Specify this option.

## Slide 5: Proposal 2. Encrypt SA/DA
Description
  Transmitter: make SA/DA part of the GCMP/CCMP plaintext for the encryption processing, resulting in encrypted SA/DA.
  Receiver: make encrypted SA/DA part of the GCMP/CCMP ciphertext for the decryption processing, resulting in SA/DA.
  Options for transmitting the encrypted SA/DA:
    Proposal 2a: Encrypt SA/DA as part of the GCMP/CCMP. Transmit in the A3/A4 fields.
    Proposal 2b: Encrypt SA/DA as part of the GCMP/CCMP. Transmit as part of the payload.
Analysis
  Advantages: Prevents presence monitoring. No additional overhead. Re-uses encryption algo.
  Disadvantages: Requires new normative text. Introduces processing flow/hardware changes.
Authors’ Suggestion: Specify this option if A-MSDU is unacceptable.

## Slide 6: Proposal 3. SA/DA obfuscated by Frame Anonymization
Description
  Extend Frame Anonymization to obfuscate SA/DA
    Every epoch, generate 48-bit EDP_SA_DA_offset
    For each frame, produce obfuscated OSA (if SA is transmitted) and ODA (if DA is transmitted) using simple operations:
      OSA = SA xor EDP_SA_DA_offset,
      ODA = DA xor EDP_SA_DA_offset,
    Alternatively, use “addition modulo 248” in the place of “xor”.
Analysis
  For given non-AP MLD and given epoch, EDP_SA_DA_offset identical for all source/destinations.
  Suppose multiple source devices with MAC addresses SA1, SA2 , SA3, …  OSA1, OSA2, OSA3, …
    OSAi = SAi xor EDP_SA_DA_offset,
    OSAi xor OSAj = (SAi xor EDP_SA_DA_offset) xor (SAj xor EDP_SA_DA_offset) = SAi xor SAj,
    OSAi xor OSAj is independent of EDP_SA_DA_offset, i.e., doesn’t change.
  Advantage: Simple
  Disadvantage. Does not prevent presence monitoring! Not effective.
Authors’ Suggestion: Do not specify this option.

## Slide 7: Conclusion
Authors suggestion
  Add a note that A-MSDU should be used if SA/DA protection is needed

## Slide 8: References
[1] 11-21-1328-00-00bi-changing-sta-mac-addresses-per-association-and-sa-da-hiding.pptx“
[2] 11-21-1848-16-00bi-requirements-document