## Slide 1: Channel Measurement Announcement
Date: 2025-1-15
Authors:

## Slide 2: Introduction
Off Channel Scan is widely used on AP devices to measure channel quality to optimize channel
Still many APs or non-AP STAs have difficulty obtaining accurate channel measurements without dedicated scan period.
We found issues with packet losses in mesh networks when the Controller sends small packets to the Wireless Extender, while the latter is busy doing an off-channel scan.
In this contribution, we propose a Channel Measurement Announcement (CMA) to signal an off-channel scan to peer STAs. The CMA will include information about the channel to be scanned.

## Slide 3: Packet lost issue during off channel scan
Topology: Mesh network (root – wireless backhaul - extender)
Continuous Ping(Small size packet, no RTS/CTS) from root to extender (no dedicated scan chain)
Extender perform off channel every 1min, dwell time is 100ms
Packet Loss is seen on root during extender perform off channel sometimes
We also monitor packet loss issue especially Hi-Q video service played on backhaul during peer off channel scan
Root AP
Extender STA-AP
AP txop
STA txop
AP Send packet to STA on channel 1
STA response packet to STA on channel 1
AP txop
STA switch to channel 11 to scan.
AP send new packet on channel 1 to STA, after maxmim retires reach, packet drop or send successfully but with many retires
Time

## Slide 4: Recap) In-Device Coexistence
In [1] introduced,
In general, for predictable and non-urgent co-ex events, the STA (/AP) can notify the other AP(/STA) ahead of time about the upcoming unavailability for operation
  Existing technologies defined in 802.11, such as peer-to-peer TWT, can be used or enhanced to support these co-ex events For urgent co-ex events, a TXOP-level intervention is needed
  The STA(/AP) can indicate within a TXOP the reduced capability of operation due to the co-ex events
  Control frames can be used to make such indications—
    Truncated TXOP
    Reduced BW
    Reduced RX NSS etc.
  Measurement as off channel scan is similar with co-existence event which is absence event with availability info as new channel or reduced RX NSS and unavailability info as leave start time and duration on operating channel.

## Slide 5: Measurement Benefits
  Recap )[2], also list problems of existing Measurement,
  Measurement usual takes long time due to Beacon interval or active scans.
  Long term measurement create several problems as power consumption.
  Coordinated Observation Type and Transmission Type proposed.
  Also, we found some user cases as band steering, we want to observe unassociated
  link metric(RSSI) but some stations don’t send probes on that link.
  But if we can announce measurement type to that station, the station could send a probe
  packet on measurement link. It can reduce measurement time and help observer get accurate
  unassociated link metric.
  Measurement Announcement should be benefit to various measurement types.

## Slide 6: Recap) PDT MAC Coexistence
In[3], there define DUO/PUO/LOM mode.
For off-channel scan case, it’s out of ongoing TXOP. It can use PUO mode to
signal unavailability, but PUO mode requires to set up P2P TWT session with
additional TWT setup packets which is inefficient compares with a single signaling
frame.
And this signaling frame could include measurement info and limit operations
together as well for channel measurement case.

## Slide 7: CMA signaling
Root AP
Extender STA-AP
AP txop
STA txop
AP Send packet to STA on channel 1
STA repsonse packet to AP on channel 1
AP txop
STA switch to channel 11 to scan.
AP defers transmitting to STA on channel 1
Time
CMA
We proposal to send Channel Measurement Announcement to Peer before do measurement on off channel
Signal Info Field:
Measurement Type 2) Measurement Mode( Any restriction on receive packet on scan channel)
3) Target Channel 4) Target Bandwidth 5) Start time 6) Duration 7) Available NSS

## Slide 8: Summary
We proposal a new signaling method (Define a new Channel Measurement Announcement frame) in 11bn to support signal channel measurement information as measurement type, mode, channel, bandwidth, start time, duration, available NSS etc. to fix packet loss, latency, long measurement time and other measurement issues.

## Slide 9: Straw Poll 1
Do you agree that TGbn defines a new frame(Channel Measurement Announcement) or other signaling method sent from AP/STA to STA/AP to signal channel measurement information, frame type and detail signal info is TBD?
YES
No
Abstain

## Slide 10: Straw Poll 2
Do you agree that TGbn add below info into Channel Measurement Announcement Frame? Other signal info is TBD
Measurement Type
2) Measurement Mode( Any restriction on receive packet on scan channel)
Target Channel
Target Bandwidth
Start time
Duration
Available NSS
YES
No
Abstain

## Slide 11: References
[1] 24/0509r1, “Thoughts on in-device coexistence and P2P for 11bn”
[2] 24/1452r3, “Coordinated Measurement: Follow-up”
[3] 24/2040r9, “PDT MAC Coexistence”