## Slide 1: Post-Quantum Opportunistic Wireless Encryption (PQ-OWE)
Date: 2025-03-03
Authors:

## Slide 2: Abstract
Opportunistic Wireless Encryption (OWE) is widely used in the 6 GHz band. OWE makes use of the Diffie-Hellman exchange, based on finite cyclic groups and elliptic curves, to derive the PMK. These techniques are at risk of attack by quantum attackers.
This submission proposes a mechanism that would enable the use of quantum resistant techniques to achieve Post-Quantum Opportunistic Wireless Encryption.

## Slide 3: Problem
Shor developed quantum algorithms for solving the discrete logarithm problem back in 1994
Shor’s algorithm runs in polynomial time, with an ~ runtime complexity of O((log N)2 (log log N))
  This is a significant improvement in runtime over the current state-of-art sub-exponential algorithm
As far as we know, no machine today can run Shor’s algorithm
  But such a machine could have been already been built or could be developed tomorrow
    There was no press release when Enigma was hacked
  Or be built in less time than it will take to deploy PQ-OWE
Other quantum algorithms also aim to achieve the same goal, e.g. Regev’s

## Slide 4: Problem
The outcome is that Diffie-Hellman exchanges are left vulnerable when faced with a quantum attacker
  Both finite field and elliptic curve cryptography are deemed vulnerable
  The latter is most likely to fall first due to the smaller key sizes
The market is moving from classical to post-quantum cryptography
  Cloudflare, Chrome, Signal, iMessage, Zoom
  CNSA 2.0, updated for quantum-resistant algorithms, requires post-quantum cryptography to be used as default from this year in Software/ Firmware/ Browsers/ Cloud services, Networking equipment from 2026
NIST has listed Elliptic Curve Diffie-Hellman exchanges as disallowed for key establishment after 2035

## Slide 5: What does OWE look like today?

## Slide 6: What does OWE look like today?
As OWE currently relies on a Diffie-Hellman exchange, it will be susceptible to quantum attacks
  Most likely attack vector will be comprised of an end node sniffing the association process and sending the Diffie-Hellman element for processing to an off-site quantum machine
After the Diffie-Hellman exchange all steps to the PMK are deterministic
There is a need to move away from Diffie-Hellman exchanges, and thus there is a need to move away from Diffie-Hellman elements

## Slide 7: What would a post-quantum OWE look like?
NIST specifies as an asymmetric algorithm for key establishment: Module-Lattice-Based Key-Encapsulation Mechanism Standard (ML-KEM)
  ML-KEM is derived from the round-three version of the CRYSTALS-Kyber KEM, a submission in the NIST Post-Quantum Cryptography Standardization project
The specification can be found at FIPS 203
Comprised out of three main key encapsulation algorithms
  Key generation accepts no input, generates randomness internally, and produces an encapsulation key and a decapsulation key
  Encapsulation accepts an encapsulation key as input, generates randomness internally, and outputs a ciphertext and a shared key
  Decapsulation accepts a decapsulation key and ciphertext as input, does not use any randomness, and outputs a shared key

## Slide 8: What would a post-quantum OWE look like?

## Slide 9: What would a post-quantum OWE look like?
ML-KEM encapsulation key and ciphertext need to be sent over the air
ML-KEM comes in 3 flavours:
Both the encapsulation key and ciphertext are significantly longer than Diffie-Hellman public keys, and thus unsuitable for association frames
  There is a risk of extending the association frames towards and beyond the limit of an MMPDU
Parameter set | Encapsulation key (octets) | Decapsulation key (octets) | Ciphertext (octets) | Shared secret key (octets)
ML-KEM-512 | 800 | 1632 | 768 | 32
ML-KEM-768 | 1184 | 2400 | 1088 | 32
ML-KEM-1024 | 1568 | 3168 | 1568 | 32

## Slide 10: What would a post-quantum OWE look like?
NIST recommends using ML-KEM-768 as the default parameter set, as it provides a large security margin at a reasonable performance cost
While ML-KEM has longer keys than DH, it is proving to be more efficient in run-time
  If clogging wasn’t a concern for DH, it is unlikely to be one for ML-KEM
  Runtime will vary, but general consensus seems to be that ML-KEM is faster than DH
ML-KEM can, extremely seldom, fail to decapsulate correctly
  K′ ≠ K
  This will cause the 4-way handshake to fail
  A retry should fix the problem
Parameter set | Decapsulation failure rate
ML-KEM-512 | 2−138.8
ML-KEM-768 | 2−164.8
ML-KEM-1024 | 2−174.8

## Slide 11: What would a post-quantum OWE look like?
We would need a new AKM suite selector for PQ-OWE
  More than one AKM can be used if other parameter sets than ML-KEM-768 are envisioned to be used
We would probably need to mandate 256-bit TKs, hence GCMP-256 should be used
  In order to avoid any risk of attacks on symmetric encryption, facilitated by Grover’s algorithm
We will need to do more than PQ-OWE, but developing PQ-OWE is a first useful building block for authenticated protocols

## Slide 12: Straw poll
A mechanism should be added to ensure OWE is resilient against quantum attackers by adopting ML-KEM?
Y
N
A

## Slide 13: References
NIST: Module-Lattice-Based Key-Encapsulation Mechanism Standard
Shor: Polynomial-Time Algorithms for Prime Factorization and Discrete Logarithms on a Quantum Computer
Grover: A fast quantum mechanical algorithm for database search
Regev: An Efficient Quantum Factoring Algorithm
Harkins: Post-Quantum 802.11
MIT xPRO: Quantum Algorithms for Cybersecurity, Chemistry, and Optimization
NIST: Transition to Post-Quantum Cryptography Standards