## Slide 1: Access Delay for Seamless Roaming
Date: 2025-2-5
Authors:
Name | Affiliations | Address | email
Haorui Yang | China Mobile | Hangzhou, Zhejiang, China | yanghaorui0217@163.com

## Slide 2: Introduction
In [1], many Motions have been passed for seamless roaming, including the framework, request/responce frame exchange between non-AP MLD and AP MLD.
The whole SR procedure consists of the optional preparation phase and the mandatory execution phase, and is expected to be a long-duration procedure.
  The preparation phase consists of the frame exchange between non-AP MLD and source AP MLD, the context transfer between the source AP MLD and target AP MLD and the link setup with target AP MLD.
  The execution phase consists of the frame exchange between non-AP MLD and (source or target) AP MLD, the context transfer between the source AP MLD and target AP MLD and the in-coverage acknowlege from non-AP MLD to target AP MLD.

## Slide 3: Design Principle
One of the most important aspects of SR is to minimize the whole duration.
  The coverage of BSS is relatively small in deployment, such as a few tens of meters.
  The movement from the source AP MLD to the target AP MLD will be fast compared to the SR procedure duration, especially for the dense deployment.
  Therefore, the SR procedure should be completed as soon as possible.
    Avoiding the scenario that the non-AP MLD has moved into the coverage of the target AP MLD but the SR procedure with non-AP MLD initiating to the source AP MLD is not completed.

## Slide 4: Focus
The frame exchange over the air between non-AP MLD and AP MLD, possibly also between two AP MLDs, should firstly obtain the TXOP by EDCA in the baseline.
Therefore, this submission focus on how to reduce the access delay for the frame exchange over the air.

## Slide 5: Solution
To save the time used for EDCA, all the frame exchanged over the air shall be treated with AC_VO.
  The existing QMF feature can be reused with adding the newly defined frame for SR, if supported.
  For the preparation phase, the request frame from non-AP MLD is suggested to be a new Action frame with the AC_VO.
    The ML reconfiguration in the baseline to add the other link is not appropriate, becasue:
      There is no target AP MLD MAC address in the frame, with only the link ID in the pre-STA profile.
      After adding the link, all TIDs are mapped to the newly added link until TTLM is updated.
    Reassociation request frame is against the idea of adding a new link to the target AP MLD.

## Slide 6: Solution
During the execution phase triggered to source AP MLD, the target AP MLD can send a trigger frame with RU allocation to the non-AP MLD via the source AP MLD.
  The trigger frame can be put in a container in the frame sent by source AP MLD to non-AP MLD.
When the non-AP MLD moves under target AP MLD, non-AP MLD sends TB PPDU to the target AP MLD to inform its in-coverage by using the allocated RU.

## Slide 7: Summary
This submission proposes to reduece the access delay for SR.
The proposed solution includes:
  All the individually addressed management frame exchanged over the air shall be treated with AC_VO.
  The target AP MLD sends Trigger frame to non-AP MLD via the source AP MLD to allocate the RU used by non-AP MLD to inform its in-coverage to target AP MLD.

## Slide 8: Straw Poll 1
Do you support to include the following in 11bn SFD?
  All the seamless roaming related individually addressed management frame exchanged over the air between source AP MLD and non-AP MLD STA/target AP MLD shall be treated with AC_VO.
  Supporting List: [25/0237]

## Slide 9: Straw Poll 2
Do you support to include the following in 11bn SFD?
  During the execution phase triggered to source AP MLD, the target AP MLD can send a trigger frame with RU allocation to the non-AP MLD via the source AP MLD.
  Supporting List: [25/0237]

## Slide 10: References
[1]: 24/0209r8, Specification Framework for TGbn