## Slide 1: IMMW System Reuses
Date: 2025-02-08
Authors:
Name | Affiliation | Address | Phone | Email
Yanchun Li | Huawei |  |  | liyanchun@huawei.com
Yunbo Li |  |  |  | 
Ming Gan |  |  |  | 
Fan Xu |  |  |  | 
Yan Xin |  |  |  | 
Maolin Zhang |  |  |  | 
Xiang Wang |  |  |  | 
Xin Li |  |  |  | 
Xuming Wu |  |  |  | 
Jian Li |  |  |  | 
Yanchun Li (Huawei)

## Slide 2: Introduction
IMMW PAR[1] defined the basic requirements and scope of the new mmW spec, which emphasizes the reuse and MLO framework:
Use non-standalone operation in unlicensed bands in 42~71 GHz using SU OFDM based transmissions
Expand the multi-link operation (MLO) defined in the sub-7.25 GHz band specifications to support non-standalone operation in the unlicensed bands between 42 GHz and 71 GHz.
By reusing sub-7 GHz MAC/PHY, the system complexity and cost can be reduced.
This contribution considers the tradeoff between reuse and efficiency. Moderate beam searching procedure can be helpful for indoor low mobility use cases. Considering that most of actual indoor use cases do not have stringent requirement on mobility, maximize reuses of 11be (with 11ac/11ax backward compatibility) and slight extra modification can provide a 11bq baseline framework.

## Slide 3: Use cases and Market are ready
Market is expecting high throughput, low latency mmW technologies.
mmWave can provide Wi-Fi network enhancement in multiple dimensions: increased throughput, reduced latency and high degree of spatial reuse [2,3,4].
    8K/3D/Multiview UHD Video Streaming/Entertainment
    Smart Cities: Supporting applications like traffic management systems, safety monitoring, and environmental sensors
    Industrial Automation: High-speed data transfer for real-time control of robots and machinery in factory environments
    Virtual Reality (VR) and Augmented Reality (AR): Low-latency transmission of large data streams for immersive experiences.
    Autonomous Vehicles (AVs), Unmanned Aerial Vehicles (UAVs): Real-time communication between drones for coordinated navigation and data transmission.
  And sub-7GHz is already very close to its limits in these dimensions.
    11bn technical members agrees that not to go beyond 320MHz bandwidth, 4K QAM modulations, 8 spatial streams.

## Slide 4: Proposed IMMW MAC
 |  | IMMW Initial Link Setup |  |  |  |  | Beam searching /tracking | Digital MIMO | Data Transmission |  |  | Power Saving | 
 |  | Scan | Synchronization | Authenticate/ Deauthenti-cate | Associate/ Reassociate/Disassociate | Measure-ment Request/ Report |  | NDP Sounding | Block Ack | TDLS/ P2P | Multi-link Operation | TWT Power Saving | SMPS /OMI /etc.
Feature can be Reused |  |  |  | ● (11be) | ● (1be) |  |  | ● | ● | ● | ● (11be) | ● | ●
Features to be considered (e.g. minor changes) | Sub- 7GHz based | ● | ● |  |  | ● | ● |  |  |  |  |  | 
 | mmW | ● |  |  |  | ● | ● |  |  | ● |  |  | 
Initial Considerations on MAC Design
Reuse and perform most of management procedures in sub-7GHz band
NAV (Channel Sensing/RTS/CTS/NAV) in mmW band
New mmW Beam sweeping process to keep efficient and timely beam searching/tracking
Note: black dot sign means involves reuse/potential improvement
Notes: Data Transmission
1）TWT enhancement for mmW, Amend

## Slide 5: Proposed IMMW PHY
 | Reuses |  | 
 | 11be (including 11ax/ac) | 11bn | Amemded in 11bq
PPDU Structure | ● | ● ELR PPDU | 
OFDM Symbols | ● | ● | 
MCS | ● | ● UEQM New MCS 2x LDPC (Stable) | 
Beamforming | RTS/CTS based |  | Beam searching/tracking
Tx specification Spectral Mask Spectral Flatness EVM |  |  | ●
Rx specification CCA sensitivity |  |  | ●
Channelization/ Ch Numbering |  |  | ●
11be + 11bq RF spec allows quick adoption of IMMW in Initial Phase.
11bn + 11bq new beam searching + 11bq RF spec allows advanced experience with enhanced coverage and better Beam Tracking later on.
As plus, but not essential.

## Slide 6: Summary
This contribution discussed the detailed reuse and amendment under the scope of IMMW PAR.
Use cases and market for 11bq are ready.
A flexible reuse framework allows IMMW system to be built on sub-7GHz systems, first on 11be (including 11ac/11ax mode) and later on 11bn. Such two-phase approach has benefit of promoting early adoption of IMMW/make use of 60GHz spectrum and also provide advanced performance.
Sub-7GHz PHY parameters for 11bq use are already settled, e.g. LDPC, MCS, MIMO.

## Slide 7: References
[1] IMMW proposed PAR, https://mentor.ieee.org/802.11/dcn/24/11-24-0116-07-immw-immw-draft-proposed-par.docx
[2] 23/1819r1, Integrated mmWave Design Considerations, Claudio da Silva
[3] 23/1977r1, Requirements Analysis for IMMW Use Cases, Yue Xu
[4] 22/1581r0, a perspective on proposed uhr features for enterprise use cases, Brian Hart
Yanchun Li (Huawei)

## Slide 8: SP
SP : Do you support to define a flexible reuse framework that allows a baseline IMMW system to be built on 11be (support 11ac/ax modes), in SFD?
Yes
No
Abs
Yanchun Li (Huawei)