## Slide 1: EPCS Priority Access Context Transfer Date: 2025-03-XX

## Slide 2: Abstract
This presentation discusses the need for transferring context related to EPCS Priority Access during seamless roaming and describes the context that needs to be transferred

## Slide 3: Background
Emergency Preparedness Communications Service (EPCS) priority access features were specified in IEEE 802.11be [1] to provide preferential channel access to authorized users
Preferential access helps ensure that individuals with emergency and mission critical responsibilities can communicate even when Wi-Fi network access channel is congested
AP MLDs grant priority channel access via affiliated APs after verifying that non-AP MLDs have the authority to use the EPCS features

## Slide 4: Context in Seamless Roaming Motions
Motion 26 describes a seamless roaming mechanism including context transfer (details of mechanism and context to be transferred are TBD)
Motion 44 indicates frame to initiate roaming with context transfer (context is TBD)
Motion 162 describes roaming preparation phase, including transfer/renegotiation of context
Motion 282 describes ability for non-AP MLD to send request to current AP MLD to determine what context transfer (Context is TBD)
Motion 283 describes seamless roaming procedure, including transfer of context (whether/how context is negotiated is TBD)

## Slide 5: Context Transfer in Contributions
Numerous contributions have discussed context transfer in seamless roaming
  11-24/0052 assumes context can be transferred via backhaul
  11-24/0480 suggests procedures and signaling for context transfer
  11-24/0830 proposes transfer of “essential context to continue UL and DL operation”
  11-24/1425 describes a pre-roam feasibility check to ensure target can accept full context
  11-24/1476 describes how APs may determine whether to transfer or renegotiate context
  11-24/1516 describes context transfer/renegotiation and over-the-air/over-the-ds context transfer
  11-24/1595 describes need for MLME interface to facilitate context transfer
  11-24/1812 describes proactive transfer of static context and fetching of dynamic context
  11-24/1851 describes transferring static context and per-TID dynamic context
  11-24/1883 describes context transfer for AP MLDs in same seamless mobility domain
  11-25/0040 proposes that Current AP MLD retains context for period to reduce overhead for ping-pong transitions and that context transfer results (success/failure) be reported to non-AP MLD

## Slide 6: EPCS Context for Seamless Roaming
Context associated with EPCS involves two aspects
Authorization to use EPCS
  Use of EPCS is restricted to authorized non-AP MLDs
  Authorization process involves interactions with external entity (e.g., remote AAA server)
    Performing authorization post-transition would result in significant delay and prevent a “seamless” transition
Current EPCS state
  A non-AP MLD authorized for EPCS might have EPCS in the enabled or torn-down state prior to a BSS transition
    Loss of enabled state information during transition would cause EPCS to be disabled
Transferring context related to EPCS priority access during BSS transition can address these issues and seamless experience for EPCS users

## Slide 7: EPCS Authorization during BSS Transition
If Current AP MLD and Target AP MLD are in same seamless mobility domain, Current AP MLD could transfer the EPCS authorization information directly to Target AP MLD
  Avoids need for Target AP MLD to reach out to external server, simplifying transition
  Note: dot11EPCSPriorityAccessAuthorized is stored in dot11Interworking table. Current spec indicates that dot11Interworking table is moved to new AP during BSS transition [2]
  This is static context that can be transferred during preparation phase
If this transfer is not supported, need to enable Target AP MLD to perform EPCS authorization
  Given potential delay, it is preferable that this authorization step happens during the preparation phase
  If Current AP MLD collected EPCS-relevant credentials from non-AP MLD, need to pass them to Target AP MLD

## Slide 8: EPCS State during BSS Transition
Loss of state information during transition would have several undesirable effects
  Lack of priority treatment in Target BSS could adversely affect continuity of communications
  If transition is otherwise seamless, user might be unaware that EPCS priority access is no longer active
  Even if user was informed, would be burdened with re-enabling after each transition
It is desirable to retain EPCS state information across transitions
  Current AP MLD should inform Target AP MLD of EPCS priority access state
    This context is more dynamic than authorization, so might be preferable to transfer during roaming phase
Note: Target AP MLD needs to inform non-AP MLD of EPCS EDCA parameters to use
  One option is to have Target AP MLD automatically send unsolicited EPCS Priority Access Enable Response frame with EDCA parameters to non-AP MLD immediately after reassociation when EPCS is enabled

## Slide 9: Summary
EPCS priority access provides preferential treatment that should be retained to ensure seamless BSS transitions for authorized users
Context transfer of EPCS priority access needs to include both EPCS priority access authorization information and current EPCS priority access state

## Slide 10: Straw Poll -1
SP1: Do you agree to include EPCS priority access authorization and state information as part of Seamless Roaming context transfer?
  Notes:
    Feature is optional – only supported by devices supporting Seamless Roaming and EPCS.
    Specific details of context to be transferred and the phase during which it is transferred are TBD.
Y –
N -
A -

## Slide 11: References
IEEE 802.11be Draft 7.0: See clauses 4.5.13 and 35.16.
  https://ieee802.org/11/private/Draft_Standards/11be/Draft%20P802.11be_D7.0.pdf
IEEE 802.11REVme Draft 7.0: See Annex C: ASN.1 encoding of the MAC and PHY MIB, entry for dot11Interworking TABLE, page 5764-5765
  https://ieee802.org/11/private/Draft_Standards/11me/Draft%20P802.11REVme_D7.0.pdf