## Slide 1: Co-SR Power Control Considerations
Date: 2025-01-24
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 

## Slide 2: Introduction
The following motion has passed in TGbn for Coordinated Spatial Reuse (Co-SR).
TGbn defines a multi-AP Coordinated Spatial Reuse (Co-SR) at TXOP-level with power control.
In this contribution, we discuss the power control signalling for Co-SR.

## Slide 3: Power control in Co-SR
The Co-SR transmission procedure (including the power control aspects) can be briefly described as the following:
Step1: AP1 (sharing AP) has DL data to transmit to STA1, so it starts the channel access procedure
Step2: AP1 successfully contends the channel, and it finds that there’s another AP, i.e., AP2, which satisfies the following conditions
  AP1 has successfully setup a MAPC agreement for Co-SR with AP2
  AP2 also has DL data to transmit
  The interference from AP2 to STA1 is not very strong
Step3: AP1 determines the AP2’s TX power limit based on
  the pathloss between the shared AP and STA1
  the MCS/NSS that the sharing AP intends to use to transmit to STA1
  Note-AP1 can first decide the MCS/NSS for STA1, and then calculate the max allowed interference from AP2, and then calculate the max TX power of AP2 based on the pathloss between AP2 and STA1.
  Note- the pathloss between AP2 and STA1 should be known to AP1 in advance of calculating the TX power limit

## Slide 4: Power control in Co-SR
Step4: AP1 transmits a Trigger frame to AP2 to initiate Co-SR transmission
  The Trigger frame shall indicate the TX power limit of AP2
  AP2 shall make sure its TX power is less than or equal to the indicated TX power limit during Co-SR transmission
  Note-the Trigger frame shall also indicate the TX power of AP1 so that AP2 can calculate the estimated interference from AP1, and decide appropriate parameters for its own transmission
Step 1: pending DL data
AP1
STA1
AP2
Step 2: AP1 finds AP2 satisfying the pre-defined conditions
Step 4: co-SR Trigger Frame
indicating DL co-SR transmission, carrying the PPDU length, and the max TX power of AP2
Trigger
Step 3: TX para. calculation, including AP2’s TX power limit

## Slide 5: Other considerations
According to the above descriptions, the sharing AP may assign any value of the TX power limit for AP2
However, if the indicated TX power limit for AP2 is too small, AP2 may not be able to finish a successful transmission even when using the most robust transmission parameter
Hence, we should have a way for AP2 to tell AP1 what’s the minimum accepted TX power limit of AP2, which can be achieved during the MAPC agreement setup procedure

## Slide 6: Other considerations
During the MAPC agreement setup procedure for Co-SR, the initiator AP and the responder AP can indicate their minimum allowed power value during Co-SR transmission in the request frame and response frame, respectively.
The minimum allowed power is determined by each AP individually.
When transmitting the Trigger frame for Co-SR, the sharing AP shall make sure the indicated TX power limit for the shared AP is larger than or equal to the minimum allowed power indicated by the shared AP during the MAPC agreement setup procedure for Co-SR.

## Slide 7: Conclusion
We propose the power control signaling for Co-SR, including
  The Trigger frame transmitted by the sharing AP that initiates the Co-SR transmission shall indicate the TX power limit of the shared AP
  APs that negotiate a MAPC agreement for Co-SR can indicate their minimum allowed power value during Co-SR transmission

## Slide 8: SPs
SP1:Do you support to include in the 11bn SFD:
In Coordinated Spatial Reuse, the following information shall be carried in the Trigger frame that initiates concurrent CSR transmissions:
  The transmit power limit of the shared AP
    The shared AP Tx power limitation indicated by the sharing AP should not be lower than the minimum TX power indicated by the shared AP in its request.
  The transmit power of the sharing AP