## Slide 1: IMMW for Mobile Device and TGbq timeline
Date: 2025-03-10
Authors:

## Slide 2: Introduction (IMMW PAR/CSD)
Scope of the project
  Non-standalone operation in 42-71 GHz using single-user OFDM
  11bq device is required to support at least one of sub-7.25 GHz bands
  Multi-Link Operation (MLO) defined in sub-7.25 GHz (i.e., 11be) to support non-standalone operation in 42-71 GHz
    leverage or reuse existing PHY/MAC defined for sub-7.25 GHz bands, e.g., SU PPDU format and MAC frames, and define BW mode operating in non-overlapping channels
Need for the project
  Demands of new applications (e.g. augmented and virtual reality, proximity ranging and sensing) both in terms of throughput, latency bounds and accuracy even in in the densest environments
  Cost effective manner is achieved by enabling non-standalone operation in 42-71 GHz bands

## Slide 3: IMMW SG Discussion Summary
Considerations | Specific values or mentions in IMMW SG contributions | 11ad/11aj/11ay
Reused and modified sub 7GH MAC | Leverage 11be/11bn Multi-Link Operation [1,2,6,8,15] Non-standalone IMMW link [1,2,8,15] Leverage other 11be MAC features [1,8,15] | -
Reuse and modified sub 7GHz PHY | Upclocking [2,5,13], processing capabilities [3] | -
Single-User/Multi-User | Single-User [1,2,6,8,19] Multi-User for the next release [2] | SU (11ad), MU (11ay)
Bandwidth (BW) | Min 80/160 MHz (160 for AP) [2] Min 160 MHz & [160, 640] range [12], [160, 1280] range [6] 320, 640 MHz [1], Min 320 MHz & [320, 2560] range [7] Current support channel width in sub 7GHz [2,8] | 2.16 GHz (11ad/11ay), 540/1080 MHz (11aj),
Sub-carrier spacing | 312.5 kHz x 8 = 2.5 MHz [6] | 5.12 MHz (11ay)
Modulation | Up to 16 QAM [1] Up to 64 QAM [5] , up to 256 QAM [7] | SC only 64 QAM (11ad/11ay)
Number of Spatial Streams (NSS) | 1 [1] 2 [2,11], SU-MIMO [5] up to 2 [19] or 4 [7] | 1 (11ad), SU/MU-MIMO (11ay)
Throughput | Depending on max bandwidth, NSS, and modulation scheme | 8.1/ 37.9 Gbps (11ad/11ay)
Latency | Low latency (<10ms) for IMMW use cases (e.g., XR/VR applications) [10] | -
Sensing/Localization | Other related TG will expand 11bq amendment [8,19], 11bk/az/bf as baseline [17,19] | -

## Slide 4: Use case and Considerations on Consumer Mobile Device
Use Case
  High throughput hotspot
  Screen mirroring: up to 8K video mirroring with wire-equivalent latency
  AR/VR application with wire-equivalent latency and proximity/gesture detection [3]
  …

## Slide 5: Use case and Considerations on Consumer Mobile Device
Further considerations
  Small form-factor size with a single antenna for mmW preferred for consumer device
  Latency reduction is important to support AR/VR application with low latency traffic (e.g., 10 ms with 99-percentile wireless delay) [4,10]
  Throughput bottleneck due to Application Processor (e.g., 5 Gbps with single-core) or PCIe interface capability
    Some moderate throughput (< 5 Gbps IMMW link throughput) may be enough [1,3]
  User experience: low battery drain rate [8,10,16], reduced batter/device heating
    Absolute heat reduction is more important than J/bit metrics. High throughput or active usage of mmW Tx chain can increase heat, which may be better to be avoided
  With the benefit of small form-factor and reduced battery heating, DL-only operation in mmW (UL TX, e.g., Ack tx, in sub-7GHz) may be considered as one of implementation options [18]
  In consideration of hand grip loss and human body disturbance, user’s mobility, a robust (re)transmission protocol design is required

## Slide 6: TBDs
To be determined in consideration of practical IMMW use case, power consumption, cost, target throughput, target latency, etc. [11]
  Baseline sub-7GHz PHY to reuse for IMMW: 11ac, 11ax, or 11be
  Minimum bandwidth: upclocking factor
  Mandatory bandwidth range, Maximum bandwidth
  Mandatory number of spatial streams (NSS), Maximum NSS
  Maximum modulation

## Slide 7: Other TGs’ Timelines (as a reference)
 | PAR | PAR approved | First TG meeting | WG Letter Ballots (D1.0) | SA Ballot (D3.0/4.0/5.0) | Final 802.11 WG Approval | RevCom Approval
11ad | Very High Throughput 60GHz | 2008-12-10 |  | 2010-10-24 | 2012-01-05 | 2012-07-01 | 2012-10-23
11ay | Next Generation 60GHz | 2015-03-26 |  | 2018-01-07 | 2020-01-09 | 2020-11-01 | 2021-03-01
11bf | WLAN Sensing | 2020-09-25 | 2020-08 | 2023-03-02 | 2024-06-12 |  | 
11bh | Randomized and Changing MAC Addresses | 2021-02-10 |  | 2023-07-01 | 2024-05-09 | 2024-07-01 | 
11bi | Enhanced Data Privacy | 2021-02-10 |  | 2025-01 |  |  | 
11bk | 320 MHz Positioning | 2022-12-03 |  | 2023-12-28 | 2024-11-10 |  | 
11bp | Ambient Power Communication | 2024-03-19 | 2024-05 | 2026-02 | 2027-08 | 2028-01 | 2028-05
from first TG meeting to D1.0: 1-3 years
from D1.0 to 11 WG approval: 1-2 years

## Slide 8: Proposal: TGbq Timeline Adjustment
TGbq timeline needs to be adjusted and PAR extension may be required considering the start date of TGbq (Feb. '25), sufficient technical discussions period (1-2 years), the practical letter ballot period (1-2 years), and SA ballot period (0.5 year)
  Roughly we have three options, i.e., Option 1 (maintaining PAR timeline, the expected completion time: Mar. 2027), Option 2 (+ 1 year, e.g., a timeline for compact spec. feature set, the expected completion time: Apr. 2028), and Option 3 (+ 2 years, e.g., a timeline for big spec. feature set, the expected completion time: Apr. 2029)
2024
2025
2026
2027
Break
2028
PAR/CSD
approved in WG
(Jul. '24)
IMMW SG
(Nov. '23)
34 contributions discussed
First TGbq
(Feb. '25)
Initial SA Ballot (D4.0)
(Jul. '26)
16 month
8 month
Submittal to RevCom
(Mar. '27)
10 month
D0.1 (Jan. '26)
D4.0
(Jul. '27)
Submittal to RevCom
(Mar. '28)
Option 2 (+1 year)
6 month
6 month
D1.0
(Jul. '26)
12 month
2029
Option 1 (PAR timeline)
16 month
D1.0
(Jul. '27)
Option 3 (+2 years)
D0.1
(Jul. '26)
12 month
D4.0
(Jul. '28)
Submittal to RevCom
(Mar. '29)
6 month
12 month
D0.1
D1.0
Mar. '25 (now)

## Slide 9: Conclusion
Various technical discussions have been studied in the IMMW SG, and now specific upper limits and mandatory sets of spatial stream, bandwidth, modulation, etc. need to be determined in consideration of target throughput and latency that support practical IMMW use cases
We need a more realistic and reasonable timeline for TGbq in consideration of the other TGs’ timelines, sufficient technical discussion period and comment resolution period
  D0.1
    Discussion on target performance metrics and which specific MAC/PHY features we can reuse for TGbq to achieve them
    MAC enhancement to support Multi-Link Operation for non-standalone mmW link
  D1.0 – D4.0: comment resolution period (it typically takes 1-2 years)

## Slide 10: Reference
[1] 11-23/1905r0, High Level Thoughts on IMMW, Bin Tian, Qualcomm
[2] 11-23/1968r0, Discussion on general direction of integrated mmWave, Ming Gan, Huawei
[3] 11-23/1974r0, Flexible sub-7GHz and mmWave Integration in IMMW, Yanchun Li, Huawei
[4] 11-23/1977r1, Requirements Analysis for IMMW Use Cases, Yue Xu, Huawei
[5] 11-23/1991r0, Discussion on Enabling MIMO in IMMW, Mengshi Hu, Huawei
[6] 11-23/2004r0, Technical scope proposal, Laurent Cariou, Intel
[7] 11-23/1878r1, High-level Design Considerations in IMMW, Jianhan Liu, MediaTek
[8] 11-23/1819r1, Integrated mmWave Design Considerations, Claudio da Silva, Meta
[9] 11-23/2102r1, IMMW Multi-Link Operation for mmWave Wi-Fi Sensing, Saira Rafique, Vestel
[10] 11-24/0066r0, Discussion on Target Objectives for IMMW, Eunsung Park, LG Electronics
[11] 11-24/0069r0, MIMO Analysis for IMMW, Bo Gong, Huawei
[12] 11-24/0076r0, Comparison of OFDM and EDMG SC Waveform, Thomas Handte, Sony
[13] 11-24/0133r0, Channel raster considerations for 60GHz band in IMMW, Micky Mehta, Pharrowtech BV
[14] 11-24/0167r0, Discussion on Bandwidth Issue in IMMW, Yue Xu, Huawei
[15] 11-24/0459r0, Multi-Link Operation for IMMW, Insun Jang, LG Electronics
[16] 11-24/0471r0, Considerations on Power Consumption, Sang Kim, LG Electronics
[17] 11-24/0723r1, Sensing and Ranging in IMMW, Tony Xiao Han, Huawei
[18] 11-24/0823r1, Further Simplifications to Promote IMMW Adaoption, Bilal Sadiq, Samsung Electronics
[19] 11-24/1104r1, Thoughts on IMMW for the Industry Use, Yue Xu, Huawei

## Slide 11: Straw Poll #1
Do you agree with extending the timeline since the current PAR timeline is considered unrealistically tight?

## Slide 12: Straw Poll #2
Which of the following options do you think a realistic and reasonable timeline for TGbq?
  Option 1) the expected completion time (submittal to RevCom): Mar. 2027
    This option aligns with the timeline in the PAR
    Expected milestone: D1.0 (late '25 or early '26), D4.0 (Jul. '26)
  Option 2), the expected completion time: Mar. 2028
    Expected milestone: D0.1 (Jan. '26), D1.0 (Jul. '26), D4.0 (Jul. '27)
      One year of technical discussions to get D0.1
  Option 3), the expected completion time: Mar. 2029
    Expected milestone: D0.1 (Jul. '26), D1.0 (Jul. '27), D4.0 (Jul. '28)
      One and a half years of technical discussions to get D0.1
  [Note 1] If straw poll #1 is passed, then option 1 is not valid.