## Slide 1: Co-RTWT Start Time Protection Rule
Jan 2025
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Binita Gupta | Cisco Systems |  | 
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Javier Contreras | Cisco Systems |  | 
Pelin Salem | Cisco Systems |  | 

## Slide 2: Situation (1/3) For Co-RTWT, the 11bn SFD calls out a) AP coordination and b) rigorous respect for the Start Time Protection Rule (STPR)
SFD [1] section 3.10 has:
  “Define mechanisms that enable APs to coordinate their rTWT schedule(s) and/or to ensure that one AP provides the protection of the rTWT schedule(s) of the other AP.
    NOTE – TBD mechanisms including negotiation between 2 APs and advertisement.
    [Motion #48, [1] and [131-148]]
  If an AP extends the protection of the rTWT schedule of another AP, following negotiation or through other means, then:
    The AP shall ensure its TXOP ends before the start time of the corresponding OBSS rTWT SP(s)” // = STPR

## Slide 3: Situation (2/3) We Can Consider Three Kinds of AP Co-RTWT Scheduling
AP scheduling can be:
  TBTT-centric
    A BI is divided into M SPs
    Given up to N overlapping BSSs, each AP gets 1 SP every N of these SPs
      So SI = BI*N/M TUs, and time between start of adjacent SPs (and max SP duration) is BI*N/M TUs
      E.g., BI = 100 TU, M = [2 5 10 20 50 100 200 500 1000] SPs, time between the start of adjacent SPs (and the max SP duration) is [50 20 10 5 2 1 0.5 0.2 0.1] TUs respectively
  Round-number-centric
    Each RTWT uses the same SI which is chosen to be suitable across a range of use cases
      E.g., a new SP starts every 2 msec, and each AP gets a SP every 12 msec [1]
  Flow-centric
    Each Co-RTWT agreement corresponds to a flow (or a flow aggregate for very similar flows)
      E.g., one agreement provides a SP every 20.01 msec and another agreement provides a SP every 16.65 msec

## Slide 4: Situation (3/3) We Need to Design for Six Real-World Realities
Typical periodic flows nominally operate at a mix of rates 50/60/72/80/90/120/1000 Hz (etc)
The typical Beacon Intervals is BI = 100 TU (102.4 msec)
  (But there are rarer exceptions)
There may be (typically is) clock skew between networks
  And potentially between APs of in same network
Connectivity between networks may be multihop: A  B  C  D  E
  Plus: branches, loops, and one-way connectivity
  Especially common in apartment buildings, malls, multi-tenant office buildings and dense urban (etc)
APs can be mobile:
  Carried by people
  Mounted on cars, buses, trains, ships (planes can be ignored, for now)
Beacons + groupcast (including MBSSID Beacons) TBTTs are best addressed as a further flow for Co-RTWT

## Slide 5: Problem (1/2) An adequate level of AP Coordination between networks is NOT easy to assure
Very hard to ensure that overlapping networks select a common timebase
  While encouraging use of GNSS as the reference time source is (very) desirable, globally mandating use is unrealistic given 802.11’s (deep) indoor use cases
  Without a common timebase, initially well-spaced SP start times will drift and can become closely spaced
  Problem for TBTT-centric, Round Number-centric; N/A for Flow-centric
Very hard to ensure that overlapping networks select a common SI (or (sub)multiples thereof)
    A one-size-fits-all mandate will be ill matched to dense-urban vs rural vs automated manufacturing / warehousing
    A one-size-fits-all mandate may not be future proofed to new technologies
    Do we pick 1./[50, 60, 72, 80, 90, or 1000] Hz, or [20, 16, 14, 12, 11, or 1] TU or [3 6 or 12] msec or what?
    Problem for TBTT-centric, Round Number-centric; impossible for Flow-centric
Even if we could find a common timebase and SI, how do APs space out their Service Start Times?
  Given the variable number of OBSS APs, mobile APs, APs changing to/from this channel, etc
    Note: This is really talking about AP radios since this ignores multiple colocated BSSIDs
  Problem for TBTT-centric, Round Number-centric; N/A for Flow-centric

## Slide 6: Problem (2/2) Essence of the challenge
Even with the best will in the world, at network boundaries we must anticipate that the start times of SPs will intermittently but regularly land very close to each other:
  Either persistently close (due to drift) or randomly close (e.g., due to 102.4 msec and 16.667 msec periods)
  The next OBSS AP’s SP start time could be later by 0.001, 0.01, 0.1, 1, or 10 msec
If the next SP is a very short time later, then the following SFD language means that an AP’s SP might be vastly truncated, such that the AP cannot meet its underlying QoS/determinism goals
  “The AP shall ensure its TXOP ends before the start time of the corresponding OBSS rTWT SP(s)”
… We need something more nuanced
SPs are initially non-overlapping with full SP duration available
Co-RTWT A in network 1
Co-RTWT B in network 2
Beacons in network 2
Beacons in network 1
After drift, SPs from Co-RTWTs A and B are highly-overlapping, and SPs from Co-TWT A get a minimal SP duration

## Slide 7: Solution STPR Flexibility
AP A determines that the start time of the next SP of AP B (e.g., from a different administrative domain) closely follows the start time of AP A’s SP
  Sidebar: Almost always the situation is reciprocal: i.e., later, AP B will determine that the start time of AP A’s next SP closely follows the start time of AP B’s SP
11bn should define how AP A and AP B may negotiate an exception to the SFD’s STPR rule
For example, AP A can establish a TXOP that extends past the start time of AP B’s SP if, in exchange, AP A determines the medium resources needed by AP B during the ICF/ICR exchange at the start of AP A’s SP, and allocates commensurate medium resources to AP B during the TXOP
  With fairness guardrails if the combined total would exceed the TXOP limit: e.g., mutual downscaling
  Medium resources = time resources (Co-TDMA); could consider spatial resources too (Co-SR and/or Co-BF)
Co-RTWT A in network 1
Co-RTWT B in network 2
Co-RTWT A in network 1
Co-RTWT B in network 2
Converted to Co-TDMA TXOP with leading ICF+ICR
Two Co-RTWT SPs with inviolate STPR

## Slide 8: Summary
It is very challenging for APs to coordinate their Co-RTWT schedules, especially APs in different administrative domains
A likely side-effect is that the start times of different APs’ SPs could be “pseudo-randomly” very close (0.001 / 0.01 / 0.1 / 1 msec apart)
  Due to different timebases, different SIs, mobile APs, etc
  Either persistently close (due to drift) or randomly close (e.g., due to 102.4 msec and 16.667 msec periods)
We propose a simple fix: APs can negotiate with each other to allow mutually-agreeable exceptions to the Co-RTWT STPR rule

## Slide 9: Strawpoll 1
Do you agree to add the following text to the 11bn SFD:
    Do you support defining protocol for an AP with a runt Co-RTWT SP, due to the imminent start time of another AP’s Co-RTWT SP, to negotiate a more balanced allocation of wireless resources with the other AP?
Y / N / A

## Slide 10: References
[1] 23/1962, “Gain analysis for coordinated AP transmission”, Abhishek Patil

## Slide 11: Backup