## Slide 1: R-TWT Sharing Follow-Up
Date: 2025-3-3
Authors:

## Slide 2: Introduction
11be defined Restricted Target Wake Time (R-TWT) to support latency sensitive traffic (e.g., by providing start time protection within the BSS)
In the TGbn SFD [1], Co-RTWT builds on R-TWT by providing mechanisms for multiple APs to coordinate and/or protect their R-TWT schedules
In addition, we proposed in 11-24/1457r0 [2] to enable the sharing of the TXOP obtained during an R-TWT SP to support latency sensitive traffic of a neighbour AP (OBSS)
In this contribution, we provide more information on the proposed procedure

## Slide 3: Some R-TWT scheduling options
When an AP determines to schedule an R-TWT SP, it can…
Ignore OBSS R-TWT schedules
  Simplest approach
  May result in issues due to scheduling conflicts
Consider OBSS R-TWT schedules – e.g., shift to avoid conflicts
  Avoids conflicts but may result in non-optimal schedule (e.g., too early or late)
  AP may further request protection from OBSS based on Co-RTWT
(Proposed) Leverage OBSS R-TWT schedules
  Request the OBSS AP to (always) share the TXOP obtained during a relevant R-TWT SP
  OBSS AP may accept or reject the request (similar to how it manages TWT requesting STAs)
  This option can allow the AP to achieve a more optimal schedule

## Slide 4: Proposed R-TWT sharing protocol
R-TWT membership setup – AP requests
  Similar to how a TWT requesting STA would request to join an R-TWT
  The AP sends a management frame containing a TWT request to the OBSS AP
  Based on the TWT element (including Restricted TWT Parameter Set field(s))
    TWT Request set to 1 (TWT requesting STA)
    Trigger field set to 1
    Broadcast TWT ID set to identify the intended OBSS AP’s R-TWT
    Negotiation Type set to 3 to (broadcast TWT)
    TWT Setup Command set to, e.g., 2 (demand)

## Slide 5: Proposed R-TWT sharing protocol
R-TWT membership setup – OBSS AP responds
  Similar to how a TWT scheduling STA would accept a member for an R-TWT
  The OBSS AP may determine to accept or reject the request for that R-TWT
  To accept, the OBSS AP sends a management frame containing a TWT response
  Based on the TWT element (including Restricted TWT Parameter Set field(s))
    TWT Request set to 0 (TWT scheduling STA)
    Trigger field set to 1
    Broadcast TWT ID set to identify the intended OBSS AP’s R-TWT
    Negotiation Type set to 3 to (broadcast TWT)
    TWT Setup Command set to 4 (accept TWT) or 7 (reject TWT) to reject

## Slide 6: Proposed R-TWT sharing protocol
R-TWT membership termination – AP initiates
  Similar to how a TWT scheduled STA’s R-TWT membership may be terminated
  The AP may terminate its membership for an R-TWT SP
  The AP sends a management frame to the OBSS AP
  Based on the TWT element
    TWT Request set to 1 (TWT scheduled STA)
    Broadcast TWT ID set to identify the intended OBSS AP’s R-TWT
    Negotiation Type set to 3 to (broadcast TWT)
    TWT Setup Command set to 7 (reject TWT)

## Slide 7: Proposed R-TWT sharing protocol
R-TWT membership termination – OBSS AP initiates
  Similar to how a TWT scheduled STA’s R-TWT membership may be terminated
  The OBSS AP may terminate an AP’s membership for an R-TWT SP
  The AP sends a management frame to the OBSS AP
  Based on the TWT element
    TWT Request set to 0 (TWT scheduling STA)
    Broadcast TWT ID set to identify the intended OBSS AP’s R-TWT
    Negotiation Type set to 3 to (broadcast TWT)
    TWT Setup Command set to 7 (reject TWT)

## Slide 8: Proposed R-TWT sharing protocol
Additional considerations
  The OBSS AP is obligated to share the TXOP obtained for the R-TWT SP with the AP
    Based on MU-RTS TXS (similar to TXOP sharing)
  When announcing the R-TWT, the OBSS AP may indicate if the R-TWT can accept an AP’s request
  The AP can provide additional information in the request about the expected traffic (TBD)

## Slide 9: Summary
When considering to schedule an R-TWT SP, it would be good for an AP to have the option of requesting a neighbour (OBSS) AP to share the TXOP obtained during its (OBSS) R-TWT SP
We have provided information on how we can enable this (by reusing existing R-TWT protocol)

## Slide 10: Straw Poll 1
Do you agree to add the following text to the SFD “11bn shall define a mechanism that enables an AP to request an OBSS AP to share the TXOPs obtained during the R-TWT SPs of a desired R-TWT schedule of the OBSS AP.”
  Y
  N
  A

## Slide 11: Straw Poll 2
Do you agree to add the following text to the SFD “An AP may request the sharing of the TXOPs obtained during the R-TWT SPs of the OBSS AP by sending a management frame with a TWT element to the OBSS AP to become a member of a desired R-TWT. An AP that accepts such a request shall share a portion of the TXOPs obtained for the corresponding R-TWT SPs with the other AP.”
  Y
  N
  A

## Slide 12: References
[1] Ross Jian Yu (Huawei), 'Specification Framework for TGbn', 24/209r9, Feb, 2025
[2] Gaius Wee (Panasonic), 'R-TWT Sharing', 24/1457r0, Sep, 2024